COATS

Technical Memorandum One

Volume One:

REVIEW OF LEGACY SYSTEMS

Prepared by

Eli Cuelho, Research Associate & Amy Gill, Research Assistant

of the

Western Transportation Institute

Civil Engineering Department

Montana State University - Bozeman

for the

State of California

Department of Transportation

New Technology and Research Program

and

State of Oregon

Department of Transportation

Traffic Management Section

in cooperation with the

U.S. Department of Transportation

Federal Highway Administration

November 1998

Disclaimer

The opinions, findings and conclusions expressed in this publication are those of the authors and not necessarily those of the California Department of Transportation, Oregon Department of Transportation or the U. S. Department of Transportation, Federal Highway Administration.  Alternative accessible formats of this document will be provided upon request.

Persons with disabilities who need an alternative accessible format of this information, or who require some other reasonable accommodation to participate, should contact the California Department of Transportation, at: Coco Briseno, Chief, Advanced Rural Transportation System Branch, New Technology and Research Program MS #83, 1227 O Street, P.O. Box 942873, Sacramento, CA  94273 – 0001; telephone number (916) 654-6980.

Acknowledgments

Grateful appreciation is extended to the following agencies for their support, guidance and advice that facilitated the successful completion of this report.  Specifically appreciated are the COATS Steering Committee; the various programs, divisions and districts/regions in the Oregon Department of Transportation and Caltrans; the California Highway Patrol; the Southern Oregon Visitors Association; and the USDOT Federal Highway Administration.  In addition, thanks to all who took time from their busy schedules to gather, organize and send the necessary data.

Glossary of Abbreviations

ARTS		Advanced Rural Transportation Systems

ATR		Automatic Traffic Recorder

AVI		Automatic Vehicle Identification

Caltrans	California Department of Transportation

CARS		California Amateur Radio System

CCTV		Closed Circuit Television

CHP		California Highway Patrol

COATS	California/Oregon Advanced Transportation Systems

CMS		Changeable Message Sign

CPA		Critical Program Area

CWRR		California Western Railroad

CVISN	Commercial Vehicle Information Systems and Networks

CVO		Commercial Vehicle Operations

CW		Continuous Wave

DMS		Dynamic Message Sign

DOT		Department of Transportation

DSIS		Downhill Truck Speed Information Systems

EMS		Emergency Medical Systems

EMSA		Emergency Medical Services Authority

GIS		Geographic Information Systems

GPS		Global Positioning Systems

GPRA		Government Performance and Results Act

HAR		Highway Advisory Radio

HF		High Frequency

ISTEA		Intermodal Surface Transportation Efficiency Act

ITEN		Integrated Tactical Enforcement Network

ITIP		Interregional Transportation Improvement Plan

ITS		Intelligent Transportation Systems

LPR		License Plate Reader

LROP		Long Range Operational Plan

MPO		Metropolitan Planning Organization

MSU		Montana State University

NCR		North Coast Railroad

NWP		Northwestern Pacific Railroad

NSA		National System Architecture

ODOT		Oregon Department of Transportation

OSP		Oregon State Police

RABA		Redding Area Bus Authority

RCMS		Radar Changeable Message Sign

RTPA		Regional Transportation Planning Agency

RWIS		Remote Weather Information System

SHOPP	State Highway Operation and Protection Program

SOC		Satellite Operation Center

SOVA		Southern Oregon Visitors Association

STIP		Statewide Transportation Improvement Plan

TDM		Transportation Demand Management

TIF		Truck Inspection Facility

TMC		Traffic Management Center

USDOT	United States Department of Transportation

VMS		Variable Message Sign

WIM		Weigh In Motion

WTI		Western Transportation Institute

Table of Contents

1	Introduction	1

1.1	Review of Legacy Systems Report Objectives	2

1.2	Volume One Contents and Organization	3

2	data collection and review	4

2.1	Data Collection Survey	4

2.2	Categorization and Review of Documents	4

2.2.1	Documents Discussing California’s Advanced Technology-Related Approaches	5

2.2.1.1	California Interstate 5 Canyon Closure	5

2.2.1.2	Route Concept Reports	5

2.2.1.3	District 1 Long Range Operational Plan and Modal Transfer Locations	7

2.2.1.4	Transportation Management Center Master Plan	7

2.2.1.5	District 1 System Management Plan	7

2.2.1.6	1998/99 Transit Needs Assessment for Shasta County	8

2.2.1.7	Draft - Regional Transportation Plan for Shasta County	8

2.2.1.8	Caltrans Strategic Plan	8

2.2.1.9	Caltrans Strategic Plan Supplemental: Strategic Priorities and Implementation Framework	8

2.2.1.10	Feasibility of ITS Applications in Rural California	8

2.2.1.11	Traffic Management Plan State Route-70 Corridor	9

2.2.1.12	Caltrans Emergency Operations Plan	9

2.2.1.13	Caltrans Incident Command System	9

2.2.1.14	Special Study for Route 299 (including Appendix)	9

2.2.2	Documents Discussing California’s Traditional Approaches	10

2.2.2.1	Statewide Transportation Improvement Plan Interim Guidelines for 1998	10

2.2.2.2	Interregional Transportation Improvement Plan (ITIP)	10

2.2.2.3	1998 Interregional Transportation Improvement Program	10

2.2.2.4	California Rural Advanced Transportation System	10

2.2.2.5	Shasta County Social Service Transportation Coordination Plan and    Inventory	11

2.2.2.6	Caltrans’ Planning Documents	11

2.2.3	Documents Discussing Oregon’s Advanced Technology-Related Approaches	11

2.2.3.1	Draft Emergency Operations Plan	11

2.2.3.2	Model Incident Response Procedures	11

2.2.3.3	Oregon ITS Strategic Plan 1997-2017	11

2.2.3.4	Public Transit Management System Transportation Entities and Performance Results	12

2.2.4	Documents Discussing Oregon’s Traditional Approaches	12

2.2.4.1	Final Statewide Transportation Improvement Program (STIP) 1998-2001	12

2.2.4.2	Oregon’s Visitor Industry	12

2.2.5	Other Pertinent Documents	12

2.2.5.1	U.S. Department of Transportation’s Advanced Rural Transportation Systems Strategic Plan	12

3	existing and planned transportation systems	13

3.1	Advanced Technology-Related Approaches	13

3.1.1	Traveler Safety and Security	14

3.1.1.1	Road Weather Information Systems	15

3.1.1.2	Automated Seismic Road Closure Systems	15

3.1.1.3	Dynamic Message Signing	17

3.1.1.4	Highway Advisory Radio	17

3.1.1.5	Motorist-Aide Call Boxes	17

3.1.2	Emergency Medical Services	18

3.1.3	Tourism and Traveler Information Services	18

3.1.3.1	Internet Links	18

3.1.3.2	Kiosks	20

3.1.4	Public Traveler Services/Public Mobility Services	20

3.1.5	Infrastructure Operations and Maintenance	21

3.1.5.1	Automatic Traffic Recorders	21

3.1.5.2	Traffic Management Centers	23

3.1.5.3	Regional Management Efforts	23

3.1.6	Fleet Operations and Maintenance	24

3.1.7	Commercial Vehicle Operations	24

3.1.7.1	Weigh-In-Motion/Automated Vehicle Identification	24

3.1.7.2	Speed and Curve Warning Systems	26

3.2	Traditional Projects, Programs and Improvements	26

3.2.1	Infrastructure	26

3.2.1.1	Rail	27

3.2.1.2	Air	27

3.2.1.3	Marine	27

3.2.1.4	Intermodal Hubs	29

3.2.1.5	Safety Rest Areas	29

3.2.1.6	Commercial Vehicle Operations	29

3.2.2	Emergency Medical Services	31

3.2.3	Transit Systems	31

4	Summary	34

References	35

Appendix A – Data Collection Survey	40

Appendix B – California Major and Minor STIP	45

Appendix C – Oregon STIP/SHOPP	52

Appendix d – Advanced Technology Projects/Programs	59

Appendix e – Traditional Projects/Programs	73

List of Figures

Figure 1: ARTS Critical Problem Areas Cluster Relationships	 14

Figure 2: Map of Traveler Safety and Security Programs/Projects	 16

Figure 3: Map of Tourism and Traveler Information Services	 19

Figure 4: Map of Infrastructure Operations and Maintenance	 22

Figure 5: Map of Commercial Vehicle Operations	 25

Figure 6: Map of Traditional Infrastructure Elements	 28

Figure 7: Map of Traditional Commercial Vehicle Operations	 30

Figure 8: Map of Traditional Emergency Medical Services	 32

Figure 9: Map of Traditional Transit Services	 34

# Introduction

The overall goal of rural ITS planning, demonstration, and deployment is to “…make rural travel safe, dependable and convenient”.  This goal will be accomplished by providing an integrated system whereby transportation agencies, transit providers, emergency managers and tourism officials will be able to manage the transportation system more efficiently within the predominantly rural study area.  More specifically, the objectives of the California/Oregon Advanced Transportation Systems (COATS) project include:

identifying rural transportation problems,

matching potential ITS-related solutions to these problems and

determining feasible ways to implement these solutions.

To carry out these objectives, investigations of technical, institutional, planning, maintenance, operations, phasing, cost, and deployment issues will be considered.  Specifically, the COATS project will attempt to:

identify the transportation and information needs within the study area;

determine ITS solutions that would be beneficial, cost-effective and deployable, using the nationally-defined ITS user services/market packages (national architecture) to identify potential technologies for consideration;

identify, design and deploy initial, small-scale projects/systems on a multi-year basis to test the feasibility of rural ITS; and

develop a Model Deployment and Evaluation Plan for implementing rural ITS strategies on a larger scale.  Emphasis will be placed on the integration and expansion of future ITS components within the study area.

To maximize resources and foster cooperation, the California Department of Transportation (Caltrans) and the Oregon Department of Transportation (ODOT) are partnering to investigate the feasibility of Intelligent Transportation Systems (ITS) in rural areas.  Specifically, the rural areas of interest are located in Northern California and Southern Oregon, as shown in Figure 1.  A key element of this effort will be to adopt a strategy that will lead to the use of ITS technologies to enhance safety and improve the movement of people, goods, and services, thereby promoting economic development in the bi-State region.  WTI is working with Caltrans, ODOT and their respective regional and local governments to solve significant transportation-related problems in rural portions of their States, northern California and southern Oregon.

## Review of Legacy Systems Report Objectives

The Review of Legacy Systems report attempts to summarize existing transportation systems and planned transportation improvements within the COATS corridor and include them in GIS maps, thereby completing Tasks 2.1, 2.2 and 2.5.  These tasks, again, are to review local and statewide Intelligent Transportation Systems (ITS) plans and programs (Task 2.1), inventory ITS and Other Local Systems (Task 2.2) and to establish geographic areas of focus (Task 2.5).  By reviewing and documenting local and statewide efforts, redundancy among the various projects can be reduced.  Although the name of this report is the Review of Legacy Systems, the term “Legacy” does not imply that only existing transportation systems/projects/programs are included.  The Review of Legacy Systems report also contains information regarding planned transportation systems/projects/programs.  Planned projects are those in which money has been allocated.

The Western Transportation Institute (WTI) at Montana State University (MSU) surveyed appropriate project participants to identify and inventory existing systems and planned programs.  These existing and planned programs fall into one of two categories: advanced technology-related programs/projects or traditional programs/projects.  The advanced technology-related programs/projects were divided into the seven following categories.

Traveler Safety and Security

Emergency Services

Tourism and Travel Information Services

Public Traveler Services/Public Mobility Services

Infrastructure Operations and Maintenance Systems

Fleet Operations and Maintenance

Commercial Vehicle Operations

The traditional programs/projects were divided into three main categories: infrastructure, emergency medical services and transit services.  Included in the infrastructure category were rail, air, marine and intermodal facilities, as well as safety rest areas and commercial vehicle operations.

The information collected in this report coupled with future reports will assist in identifying gaps and potential correlation between existing or planned systems and help identify future ITS solutions that may add value to on-going efforts.  The Review of Legacy Systems report is Volume One of a two-volume report called, Technical Memorandum One.  Volume Two of this report is called the Conditions and Performance report.  Volume One details the existing and planned transportation systems within the corridor and Volume Two details the types of transportation challenges existing within the corridor.  The Traveler Needs Survey, or Technical Memorandum Two, summarized the perceived needs and information preferences of the general traveling public.  Using both volumes of Technical Memorandum One and Technical Memorandum Two, ITS-related programs and projects can be identified and prioritized for use in specified areas.

## Volume One Contents and Organization

The five main sections contained within the Review of Legacy Systems report are 1) Introduction, 2) Data Collection and Review, 3) Summary of Existing and Planned Transportation Systems, 4) Summary of the Report and 5) Appendices.  Data collection was performed using surveys and personal interviews of various project participants and stakeholders.  Basic discussions of each of the pertinent reports and data received are contained in Section 2.  The data collected from each State is categorized into one of two categories: 1) advanced technology-related data and 2) traditional approach data.  Section 3 contains detailed descriptions of pertinent transportation systems/solutions, as well as GIS maps of their locations.  Transportation systems/solutions are categorized by the Advanced Rural Transportation Systems (ARTS) Strategic Plan (1) Critical Problem Areas (CPAs).  Section 4 provides a general summary of the document.  Tabulated data of the existing and planned transportation systems/solutions are located in Appendices D and E.

# data collection and review

Due to the large amount of data available regarding legacy systems in northern California and southern Oregon, a system of collecting and organizing pertinent data was necessary.  The three main steps to acquiring and organizing the legacy systems data were to:

- develop and distribute a survey to project participants,

- use information from the survey to identify and contact additional stakeholders, and

- review and categorize incoming data.

## Data Collection Survey

A survey was designed and distributed to project participants by WTI (Appendix A).  The purpose of the survey was to collect data regarding existing or planned transportation systems and improvements (both advanced and traditional) within the study area.  In addition, data were collected for Task 2.3 (Identifying Transportation and Safety Related Problems) since many of these participants would be able to include these types of data along with legacy data.

The survey contained nine main sections or areas of questioning corresponding to the ARTS CPAs.  Questions that were related to accident data collection, emergency incidents and response times, traffic counts, visitor demographics and State/National Park operations were used to fulfill the requirements of Task 2.3 (see Volume Two).  Information was also requested regarding regional management and coordination, stakeholder identification and other ITS programs and activities not directly addressed in the survey.

## Categorization and Review of Documents

The various documents submitted by project partners in California and Oregon were reviewed and organized by State into the following categories: advanced technology related documents and traditional programs, projects and improvements.  Documents that provided information regarding advanced approaches to transportation system problems (existing or planned) were categorized into the advanced section.  Documents that provided information regarding traditional approaches to transportation problems (existing or planned) were placed in the traditional section.  Due to the nature of some of these documents, the information within them contains both advanced and traditional legacy data.  Where this occurs it will be noted.  Information will also be categorized by the State to which it pertains.

Within this section, a brief description of each of the documents received is given.  This description is intended for the reader to gain knowledge regarding the general purpose of the document and the types of information it includes. Information that is more specific will be provided when pertinent.

### Documents Discussing California’s Advanced Technology-Related Approaches

#### California Interstate 5 Canyon Closure

The California Interstate 5 Canyon Closure (2) document contains four different plans for closing sections of I-5 upon notification of an incident.  It also includes the procedures to re-open the roadway and a list of agencies that may need to be notified of an incident.

#### Route Concept Reports

Route Concept Reports contain the Department of Transportation’s goal for the develop-ment of each route in terms of level of service, and broadly identify the nature and extent of improvements needed to reach those goals.  Some areas covered in all Route Concept Reports include: route definitions, route purpose, existing facilities, related facilities, current operating conditions, route concept, concept rationale, and issues of concern and improvements.

Route I-5: (3)

Rest Stops at Corning, Red Bluff (PM 33.3), Red Bluff (PM 34.3), O’Brien, Lakehead, Weed and Collier

Park and Ride Lot at Bowman Road Intersection,

Greyhound – 28 daily trips in Tehama and Shasta Counties and 14 in Siskiyou County

Trailways Lines, Inc. – 6 daily trips in Tehama, Shasta and Siskiyou Counties

STAGE – 17 daily trips in Siskiyou County

Proposed measures to reduce deer accidents using fencing, deer mirrors, and/or roadside clearance

Route 3: (4)

Proposed measures to reduce deer accidents using fencing, deer mirrors, and/or roadside clearance

STAGE schedules two daily commuter trips, five days/week between Etna and Yreka and mid-day trips on Tuesday and Thursday

Route 36: (5)

Rest Stop at Chester

Mount Lassen Motor Transit daily bus service from Red Bluff to Susanville

Considered highway construction in Lassen County

Route 44: (6)

Rest Stops at Shingletown and Bogard

Park and Ride Lots on Deschutes Road, Black Butte Store and Shingletown

Route 89: (7)

Proposed measures to reduce deer accidents using fencing, deer mirrors, and/or roadside clearance

Rest Stop in Plumas County (left)

Park and Ride Lots at Blairsden, Burney and Mt. Shasta

STAGE – three trips/day, five days/week between Mt. Shasta and McCloud

Route 96: (8)

Rest Stops at Collier (Junction 96/I-5) and Independence Creek

Park and Ride Lot at Pacific Crest Trailhead

STAGE (Siskiyou Transit and General Express) – one round trip per day, two days/week between Yreka and Happy Camp

Proposed measures to reduce deer accidents using fencing, deer mirrors, and/or roadside clearance

Route 97: (9)

Rest Stops at PM 0.2 (left) and PM 21.7 (left)

Portable Scale Pit at PM 3.0 (left and right)

STAGE schedules two trips/day, five days/week from Yreka to Weed

Greyhound – six routes daily

Route 101: (10)

Park and Ride Lots at Eureka and Trinidad and near Fortuna

Mendicino Transit Authority runs from Ukiah to Arnold

Humboldt Transit Authority runs from Scotia to Trinidad

Del Norte Public Bus runs from Klamath to Crescent City

Route 139: (11)

Proposed measures to reduce deer accidents using fencing, deer mirrors, and/or roadside clearance

Greyhound – two scheduled runs daily (north and south)

Route 161: (12)  No issues of concern or planned improvements.

Route 299: (13)

Rest Stops at Douglas City (right) and Hatchett Mountain (right)

Park and Ride Lot at Junction 89/299

Truck Scales at Shasta County, PM 12.7 (right), Shasta County, PM 54.3 (left) and Shasta County, PM 76.2 (left)

Redwood Empire Lines – five scheduled routes from Eureka to Redding

Greyhound – four routes

Route 395: (14)

Rest Stops at Honey Lake (right) and Secret Valley (left)

Park and Ride Lot at Janesville

Greyhound – scheduled routes

#### District 1 Long Range Operational Plan and Modal Transfer Locations

The District 1 Long Range Operational Plan and Modal Transfer Locations (15) document lists existing and planned ITS projects within District 1 in California.  This plan discusses the purpose and responsibilities of the Traffic Management Team in District 1.  Also included with this document was a list of intermodal transfer locations.

#### Transportation Management Center Master Plan

The Transportation Management Center Master Plan (16) discusses methods to increase safety and reduce incidents, delay, environmental degradation, and cost to taxpayers.  The discussion covers TMC facility development, costs and benefits, regionalization, partnerships, management, operations and ITS architecture and solutions.  Some of the ITS equipment that is being looked at includes CMSs, HARs, automatic toll collection, transit management, information kiosks, fleet management, and alternatives to transportation.

#### District 1 System Management Plan

The purpose of the District 1 System Management Plan (17) is to describe how the District envisions the transportation system will be maintained, managed, and developed over the next 20 years and beyond.  This Plan discusses each of the primary modes of transportation in the District, including the existing system, anticipated future directions, issues, proposed improvements, and strategies for development of each mode.

Rail – North Coast Railroad (NCR), California Western Railroad (CWRR) and Northwestern Pacific Railroad (NWP) serve 101 from Eureka to San Francisco Bay and 20 west of Willits.

Maritime Facilities – Humboldt Bay, Crescent City Harbor and Noyo Harbor at Fort Bragg.

#### 1998/99 Transit Needs Assessment for Shasta County

The 1998/99 Transit Needs Assessment for Shasta County (18) includes discussions in the following areas: unmet transit needs, transit demand analysis, description of existing transit services, existing transit performance, and transit evaluation.  The summary of this needs assessment is that, generally, public and private transit operators serve the primary areas of high transit demand, as well as many other specialized transit needs throughout the county.  All the information pertains to Shasta County in California.

#### Draft - Regional Transportation Plan for Shasta County

The Draft – Regional Transportation Plan for Shasta County (19) contains a discussion of regional transportation issues, problems and possible solutions.  The Plan includes goals, objectives and policies for each transportation mode and area of concern, as well as actions to be taken to implement Plan goals, objectives and policies, and estimated available funding.  Some of the areas of concern include transit and paratransit, streets and highways, goods movement, aviation, passenger rail, air quality, environmental resources and costs.  Short-range and long-range objectives are listed for each area of concern.

#### Caltrans Strategic Plan

The purpose of the Caltrans Strategic Plan (20) is to help Caltrans in its ongoing development of dynamic, open models for planning, management and resource allocation.  This Plan also develops Caltrans’ system for gauging its success.  It includes a short discussion of values, visions, planning processes, performance measures, assumptions and the 1998 Strategic Priorities for Caltrans.

#### Caltrans Strategic Plan Supplemental: Strategic Priorities and Implementation Framework

The Caltrans Strategic Plan Supplemental (21) includes the four new 1998 Strategic Priorities, which include Transportation Partnerships, Developing our Workforce, Integrating Project Management, and Optimizing Transportation Operations, including the Implementation Framework.  The key issues in this Plan are to prepare a 1999 Caltrans Comprehensive Plan, to maintain, manage, and improve the transportation system to achieve optimal results, to address customer needs and values, to improve organizational competency and to improve partnerships.

#### Feasibility of ITS Applications in Rural California

The Feasibility of ITS Applications in Rural California (22) report contains prioritized stakeholder input on problems and advanced technology solutions and examines potential Advanced Rural Transportation System applications based on a pilot workshop in Bishop, California.  This study recommends short term and long-term deployment strategies, research and development, funding opportunities and next steps to build a successful Intelligent Transportation System that meets stakeholder needs.

#### Traffic Management Plan State Route-70 Corridor

The State Route-70 Corridor Traffic Management Plan (23) was written to identify the roadwork activities scheduled for the SR-70 Corridor and to address its cumulative affect on traffic.  This report is primarily focused on two areas: public information and traffic flow maintenance.

Portable Dynamic Message Signs (DMSs) will be placed at several locations to advise motorists of expected delays due to construction.

California Highway Patrol will input information into the California Highway Information Network (CHIN) for public access.  This information will include lane closures and conditions causing significant delays.

Permanent and possibly one portable Highway Advisory Radio (HAR) will be used to provide the public with complete real-time road information.  They will be used in conjunction with the DMSs.

The Internet web site used to gather road information similar to CHIN is located at http://www.dot.ca.gov/hq/roadinfo/index.htm.

#### Caltrans Emergency Operations Plan

The Caltrans Emergency Operations Plan (24) was established to provide guidelines on how to respond to and manage emergencies resulting from natural or man-made disasters, technological incidents or nuclear related operations.

#### Caltrans Incident Command System

The Caltrans Incident Command System (25) document describes the components, operations, and responsibilities of the Incident Command System in California.

#### Special Study for Route 299 (including Appendix)

The Special Study for Route 299 (26) was done to determine the most effective mix of projects eligible for STIP funding over the next 20 years.  This covers Route 299 from Arcata to Redding.

### Documents Discussing California’s Traditional Approaches

#### Statewide Transportation Improvement Plan Interim Guidelines for 1998

The purpose of the Statewide Transportation Improvement Plan Interim Guidelines for 1998 (27) is to assist Caltrans and regions in the development of their project proposals for the 1998 State Transportation Improvement Program (STIP).  These guidelines include such topics as display of project descriptions and costs, shared balances and adjustments, commission action and adoption, STIP management, and STIP development schedule and procedures.

#### Interregional Transportation Improvement Plan (ITIP)

The Interregional Transportation Improvement Plan (28) contains information on the vision for the interregional system and strategies for development, measured performance of the transportation system, State highways overview, priority considerations for State highways, gateways, and factors for timing and selection of ITIP improvements.  The vision includes intercity passenger rail, grade separations at railroad crossings and mass transit guideways.  It also includes using advanced technologies on the highway system.  Analysis of the projects included in the prior plan indicated that most of the improvements contemplated in the earlier plan have not been accomplished and are still needed and of high priority.  Caltrans also realizes that new opportunities and challenges, not identified in the earlier planning efforts, may deserve active consideration.  This document also identifies high emphasis Interregional Routes and “Gateways”, which include 101, 99, 395, 58, 198, 41, 46, 152, 156, 20 and 299.

#### 1998 Interregional Transportation Improvement Program

The Interregional Transportation Improvement Program (29) includes a listing of projects on the California State highway system.  Most of the proposed highway projects are on focused and gateway routes that are needed to build the higher standard statewide truck system required for linking rural and smaller urban centers to the larger high growth urban centers.  These projects are designed to significantly improve safety while reducing interregional travel time for people and goods.

#### California Rural Advanced Transportation System

The California Rural Advanced Transportation System documents (30) are Caltrans’ major and minor programs of existing and planned construction in District 1 from the years 1994 to 2002.  The projects are listed by year, county, route, type of work, etc.  These documents also include a cost estimate for each project.

#### Shasta County Social Service Transportation Coordination Plan and Inventory

The Shasta County Social Service Transportation Coordination Plan and Inventory (31) is an inventory update where the findings from the inventory are used as a base to develop or reaffirm goals, objectives and policies for coordination of social service transportation systems, based on local conditions.  Each agency has a list of responsibilities based on the findings from the inventory.

#### Caltrans’ Planning Documents

This packet includes background information for Caltrans along with descriptions and tables of planned construction projects for their Transportation Programs.  These Programs include the State Highway Operation and Protection Program (SHOPP) and the State Transportation Improvement Program (STIP).

### Documents Discussing Oregon’s Advanced Technology-Related Approaches

#### Draft Emergency Operations Plan

The Draft Emergency Operations Plan (32) sets ODOT’s emergency response policy and provides for a coordinated response with ODOT’s local, state, federal, tribal, and private sector partners.  It describes what actions ODOT will take to respond to an emergency, emergency response roles of units within ODOT, and ODOT emergency response equipment, facilities, and resources.  This document also shows the locations of ports of entry, commercial service airports, general aviation airports and transit districts.

#### Model Incident Response Procedures

The Model Incident Response Procedures (33) are part of  ODOT’s Emergency Operations Plan.  The procedures provide guidance and instructions for ODOT employees to handle incidents, including disabled vehicles, obstacles or debris on the roadway, spilled cargo or material,  motor vehicle accidents, or any other situation which may affect normal traffic flow or pose a hazard to the public.  These procedures incorporate the use of news media, variable message signs, road and weather reports, and Emergency Aid Center signs.

#### Oregon ITS Strategic Plan 1997-2017

The purpose of the Oregon ITS Strategic Plan for 1997-2017 (34) is to identify transportation challenges and ITS solutions within the State of Oregon.  More specifically, it is designed to evaluate the effectiveness of different technologies that meet the present and future goals of the Oregon Transportation Plan, to develop a coordinated program of deploying suitable ITS technologies and strategies, to develop an institutional framework for ITS deployment and operations and to identify the necessary policies and legal parameters for successful ITS deployment.

#### Public Transit Management System Transportation Entities and Performance Results

The Public Transit Management System Transportation Entities and Performance Results documents (35) are summaries of all the transportation entities and the performance results for Regions 3, 4, and 5 in Oregon.  These documents include such information as operation hours, passenger trips, operating expense, cost/trip, etc. for the 1996 Fiscal Year.

### Documents Discussing Oregon’s Traditional Approaches

#### Final Statewide Transportation Improvement Program 1998-2001

The Final Statewide Transportation Improvement Program for 1998-2001 (36) prioritizes, schedules, and assigns funding to projects, thus defining the capital improvement program for Oregon.  The document includes multi-modal (highway, rail, aeronautics, public transit and safety) projects, thereby fulfilling the requirements of the Intermodal Surface Transportation Efficiency Act (ISTEA).  The document also includes projects of regional interest that are fully funded by the metropolitan planning organizations (MPOs) and projects on the state, city, and county transportation systems, as well as projects in the National Parks, National Forests and on Indian Reservations.  The program is updated every two years.

#### Oregon’s Visitor Industry

The Oregon’s Visitor Industry report (37) includes the following information on tourism in Oregon: direct economic impacts, employment, regional visitation, out-of-state and in-state visitors, visitor satisfaction and their trip characteristics.  This document also includes the locations of the rest areas in Oregon.

### Other Pertinent Documents

#### U.S. Department of Transportation’s Advanced Rural Transportation Systems Strategic Plan

The U.S. Department of Transportation’s Advanced Rural Transportation Systems Strategic (ARTS) Plan (1) defines the role of the Federal Government in developing rural ITS options.  It discusses the management strategy of the Government with emerging ITS technologies within rural settings from conception to viable options for implementation.  This Plan meets the needs of the U.S. Department of Transportation by providing a basis for decision making as well as addressing requirements of the Government Performance and Results Act (GPRA).

# existing and planned transportation systems

Existing and planned transportation systems fall into two categories.  These two categories are projects, programs and improvements that 1) are advanced technology-related, or 2) utilize traditional engineering approaches.  Since there are several advanced technology approaches that can be implemented to solve transportation issues, classifications that are more specific need to be used.  These classifications, called “clusters”, have evolved through several rural outreach sessions and represent the general categories that emerged from rural needs assessment studies and are defined by the United States Department of Transportation (USDOT) ARTS Strategic Plan (1).  Traditional engineering approaches can also be more specifically classified into three categories.  These categories are defined as 1) infrastructure programs and projects, 2) emergency medical services and 3) transit services.

## Advanced Technology-Related Approaches

Traditionally, research and application of ITS solutions have focused primarily on urban transportation problems and needs.  Advanced technology applications in rural settings offer a unique challenge in terms of needs, priorities, technologies, benefits, communications infrastructure, and public and private sector roles and responsibilities.  In an effort to simplify and organize research and application efforts, advanced approaches to rural transportation system problems and needs have been categorized into general focus areas or “clusters” called Critical Problem Areas (CPAs).  The seven CPAs are defined as:

- Traveler Safety and Security:  Addresses the need for improving driver ability to operate a vehicle in a safe and responsible way and for improving driver notification of potentially hazardous driving conditions.

Emergency Services:  Focuses on improving communications, management of emergency service fleets and critical information transmission. This cluster also deals with improving coordination efforts between service providers and improving real-time emergency information.

Tourism and Travel Information Services:  Focuses on providing travel information and mobility services to travelers unfamiliar with a rural area.

Public Traveler Services/Public Mobility Services:  Focuses on improving accessibility and reducing isolation for travelers using or relying on public transportation.

Infrastructure Operations and Maintenance:  Focuses on improving the efficiency and operation activities of rural transportation systems.

Fleet Operations and Maintenance: Focuses on providing efficient scheduling, routing, locating and maintaining of rural fleets.

Commercial Vehicle Operations: Focuses on the coordination and provision of services for rural fleet operations management (1).

The aforementioned clusters are not mutually exclusive and overlap is to be expected when all categories are utilized in a specific rural setting.  In addition, boundaries between cluster groups are not fixed, allowing relationships between cluster concepts.  Figure 1 shows the mutual and conceptual relationship between these clusters.

Figure 1: ARTS Critical Problem Areas Cluster Relationships (1).

Review and discussion of the advanced technology-related programs and planned improvements within the COATS corridor have been organized to align with the CPAs.  This method of organization will enable the review of current efforts to correspond with the National System Architecture (NSA), thereby ensuring compatibility with future project efforts in identifying applicable solution technologies and systems.

### Traveler Safety and Security

Systems within the study area that are classified in the Traveler Safety and Security CPA category include Road Weather Information Systems (RWIS), Automated High Wind Advisory Systems, Changeable Message Signing (CMS), Highway Advisory Radio (HAR), and Motorist-Aide Call Boxes.  Locations of existing and planned Traveler Safety and Security infrastructure are shown in Figure 2.

#### Road Weather Information Systems

Road and Weather Information Systems are designed to help transportation system managers, the motoring public, and commercial vehicle operators make better travel and/or maintenance decisions by describing current and predicted weather conditions.  RWIS stations may be used to relay pertinent travel information to motorists, including road surface conditions, wind speed and direction, air temperature, relative humidity, precipitation, visibility levels, snow depth and sub-surface temperature.  Transmission of information can be made through the Internet, kiosks or variable message signs.  Department of Transportation personnel may be able to use information from RWIS locations to update travel advisories or manage specific infrastructure operations, such as snow removal.  In the future, officials involved with these systems envision networking RWIS with similar systems in surrounding States.

Current efforts in northern California include three existing and 14 planned RWIS stations.  The planned RWIS sites in California are to be located in District 2 as part of its 5-Year ITS Implementation Plan (38).  One of the existing RWIS stations also contains an Automated Wind Advisory System and two of the planned RWIS stations are expected to utilize this system.  District 1 is planning to install pavement sensors south of Crescent City on Highway 101 (39).  These sensors will be linked to a variable message sign to indicate when potentially hazardous pavement conditions exist.

There are 38 existing and 18 planned RWIS sites in southern Oregon (40, 41).  Seven of the existing RWIS sites are located Region 2, 16 in Region 3, 12 in Region 4, and three in Region 5.  The planned RWIS stations are part of a two-phase project where eight of the RWIS stations are to be constructed in the fall of 1998 and the remaining 10 are scheduled to be constructed the following year.  Part of Oregon’s RWIS deployment provides for pavement conditions forecasting that enable maintenance crews to perform “pre-icing” treatments.

#### Automated Seismic Road Closure Systems

The seismic road closure system aids in highway operation and increased traveler safety and security by warning or redirecting bridge travel during seismic activity.  Bridges that have not been retrofitted for seismic activity can be fitted with automatic gates to close the highway during potentially unsafe conditions.  Sensors activate pagers to expedite DOT dispatch and response personnel so qualified employees can confirm the structural integrity of the bridge (39).

#### Dynamic Message Signing

Dynamic Message Signs (DMSs) which consist of either variable message signs (VMSs) or changeable message signs (CMSs), are used to transmit real-time data to transportation users.  Sophisticated DMSs may be updated using a modem from a satellite operation center or a traffic management center.  The primary use of these signs is incident management with secondary uses in maintenance and construction activities.

In California, there are 12 existing DMSs with plans for adding 30 additional signs.  Eight of the existing DMSs are permanent and four are portable.  Seven of the eight permanent DMS locations are within District 2 and the remaining one in District 1 (15).  All four of the portable DMS locations are within District 1.  In District 1 there are also five portable DMSs outside the corridor that would most likely be available for use within the corridor.  Nineteen of the planned DMS locations are for District 1 and 11 are for District 2.  The planned DMS locations in District 2 are part of that District’s 5 Year ITS Implementation Plan (38).

Oregon currently has one existing DMS in Region 3 and has plans (40) to implement two DMS locations in the fall of 1998.  The existing DMS is part of Oregon’s ITS Strategic Plan for 1997-2017 (34).

#### Highway Advisory Radio

Highway advisory radio is used to inform travelers of road conditions, weather conditions, possible road closures, chain requirements, and so forth, as well as an incident management aid.  This technology may be used with the DMSs to provide information that is more detailed.

Currently, there are nine existing and six planned highway advisory radio locations in California.  Four of the existing HAR locations are within District 1 (42), leaving the remaining five in District 2.  All of the planned HAR locations are within District 2 and are part of that District’s 5 Year ITS Implementation Plan (38).  One of the planned HAR locations is considered a Super Station.  According to the Oregon ITS Strategic Plan (34), Region 5 has installed DMS and a radio system for broadcasting weather conditions.

#### Motorist-Aide Call Boxes

Motorist-aide call boxes provide transportation users with the ability to call for roadside assistance.  Each call box location gives the motorist pertinent information, such as a call box telephone number, identification number, post-mile, county and highway information to help motorists identify their exact location.  District 1 has 71 call boxes covering 275 miles with an average spacing of 8.5 miles between boxes (43).  Current plans call for an additional 40 call boxes to be installed per year.  There are no motorist-aide call boxes in District 2 of California or in southern Oregon.

### Emergency Medical Services

Advanced technology-related emergency services that are existing or planned within the corridor include projects/programs that are specifically designed to enhance transportation-related challenges within emergency services.  These technologies may be used in any of the traditional emergency services such as fire stations, ambulance services, highway patrol, state police and air ambulance services.  Most of the information received from project participants did not include whether these types of advanced technologies existed in any of the existing emergency services.  The only plans for using ITS systems to enhance emergency services is in District 1 in California.  District 1 is planning to implement three advanced technology EMS systems near Willits, California by the year 2000 (15).

### Tourism and Traveler Information Services

Programs contained within this CPA include both public and private efforts designed to inform motorists of road and weather conditions, local and statewide points of interest, seasonal activities, highway maintenance operations or construction projects to provide additional information that may influence travel decisions.  Specific technologies that will be considered for discussion include Internet links and kiosks.  Figure 3 shows a map of the tourism and traveler information services available within the region.

#### Internet Links

Rapid growth in Internet use has made it possible to utilize it as an effective means of communication with travelers and tourists.  By providing real-time information, system users can be better informed as to possible delays, detours or basic travel news.  By connecting the Internet with various data collection devices, such as RWIS, critical weather information can be made available.  For those who travel frequently, monthly travel news reports can be sent to them using email.

The California Department of Transportation has developed Internet links for disseminating travel and tourist information (44).  Their website contains searchable information by route.  Plans are to have all of the RWIS, closed circuit television (CCTV) and HAR data, as well as DMS displays, available through the Internet.  Other Internet efforts are made mostly by private companies with a local interest in tourism or travel.

As part of Oregon’s ITS Strategic Plan for 1997-2017 (34), ODOT is planning to integrate RWIS information into their website (45).  Current efforts include a BBS/Internet Public Information System and email information transfer in Region 4.  ODOT has also developed a News Media Paging System in Region 4.  Private companies in Oregon also supply travel information via the Internet (46).  Oregon has now implemented their Travel Advisor on the Internet that provides real time information regarding construction, cameras, rail, airports, buses and scenic routes (www.odot.state.or.us/roads/index.htm).

#### Kiosks

Kiosks are a high quality technology used to disseminate pertinent information to travelers and tourists through a touchscreen interface.  Kiosks generally use laserdisk technology, which can be upgraded several times per year.  Kiosks also have the ability to be fitted with an Internet connection, allowing users to search for information that is updated on a more consistent basis.  General locations for kiosks might be truck stops, rest areas or visitor information centers.

California’s District 2 has plans for installing nine information kiosks at several rest areas and a truck stop and truck scale in 1998 as part of that district’s 5 Year ITS Implementation Plan (38).  Information regarding kiosk locations within District 1 was not provided.

There are 27 information kiosks currently being used in Oregon in Regions 2, 3 and 4 (47).  One kiosk is located in Region 2, 23 in Region 3 and three in Region 4.  Technologies using both DMS and information kiosks are planned for all regions of Oregon as part of Oregon’s ITS Strategic Plan for 1997-2017 (34).  As part of Oregon’s Green Light Project (45), a travel advisory system called “TRIPNET” is being designed that will provide motorists with real-time road and weather information from sophisticated monitoring devices.  This information can be delivered to motorists via the Internet or kiosks.  Specific locations have not yet been determined.  SOVA also has various kiosk locations around the State (46).

### Public Traveler Services/Public Mobility Services

This cluster is focused on providing accessibility to rural travelers, visitors and residents.  Some of the advanced systems to be considered to help improve mobility to these rural transportation users might be advanced transit or paratransit systems or advanced ride sharing and matching systems.  Other advanced systems might include technologies such as computer aided dispatching or improved fixed-route and demand responsive operations.  Information regarding advanced transit or paratransit systems has not been received from California.  Oregon is planning to develop 50 “smart” passenger and freight trains as part of the Oregon ITS Strategic Plan for 1997-2017 (34).

### Infrastructure Operations and Maintenance

In general, this cluster is focused on improving and automating pavement management systems, providing early detection and deployment of services, assisting in traffic operations and managing work zones.  Specific technologies within this cluster might include road weather information systems, variable message signs, automated scour detection systems, seismic bridge closure systems, high wind advisory systems, unstable slope monitors, highway advisory radio, closed circuit television (CCTV) cameras and automatic traffic recorders (ATRs).  Also included in this section is discussion related to current communications infrastructure.  Figure 4 shows a map of the infrastructure operations and maintenance within the region.

Current work in California includes flood and scour detection at two sites in District 2 (38).  This system is designed to automatically contact maintenance personnel when river flows reach a level in which scour will occur on a ‘scour-critical’ bridge, thereby ensuring continuous monitoring as to its structural integrity until scour conditions cease.

Closed circuit television cameras are used to verify and monitor traffic incidents and traffic, roadway and weather conditions.  There are currently four CCTV locations planned in District 2.  These existing and planned sites were all set up as part of District 2’s 5-Year ITS Implementation Plan (38).  There are no existing or planned CCTVs within District 1.

Current planning efforts in Oregon include installing four CCTV locations within the corridor.  These were developed as part of Oregon’s ITS Strategic Plan for 1997-2017 (34).  Also located within the corridor is one surveillance camera located in Region 3.  In addition, incident/traffic management centers were established in each region as part of this plan.  A more detailed discussion of these centers is given below.

#### Automatic Traffic Recorders

Automatic traffic recorders collect and store daily traffic volumes and axle configurations, allowing Department of Transportation personnel to download and utilize the data.  Data transmission can be made through hard connections like telephone or modem or through satellite connections in remote locations.

District 2 in California currently has 240 permanent traffic data recorder stations (48).  Information regarding ATR locations in District 1 and plans for additional installations of ATRs in either district was not provided.

Currently there are 39 full telemetry ATR locations in southern Oregon (49).  Four stations are located in Region 2, 19 in Region 3, 12 in Region 4 and four in Region 5.

#### Traffic Management Centers

Traffic Management Centers (TMCs) are used to coordinate operations and response associated with incidents within their defined boundaries.  Common incidents might include pass closures due to inclement weather conditions, debris on roadway or accidents.  Satellite operations centers have a Public Information Officer who controls the flow of information to the media and promotes and facilitates interagency coordination.

Northern California has two Satellite Operations Centers (SOCs), based out of the Sacramento TMC (16, 50).  These SOCs are located in Eureka and Redding.  These centers act as primary coordination points for Department of Transportation response to all types of major incidents within their jurisdiction.  Oregon has two TMC locations within the corridor (34), located in Bend and Medford.  There are also other TMCs and SOCs outside the corridor that help manage transportation facilities within the corridor.  The SOC outside the corridor is located in Kingvale, California and the TMCs are located in Marysville and Sacramento, California and in Portland and Salem, Oregon.

#### Regional Management Efforts

Regional management and coordination is critical to the success of all ITS systems.  Cooperation, communication and coordination of efforts between the many agencies and stakeholders within the study area is essential to an integrated and efficient program.

The communication infrastructure is the backbone of technology transfer and communication between agencies.  Both States in the COATS project use microwave, low-band UHF, 800 MHz radio, 47 MHz radio, cellular telephones, scanners, facsimile, telephone and Internet to transmit data, and to conduct public/private and public/public communication.  The majority of communication from office to field is conducted through microwave and radio.  Cellular communications are also used, depending on coverage.  Centrally located base stations allow multiple agencies to share the use of the microwave transmitters/receivers.  Emergency communication in California has recently been enhanced through the California Amateur Radio System (CARS), which utilizes high frequency (HF), 70 centimeter and 2 meter voice and digital modes as well as limited Continuous Wave (CW) on the HF system (51, 52, 53).

California and Oregon DOTs and Oregon State Police (OSP) are working together to coordinate northern California and southern Oregon maintenance crews and law enforcement agencies during emergencies or severe weather events.  The OSP has installed Automatic Computer Terminals in over 400 police cars and 375 troopers and are using a high band radio system for communication.

### Fleet Operations and Maintenance

Advanced technologies can be used to assist in fleet management and operations like scheduling, routing and maintaining fleet vehicles.  Services like advanced dispatching and routing, vehicle tracking or fleet maintenance and management can be provided to transit operators, paratransit operators and maintenance crews.  As part of California’s 5-Year ITS Implementation Plan for District 2 (38), an automated snowplow retrofitted with lane departure and collision warning systems will be deployed.  No information was provided for this type of activity in Oregon.

### Commercial Vehicle Operations

The Commercial Vehicle Operations CPA includes several ITS technologies and systems, such as Weigh-In-Motion (WIM), Automated Vehicle Identification (AVI), downhill speed warning and dynamic curve warning systems.  The systems that are discussed in detail below are also shown in Figure 5.

#### Weigh-In-Motion/Automated Vehicle Identification

When combined and properly integrated with a database management system, WIM and AVI form a technology known as the pre-clearance system.  Transponders carried by truckers contain information regarding the vehicle’s registration, tax payments, truck size, weight and height.  Coupling this system with the existing ATRs provides a valuable data collection tool for transportation system managers.

Current efforts in California include five weigh-in-motion sensors and two automatic vehicle identification systems.  The technologies are located in District 2 and established as part of their 5-Year ITS Implementation Plan (38).  District 1 has one WIM site and is planning to add another WIM location in 1999 (15).  District 2 also has two automatic truck-pass systems that use both WIM and AVI on Interstate 5.

As part of Oregon’s ITS Strategic Plan for 1997-2017 (34), several new technologies have been integrated into the system and others are yet planned for commercial vehicle operations.  The Oregon Department of Transportation’s Motor Carrier Division has implemented many new systems, including commercial vehicle information systems and networks (CVISN), downhill truck speed information systems (DSIS), GPS and direct communication, highway warning systems for weather hazards, integrated tactical enforcement network (ITEN), license plate

readers, pre-clearance systems, roadside communication systems and safety enhancements, and hardware and software upgrades.  Altogether, the planned systems in Oregon include 10 additional pre-clearance sites, two DSISs with weigh-in-motion, plate readers and overhead DMS, and additional integrated tactical enforcement networks.

#### Speed and Curve Warning Systems

Downhill speed-warning systems are designed to inform the commercial vehicle operator of safe operating speeds for downhill grades.  They feature weigh-in-motion scales, automatic vehicle identification readers, and overhead variable message signs.  As trucks pass over the WIM scales, the AVI reader identifies the truck and recommends a safe downhill speed based on the vehicle’s weight.  Manual override of the system allows spontaneous messages to be displayed to notify motorists of emergencies when they arise.

The dynamic curve warning system is designed to warn motorists of upcoming curves that are potentially dangerous, depending on the speed of the vehicle.  Variable message signs are used to display current vehicle speed, safe speed and a short informative message.  This system can be linked to TMCs for up-to-date messaging.

As of now, there are no speed warning systems or dynamic curve-warning systems installed within northern California.  However, there are plans for installing five Radar Changeable Message Signs (RCMS), that are part of the dynamic curve warning systems, in District 2 as part of its 5-Year ITS Implementation Plan (38).  These systems are to be installed in late 1998.

Oregon also has no speed warning or dynamic curve warning systems currently installed within the study area.  Plans for installing one speed warning system are tentatively scheduled for mid-1999 (34).  This site will include WIM, AVI and a DMS.

## Traditional Projects, Programs and Improvements

Traditional projects, programs and improvements are defined as solutions to transportation challenges that do not involve advanced technology-related systems (i.e., ITS technologies).  Traditional programs that are included in this section are those relating to infrastructure, emergency medical services and transit services.

### Infrastructure

The types of systems that will be considered for discussion are existing or planned traditional approaches to infrastructure challenges as found in each State’s transportation improvement plans and other infrastructure facilities.  The other categories include rail facilities, airports, marine facilities, intermodal transfer locations, safety rest areas and commercial vehicle facilities.  Figure 6 shows these traditional infrastructure elements.

Many of the traditional improvements were found using the Statewide Transportation Improvement Plans (STIPs), Interregional Transportation Improvement Plans (ITIPs) or Statewide Highway Operation and Protection Programs (SHOPPs) for each State (27, 28, 29, 36, 54).  STIP and non-STIP projects for California and Oregon include safety projects, rehabilitation, overlays and other types of construction.  The STIPs for each State are contained within Geographic Information Systems (GIS) databases, and are continually updated with current information.  Non-STIP projects, such as major and minor reconstruction/maintenance projects, are included when sufficient information is available.  A brief description of some of these projects, programs and improvements, as supplied by the Departments of Transportation in California and Oregon, are given in the following sections with details located in Appendix B (California) and Appendix C (Oregon).

#### Rail

Locations of rail lines and freight transfer facilities were obtained from US Census Bureau TIGER line data (55).  A noteworthy rail project in the corridor is a rehabilitation effort on 12 miles of railroad between Alturas, California and Lakeview, Oregon.  The project will involve the installation of new railroad ties between the Oregon/California border and industries in Lakeview.  Trains will be able to operate at 25mph after the project, which is a 15mph improvement over today’s speeds (34).

#### Air

Air transportation can be an effective means of transferring goods and travelers.  The locations of all major airports in California were located using a 1997-98 California Aeronautical Chart (56).  Airports in Oregon were found using Oregon’s Draft Emergency Operations Plan (32) and an Oregon highway map (57).  The purpose of this task was to identify and locate airports of sufficient size to promote and utilize intermodal transportation.  Airports with paved runways 1500 feet or greater were considered.

#### Marine

Marine facilities offer great intermodal potential, since ships loaded with cargo boxes often can be transferred to rail or truck.  California has three marine facilities near Highway 101 (17).  Region 3 in Oregon contains 14 marine facilities eight of which are located in Coos Bay and six in North Bend (58).

#### Intermodal Hubs

Intermodal programs and projects include systems that deal with the movement of goods through and within the corridor.  This usually involves more than one transportation mode, such as rail, marine, truck or air.  Specific programs include rail facilities, airports, commercial vehicle loading/unloading facilities and marine ports.  Information on these types of facilities was not provided by California, but it is assumed that these types of facilities exist.  Oregon currently has 10 unload/reload facilities: six in Region 2 (Eugene), three in Region 3 and one in Region 4 (58).

#### Safety Rest Areas

Safety rest areas are an integral part of the transportation infrastructure.  They provide opportunities for travelers to obtain travel information and help to refresh weary motorists.  Advanced technology-related systems utilized at these locations are discussed in previous sections of this report.

The State of California currently has 30 safety rest areas within the corridor (59).  Six are located in District 1, 22 in District 2 and two in District 3.  Information regarding plans for additional safety rest areas or upgrades to existing facilities was not provided.

Oregon currently has 15 safety rest areas within the corridor (60).  Two are located in Region 2, seven in Region 3, four in Region 4 and two in Region 5.  Other rest areas are owned and operated by the National Park Service but are not considered “safety” rest areas.  Information regarding plans for additional safety rest areas or upgrades to existing facilities was not provided.

#### Commercial Vehicle Operations

Traditional projects and programs involving commercial vehicle operations are included in one of three categories: unloading/reloading facilities, infrastructure facilities and weigh stations.  Since unloading/reloading facilities were discussed in more detail above, it will not be included in the discussion below.  Commercial vehicle infrastructure projects, programs and improvements include runaway truck ramps and weigh stations, inspection stations and brake check stations.  The map in Figure 7 shows the location of each of these elements.

Runaway truck ramps provide commercial vehicle operators the opportunity to leave the roadway and slow the vehicle in case of brake failure.  In California’s District 1, there are two runaway truck ramps and in District 2 there are three such facilities.

Weigh station facilities are considered a traditional approach to controlling and checking commercial vehicle operations (61, 62, 63).  There are several weigh station facilities within the COATS study area.  Plans for additional weigh station locations in both California and Oregon have not been made; however, plans for upgrading existing weigh stations with ITS technologies exist and was discussed in Section 2.  Information regarding truck inspection facilities and brake check stations was also received from District 1 (15).

### Emergency Medical Services

Traditional emergency medical services include fire stations, highway patrol, public and private ambulance services (ground and air) (64, 65).  These services are listed in the appropriate section in Appendix E.  Figure 8 shows the locations of each of these service types.

### Transit Systems

Current transit efforts in California include bus systems, passenger rail trains, rideshare programs and park-and-ride lots (19, 66, 67, 68).  There are seven bus stations within the corridor: four in District 1, and three in District 2.  In District 1, bus lines include the Mendocino Stage and the MTA Coast Van; in District 2, bus lines are the Lassen Rural Bus and the Sage Stage.  There are eight passenger rail train facilities in District 1 and three in District 2.  There are several transit providers in both districts.  In District 1, there are seven transit providers and in District 2 there are four transit providers.  There are five park-and-ride lots in California’s District 1 (42, 15) and none in District 2.  In District 1, there are two dial-a-ride providers and none in District 2.

California currently has 14 park-and-ride lots within the corridor.  The purpose of these lots is to provide a place to store an automobile while the passengers ride transit or are involved in a ridesharing program.  There are seven existing park-and-ride lots in District 1 and seven in District 2.  Plans for additional park-and-ride lots in either District have not been made; however, one lot in District 1 has plans to be eliminated due to low use.

Transit efforts in Oregon consist of bus stations, passenger rail stations, rideshare programs and various other improvement efforts (35).  Currently there are seven bus stations: one in Region 2, three in Region 3 and three in Region 4.  There are three passenger rail stations: one in Region 2 and two in Region 4.

Other efforts include an ODOT, Region 3 program designed to reduce single-occupant vehicles near urban centers, and encourage transit use.  Oregon also has plans for implementing programs like a Carpool/Transportation Demand Management (TDM) program, several rideshare programs, park-and-ride lots and bus rapid transit.  Many of the planned systems are included in the STIP for Oregon located in Appendix C.  A map of the traditional transit services and routes within the corridor are shown in Figure 9.

# Summary

The three main steps in developing the Review of Legacy Systems report were to 1) make contacts and gather information regarding legacy systems, 2) review and organize information and 3) tabulate and geographically map important transportation systems/solutions.  Contacts were made by sending a survey to all project participants that requested pertinent project information and additional contacts.  Follow-up to these additional contacts allowed a more complete database to be developed.

Information collected from project participants and stakeholders was organized into two main categories: advanced technology-related projects, programs and improvements and traditional projects, programs and improvements.  The advanced technology-related projects, programs and improvements were also divided into several categories corresponding to the ARTS CPAs.  The traditional projects, programs and improvements were divided into three categories: highway, intermodal and commercial vehicle operations.

The appendices contain the organized data from the surveys and personal interviews.  To better show the geographic locations of these technologies, maps were formed using this information.  However, due to the large volume of traditional programs and projects proposed within the corridor, GIS maps were not made to illustrate this information.

Information contained in this report cannot, by itself, be used to make recommendations regarding the implementation of ITS-related projects and programs.  Rather, this information was gathered to document previous and future efforts to avoid duplication of programs or projects.

Volume II attempts to identify and define potential transportation challenges within the COATS study area.  These challenges may include safety problems, congestion, freight movement, incident response, mobility, tourism, environmental impacts and deteriorating infrastructure.  By integrating the work in the Review of Legacy Systems report with the work in Volume II, possible solutions to these challenges can be formulated.

References

Advanced Rural Transportation Systems (ARTS) Strategic Plan, 1997, US Department of Transportation, Federal Highway Administration.

Interstate 5 Canyon Closure, February 1996, Caltrans.

Route Concept Report – Route I-5, November 1984, Caltrans.

Route Concept Report – Route 3, July 1990, Caltrans.

Route Concept Report – Route 36, October 1984, Caltrans.

Route Concept Report – Route 44, October 1984, Caltrans.

Route Concept Report – Route 89, June 1990, Caltrans.

Route Concept Report – Route 96, June 1990, Caltrans.

Route Concept Report – Route 97, October 1984, Caltrans.

Route Concept Report – Route 101, November 1994, Caltrans.

Route Concept Report – Route 139, October 1990, Caltrans.

Route Concept Report – Route 161, December 1988, Caltrans.

Route Concept Report – Route 299, October 1984, Caltrans.

Route Concept Report – Route 395, October 1984, Caltrans.

District 1 Long Range Operational Plan (LROP) and Modal Transfer Locations, May 1998, Caltrans.

Transportation Management Center Master Plan, December 1997, Caltrans.

District 1 System Management Plan, November 1992, Caltrans.

1998/99 Transit Needs Assessment for Shasta County, January 1998, RTPA.

Draft - Regional Transportation Plan for Shasta County, September 1996, Regional Transportation Planning Agency (RTPA).

Caltrans Strategic Plan, 1998, Caltrans.

Caltrans Strategic Plan Supplemental: Strategic Priorities and Implementation Framework, 1998, Caltrans.

Feasibility of ITS Applications in Rural California, February 1997, Western Transportation Institute.

Traffic Management Plan: State Route-70 Corridor, July 1998, Caltrans.

Caltrans Emergency Operations Plan, January 1998, Caltrans.

Caltrans Incident Command System, No date, Caltrans.

Special Study for Route 299 (including Appendix), May 1993, Caltrans.

Statewide Transportation Improvement Plan Interim Guidelines (STIP), January 1998, Caltrans.

Interregional Transportation Improvement Plan (ITIP), January 1998, Caltrans.

1998 Interregional Transportation Improvement Program, March 1998, Caltrans.

California Rural Advanced Transportation System, May 1998, Caltrans.

Shasta County Social Service Transportation Coordination Plan and Inventory, February 1998, RTPA.

Draft Emergency Operations Plan, February 1998, ODOT.

Model Incident Response Procedures, July 1997, ODOT.

Oregon ITS Strategic Plan 1997-2017, January 1998, DKS Associates, Pacific Rim Resources, ODOT.

Public Transit Management System Transportation Entities and Performance Results, May 1998, ODOT.

STIP, Final Statewide Transportation Improvement Program 1998-2001, December 1997, ODOT.

Oregon’s Visitor Industry, May 1998, ODOT.

District 2: 5 Year ITS Implementation Plan, May 1998, Caltrans.

Telephone conversation with Jim Graham of District 1, California, May 1998.

Planned RWIS and DMS Sites in Oregon, as of September 1998, ODOT.

RWIS Information for Oregon, as of May 1998, ODOT.

District 1 CMS/HAR Listings and Park & Ride Lots, May 1998, Caltrans.

Motorist-Aid Call Box Locations, as of September 1998, Caltrans.

Internet Links for Travel and Highway Information, as of September 1998, Caltrans Internet Web Site --www.dot.ca.gov/hq/roadinfo/index.htm.

Oregon Department of Transportation Internet Web Site, ODOT, www.odot.state.or.us/.

Southern Oregon Visitors Association (SOVA) Internet website, www.sova.com/.

Southern Oregon Information Kiosk Locations, as of June 1998, ODOT.

Permanent Traffic Recorder Station Locations, as of September 1998, Caltrans.

Permanent Automatic Traffic Recorder Station Locations, February 1996, ODOT.

Map of Existing Traffic Management Centers and Satellite Operations Centers, Caltrans.

Maps of the Communication System by District, June 1988, Caltrans.

ODOT Microwave System, June 1998, ODOT.

Caltrans Public Safety Radio System, as of July 1998, Caltrans.

Caltrans Transportation Programming – STIP and SHOPP, August 1998, Caltrans.

National Rail Network (1:100,000), 1997, Bureau of Transportation Statistics, Washington, DC.

California Aeronautical Chart, 1997-1998, Caltrans.

The Official State Map of Oregon, 1997-98, ODOT.

Intermodal Information for Oregon, as of June 1998, ODOT.

Roadside Rest Area Information, as of June 1998, Caltrans Internet Web Site, www.dot.ca.gov/hq/row/tccw/roadside.htm.

Rest Area location information – Fax, as of June 1998, ODOT.

California Weigh Station Information, June 1998, California Highway Patrol.

List of Existing Commercial Vehicle Enforcement Locations, as of September 1998, Caltrans Internet Web Site – www.dot.ca.gov/hq/traffops/trksnwim/weight/loclist.htm.

Oregon Truck Weigh Stations, May 1998, ODOT.

List of California EMS Organizations, as of September 1998, Emergency Medical Services Authority (EMSA) Internet Web Site – www.emsa.cahwnet.gov/

List of Fire Departments in Oregon, as of September 1998, Oregon Department of State Police.

Redding Area Bus Authority (RABA) System Map, September 1998, RABA.

Summary of Transit Services in District 2, as of September 1998, Caltrans.

California Transit Services in the Rural COATS Study Area, as of August 1998, Caltrans.

Appendices

Appendix A – Data Collection Survey

TRAFFIC DATA AND INFORMATION

Traveler Facilities

Please provide the number and location of the rest areas for which your agency is responsible.  (provide map if it is more convenient)______________________________

Traffic Data

Please supply traffic volume (ADT, and/or AADT), vehicle classifications, and other available traffic data for the routes contained within the corridor.  ___________________

Please supply available information on O-D surveys conducted within the study area. ________________________________________________________________________

Crash Data

Please supply three years of accident data on all corridor routes.  All available data fields are needed to determine analysis possibilities.  If possible, contact Pat McGowen, WTI, prior to assembling these data to determine the preferred format and data fields.  ________________________________________________________________________

Are animal-vehicle collisions a problem within the corridor?  If so, what data are collected regarding these crashes?  (please provide) ______________________________

Hazardous Materials Incident Data

Please provide information on all HAZMAT-related incidents/crashes that have occurred on the corridor roadways in the past three years.  Attach or send electronic file. ________________________________________________________________________

Commercial Vehicles (CVO)

On your main through routes, what is the average daily truck traffic on the main travel routes? _________________________________________________________________

Please provide information on weigh station operations and capabilities regarding weight, size, IFTA, etc… _________________________________________________________

Are there any size/weight/cargo restrictions on routes within the study area?  If so, please specify. _________________________________________________________________

Roadway Inventory

Do you have an inventory of roadway characteristics for the corridor routes in your area? (Lane widths, shoulder width, striping, guard rail, no-passing zones, etc.)  Please supply electronic copies or attach. __________________________________________________

TRANSPORTATION IMPROVEMENT NEEDS

Please provide a paper or electronic copy (if available) of improvement plans for the corridor routes including STIP and non-STIP programmed projects._________________ ________________________________________________________________________

Please list the transportation system challenges in your jurisdictions.  These would consist of items such as congested corridors, access constraints, lack of transit service, high accident areas and signal coordination. ___________________________________

Emergency Response

Do you have information on emergency notification and response times?  If so, please provide 3 year history of accident notification and response times via electronic file: Preferred format: Excel or Access. ___________________________________________

VISITOR CHARACTERISTICS

Demographics

Do you have information on visitors or tourists who visit your area (group size, age, time spent, origin, number of visits, method traveler learned of your establishment, transportation information utilized, median income, average $ spent on trip, etc.)?  If yes please supply or attach. ____________________________________________________

Public Transportation

Agencies/Operators

Are there public transit systems operating in your area?  If so, please provide the following information.

Transit Agency Name(s): ___________________________________________________

Who operates and controls this system?  _______________________________________

What type of system is it? (fixed route, demand responsive, etc.)____________________

What is its area of coverage? ________________________________________________

What are, if any, the plans for improvements or upgrades to this system? _____________

What is the size of the transit fleet and total ridership?  ___________________________

What category does the typical passengers fit into?  Elderly, Mobility-Impaired, Disabled, General Public?  __________________________________________________

What is the average number of refused rides per month (and reason)?________________

________________________________________________________________________

What system used for communication with the vehicles?  _________________________

Is there a system used to automate or partially automate vehicle dispatch (i.e., computer-aided dispatch)? __________________________________________________________

Intermodal Opportunities

Modal Transfer Locations

Please list (if any) modal transfer points located in your jurisdiction.  This would include items such as airports, bus stations, rail stations, ocean ports, and park-n-ride lots. ________________________________________________________________________

Is anything prohibiting modal transfers or use of other modes?  If so, please explain. ________________________________________________________________________

Are there currently any plans to improve the modal transfer system?  ________________

Have there been any advanced technology (ITS) studies in your area?  If yes please provide title and author.  ___________________________________________________

Inventory of Stakeholders

Stakeholders are individuals, groups or institutions who have a direct “stake” or primary interest in the improvement of the transportation system in the study area.

Please give the name and address of any major stakeholders, in your jurisdiction, that should be considered for inclusion in the planning process.  (e.g. Large Employers, Transit Providers, Tourist Attractions, Freight Operators, Military Institutions, Major Activity Centers, Special Event Centers, etc.) Use additional sheets if necessary. ________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

EXISTING AND PLANNED SYSTEMS

Communications Infrastructure

What one-way and two-way communications technologies are used within your agency operations, who is responsible for maintaining the system, and where are they located?  Provide a map if necessary.  Potential technologies include radio repeaters, Cellular radio/phones, microwave towers, Internet, Fax, Telephone, etc.

________________________________________________________________________________________________________________________________________________________________________________________________________________________

Do you share communications resources with any other agency? If so, please specify.  Communications methods may include: 2-way radio towers/repeaters (locations), cellular, radio, phone, fax, Internet, state mutual aid radio frequency, UHF/VHF frequency use/agreements, etc.…

________________________________________________________________________________________________________________________________________________________________________________________________________________________

Traveler Safety and Security

How does your agency learn of unsafe travel conditions?  _________________________ ________________________________________________________________________

How do you inform the traveling public of unsafe or potentially hazardous driving conditions (weather, traveling at excessive speed for conditions, etc.)?  ____________ ________________________________________________________________________

Where are these information devices located?  (please provide milepost, geographic location, or a map) ________________________________________________________

Does the area within the corridor have adequate cellular coverage?  If not, where are the deficiencies? _____________________________________________________________

Are there current methods for disseminating information on road closures, incidents, major events, etc. that will require traveler re-routing or delay? _____________________  ________________________________________________________________________

Weather Information and Roadway Management

Where do you have permanent count stations? (Please provide mile post, geographic location or a map) ________________________________________________________

How are the count stations controlled, and how is data transmitted/collected from these count location(s)? (fiber optics, download from portable collector, modem, radio, custom software, etc.) ____________________________________________________________

Are there any other surveillance/data collections systems (not mentioned above) that are in your area (detectors, weather sensors, cellular call-in, etc.)? _____________________  ________________________________________________________________________

Are there any Road Weather Information System (RWIS) sites on routes within the study area?  __________________________________________________________________

Are there any planned installations of such equipment in the future? ________________

How are RWIS or other weather data sources used in your jurisdiction/area within the corridor? _______________________________________________________________

Travel and Tourism Information and Services

The following questions apply to technologies such as Variable Message Signs (VMS), Highway Advisory Radio (HAR), Kiosks, Internet, etc.

What methods are used to provide the traveler with important traffic information? (Please provide operational information, milepost, geographic location or a map if applicable.)?_____________________________________________________________

How is the information updated? _____________________________________________

How is the system controlled and managed? ____________________________________

What type of information is sent by this system (standard messages)? ________________ ________________________________________________________________________

How many of these technologies are portable installations versus fixed installations? ________________________________________________________________________

What is the primary purpose message capability, and message associated with each system? _________________________________________________________________

What are the secondary uses of these systems? __________________________________

How do you inform the public about the existence of the system or presence of a current message being broadcast/displayed? __________________________________________

Are the messages prerecorded, just-in-time, or real-time? _________________________

How is the system powered? (AC, DC, solar, etc.) _______________________________

Commercial Vehicle Operations

What electronic pre-clearance, automated credential information systems, and automated enforcement capabilities are available within the corridor? _______________________ _______________________________________________________________________

Regional Management and Coordination

What regional centers are available for coordination of incident response, traffic management, emergency management, etc. ____________________________________

How do the centers coordinate on a local level? _________________________________

State/National Park Operations

What existing systems and facilities help to alleviate congestion in the State and National Parks within the study area? ________________________________________________

Are there any parking management strategies used in the State and National Parks in the Study area? _____________________________________________________________

ITS Programs/Activities

What other ITS activities/programs exist or are underway in your jurisdiction within the study area?  Please describe. ________________________

Appendix B – California Major and Minor STIP

| Fiscal Year | County | Route | Mile Post | Type of Work | Under Construction |
| --- | --- | --- | --- | --- | --- |
| Major STIP |
| 96-97 | Hum | 96 | 19.4-21.9 | Remove Slides & Realign | Compl. |
| 96-97 | Hum | 101 | 8.9-11.3 | Rehabilitate Roadway - CAPM | Compl. |
| 96-97 | Hum | 101 | 61.5-64.3 | Rehabilitate Roadway - CAPM | Compl. |
| 96-97 | Hum | 101 | 79.9-86.5 | Rehabilitate Roadway - CAPM | Compl. |
| 96-97 | Hum | 101 | R97.5-100.7 | Roadway Rehabilitation & Seismic | Yes |
| 96-97 | Hum | 299 | 0.0-5.9 | Rehabilitate Roadway - CAPM | Compl. |
| 96-97 | Hum | 299 | R1.5-R1.6 | Rehab Bridge (Scour) | Yes |
| 96-97 | Lak | 20 | 41.6 | Slide Repair | Compl. |
| 96-97 | DN,Hum,Lak,Men-Var |  |  | Curb Ramps | Compl. |
| 96-97 | DN | 101 | 36.1-36.2 | Seismic Retrofit | Compl. |
| 96-97 | DN | 199 | 22.3, 23.8 | Remove Slides | Compl. |
| 96-97 | Hum | 96 | 12.3-12.5 | Seismic Retrofit | Compl. |
| 96-97 | Hum | 96 | 25.3-R41.0 | Reconstruct Embankment | Compl. |
| 96-97 | Hum | 96 | R44.3 | Install Temporary Bridge | Compl. |
| 96-97 | Hum | 101 | 27.1-27.2 | Seismic Retrofit | Compl. |
| 96-97 | Hum | 101 | 67.4-67.5 | Reconstruct Buttress | Compl. |
| 96-97 | Hum | 101 | R129.8 | Restore Roadway | Compl. |
| 96-97 | Hum | 254 | 8.6 | Place RSP | Compl. |
| 96-97 | Hum | 254 | 10.8-10.9 | Restore Roadway |  |
| 96-97 | Hum | 255 | 0.2-0.6 | Seismic Retrofit |  |
| 96-97 | Hum | 255 | 0.6-1.3 | Seismic Retrofit |  |
| 96-97 | Hum | 255 | 0.6-1.3 | Seismic Retrofit - Activated Gates | Yes |
| 96-97 | Hum | 299 | R1.5-R1.6 | Seismic Retrofit | Yes |
| 96-97 | Hum | 299 | R25.0 | Restore Roadway | Compl. |
| 96-97 | Lak | 20 | 37.4, 39.2 | Restore Embankment | Compl. |
| 96-97 | Lak | 175 | 21.5 | Restore Roadway |  |
| 96-97 | Men | 1 | 52.6-59.7 | Seismic Retrofit | Compl. |
| 96-97 | Men | 1 | 62.0-62.6 | Seismic Retrofit | Yes |
| 96-97 | Men | 1 | 69.7-69.8 | Bridge Replacement |  |
| 96-97 | Men | 1 | 104.5 | Remove Slide & Reconstruct Roadway | Compl. |
| 96-97 | Men | 20 |  | Seismic Retrofit | Compl. |
| 96-97 | Men | 20 | 25.9, 28.5 | Restore Embankment | Compl. |
| 96-97 | Men | 20 | 33.6 | Seismic Retrofit | Compl. |
| 96-97 | Men | 101 | 93.7-93.8 | Seismic Retrofit |  |
| 96-97 | Men | 101 | 87.0, 99.7 | Remove Slides, Place K-rail, Pilot Car | Compl. |
| 96-97 | Men | 128 | 31.6-36.1 | Restore Embankment | Compl. |
| 96-97 | Men | 175 | 0.4 | Seismic Retrofit | Compl. |
| 96-97 | Men | 253 | 2.0-2.1 | Restore Roadway | Compl. |
| 96-97 | Men | 271 | 4.8-5.4 | Seismic Retrofit | Yes |
| 96-97 | Sis | 96 | 13.7-13.9 | Restore Roadway | Compl. |
| 96-97 | Tri | 299 | 4.7 | Restore Roadway |  |
| 97-98 | DN | 199 | 8.5-8.6 | Stabilize Roadway |  |
| 97-98 | Hum | 101 | 70.6-73.1 | Rehabilitate Roadway |  |
| 97-98 | Hum | 254 | 24.1, 42.8 | Place RSP & Restore Embankment | Yes |
| 97-98 | Men | 1 | 20.8-38.7 | Rehab Roadway - CAPM | Yes |
| Fiscal Year | County | Route | Mile Post | Type of Work | Under Construction |
| Major STIP |
| 97-98 | Men | 1 | 75.8-75.9 | Restore Roadway | Yes |
| 97-98 | Men | 101 | 2.1, 3.2 | Restore Roadway | Yes |
| 97-98 | Men | 162 | 13.7-15.2 | Restore Embankment & RSP |  |
| 97-98 | Lak | 20 | 38.1-38.5 | Curve Correction |  |
| 97-98 | Men | 101 | 35.5-39.1 | Median Barrier | Compl. |
| 97-98 | DN | 101 | 14.4-14.7 | Install Tieback Wall |  |
| 97-98 | Hum | 96 | 16.6-16.7 | Remove Slide | Yes |
| 97-98 | Hum | 96 | 19.9-21.5 | Restore Roadway |  |
| 97-98 | Hum | 96 | 25.2-27.3 | Restore Roadway |  |
| 97-98 | Hum | 101 | 24.6-86.6 | Restore Roadway | Compl. |
| 97-98 | Hum | 101 | 29.3-29.5 | Constr. Stab Trench | Yes |
| 97-98 | Hum | 101 | R94.0 | Stabilize Slope |  |
| 97-98 | Hum | 101 | R129.2-R129.5 | Restore Slopes |  |
| 97-98 | Hum | 101 | R131.5 | Repair Embankment |  |
| 97-98 | Hum | 101 |  | Maintain Roadway | Yes |
| 97-98 | Hum | 169 |  | Restore Roadway | Yes |
| 97-98 | Hum | 254 | 12.7-22.5 | Restore Roadway |  |
| 97-98 | Men | 1 | 4.7-6.7 | Restore Roadway |  |
| 97-98 | Men | 1 | 6.7-6.8 | Restore Roadway | Yes |
| 97-98 | Men | 1 | 41.1-41.2 | Restore Roadway | Yes |
| 97-98 | Men | 1 | 41.2-41.3 | Restore Roadway | Yes |
| 97-98 | Men | 1 | 71.8 | Restore Roadway | Yes |
| 97-98 | Men | 1 | 82.1 | Realign Roadway |  |
| 97-98 | Men | 20 | 15.4-15.5 | Remove Slide & Place Rock | Yes |
| 97-98 | Men | 20 | 20.2-20.3 | Remove Slide | Yes |
| 97-98 | Men | 101 | R34.4 | Rock Buttress | Yes |
| 97-98 | Men | 101 | R84.9-R101.9 | Stabilize Slopes | Yes |
| 97-98 | Men | 101 | 87.0-87.2 | Remove Slide | Yes |
| 97-98 | Men | 128 | 3.5-7.7 | Restore Roadway | Yes |
| 97-98 | Men | 162 | 15.5-20.9 | Reconstruct Embankment | Yes |
| 97-98 | Men,Lak | 175 |  | Restore Roadway |  |
| 97-98 | Men | 253 | 10.2-10.3 | Restore Roadway | Yes |
| 97-98 | Men | 271 | 0.2-18.6 | Restore Roadway |  |
| 98-99 | DN | 169 | 2.5-2.7 | Upgrade Rail & Widen |  |
| 98-99 | Hum | 36 | 13.5-35.4 | Rehab Roadway - CAPM |  |
| 98-99 | Hum | 96 | 3.8-8.6 | Rehab Roadway - CAPM |  |
| 98-99 | Hum | 96 | 8.6-R14.2 | Rehab Roadway - CAPM |  |
| 98-99 | Hum | 101 | 0.3-R17.9 | Rehab Roadway - CAPM |  |
| 98-99 | Hum | 101 | R17.9-R22.4 | Roadway Rehabilitation |  |
| 98-99 | Hum | 101 | 106.1-109.7 | Rehab Roadway - CAPM |  |
| 98-99 | Hum | 299 | 19.0-R29.2 | Rehab Roadway - CAPM |  |
| 98-99 | Lak | 20 |  | Rehab Roadway - CAPM |  |
| 98-99 | Lak | 29 | 0.0-19.9 | Rehab Roadway - CAPM |  |
| 98-99 | Lak | 29 | R40.4-52.4 | Rehab Roadway - CAPM |  |
| 98-99 | Men | 1 | 0.1-15.2 | Rehab Roadway - CAPM |  |
| 98-99 | Men | 1 | 43.1 | Clean & Paint Bridge |  |
| 98-99 | Men | 1 | 48.2-59.7 | Rehab Roadway - CAPM |  |
| 98-99 | Men | 1 | 60.2-60.4 | Replace Bridge |  |
| 98-99 | Men | 1 | 60.3 | Clean & Paint Bridge |  |
| 98-99 | Men | 1 | 83.0-83.5 | Realign Roadway |  |
| Fiscal Year | County | Route | Mile Post | Type of Work | Under Construction |
| Major STIP |
| 98-99 | Men | 20 | 36.4-36.5 | Widen Bridge & Upgr Rail |  |
| 98-99 | Men | 101 | R87.5-T91.3 | Rehab Roadway - CAPM |  |
| 98-99 | Men | 101 | 100.1-R101.2 | Rehab Roadway - CAPM |  |
| 98-99 | Men | 101 | R101.2-T104.2 | Rehabilitate Roadway |  |
| 98-99 | Hum | 299 | 41.2-R42.1 | Passing Lanes E/B & W/B |  |
| 98-99 | Men | 1 | 59.8-62.1 | Widen, Channel. & Signals |  |
| 98-99 | Men | 101 | 72.0-73.0 | NB & SB Passing Lanes |  |
| 98-99 | Men | 101 | 72.0-73.0 | Passing Lanes N/B & S/B |  |
| 98-99 | DN | 101 | 20.3-22.3 | 4-Lane Expressway |  |
| 98-99 | Men | 253 | 2.3-2.7 | Restore Roadway |  |
| 98-99 | Men | 128 | 1.6 | Repair Eroded Embankment |  |
| 98-99 | Men | 128 | 4.2 | Repair Eroded Embankment |  |
| 98-99 | Men | 101 | 0.8-5.0 | Road Rehabiliation (ADD ON to Allocation) |  |
| 99-00 | DN | 101 | 26.2-26.8 | Roadway Rehabilitation |  |
| 99-00 | DN | 199 | T0.5-36.4 | Rehab Roadway - CAPM |  |
| 99-00 | DN | 199 | 30.8-33.5 | Roadway Rehabilitation |  |
| 99-00 | Hum | 101 | 28.5-33.2 | Roadway Rehabilitation |  |
| 99-00 | Hum | 101 | 33.2-35.8 | Rehabilitate Roadway |  |
| 99-00 | Hum | 101 | 78.0-79.8 | Rehabilitate Roadway |  |
| 99-00 | Hum | 101 | 79.2-79.8 | Rehabilitate Roadway |  |
| 99-00 | Hum | 101 | 79.8-80.0 | Widen Bridge & Upgrade Rail |  |
| 99-00 | Hum | 101 | 87.8-R97.5 | Rehab Roadway - CAPM |  |
| 99-00 | Lak | 20 | 18.0-34.5 | Rehabilitate Roadway |  |
| 99-00 | Lak | 20 | 37.4-38.1 | Rehabilitate Roadway |  |
| 99-00 | Lak | 29 | 9.5-10.0 | Replace Bridge |  |
| 99-00 | Men | 1 | 3.7-38.2 | Reconstruct Roadway |  |
| 99-00 | DN,Hum,Lak,Men |  |  | Changeable Message Signs |  |
| 99-00 | Hum | 101 | 75.7-76.0 | Cont. Left Turn Lane |  |
| 99-00 | Men,Lak | 20 | 43.0, 0.6 | Passing Lanes E/B & W/B |  |
| 99-00 | Men | 101 | 38.2-39.4 | Curve Realignment |  |
| 00-01 | Men | 1 | 90.9-105.6 | Rehab Roadway - CAPM |  |
| 00-01 | Men | 101 | 19.5-R31.0 | Roadway Rehabilitation (Ramps) |  |
| 01-02 | DN | 101 |  | Rail Upgrade and Widening |  |
| 01-02 | Hum | 101 | 56.5-57.2 | Bridge Replacement |  |
| 01-02 | Hum | 299 | R1.5-R1.6 | Rail Upgrade and Widening |  |
| 01-02 | Hum | 299 | 33.2-35.6 | Rail Upgrade and Widening |  |
| 01-02 | Men | 128 | 28.3 | Bridge Replacement |  |
| 01-02 | Men | 128 | 43.4 | Rehabilitate Bridge Foundation |  |
| 01-02 | Men | 162 |  | Rail Upgrade and Widening |  |
| 01-02 | Lak | 20 | 12.2-13.6 | Continuous Lt Turn Lane |  |
| 01-02 | Men | 101 | T43.5-51.3 | 4-Lane Freeway |  |
| Minor STIP |
| 94-95 | Hum | 225 | 8.3 | Rehab RR-Xing | Compl |
| 94-95 | Men | 1 | 61.2-61.3 | Upgrade Inters. | Compl. |
| 94-95 | DN | 101 | 15.3-15.4 | Vert Curve Correction | Compl. |
| 94-95 | Hum | 36 | 14.4 Rt | Replace RSP | Compl. |
| 94-95 | Hum | 36 | 22.3-22.6 | Repair Drainage | Compl. |
| 94-95 | Hum | 96 | 28.1 | Remove Slide | Compl. |
| 94-95 | Hum | 221 | 74.6-76.4 | Place RSP | Compl. |
| Fiscal Year | County | Route | Mile Post | Type of Work | Under Construction |
| Minor STIP |
| 94-95 | Lak, Men | 20, 222 |  | Seismic Retrofit | Compl. |
| 94-95 | Lak | 175 | 1.9 | Reconstruct Embankment | Compl. |
| 94-95 | Lak | 175 | 21.06 | Reconstruct Embankment | Compl |
| 94-95 | Lak | 20 | 18.4-27.3 | Place RSP | Compl. |
| 94-95 | Lak | 281 | 14.55 | Remove Slide | Compl. |
| 94-95 | Men | 1 | 7.2 | Reconstruct Embankment | Compl. |
| 94-95 | Men | 1 | 82.9 | Place RSP | Compl. |
| 94-95 | Men | 1 | 82.9 | Tieback Wall | Compl. |
| 94-95 | Men | 128 | 3.5 Rt | Restore Slope |  |
| 94-95 | Men | 162 | 16.1 | Restore Roadway | Compl. |
| 94-95 | Men | 175 | 3.38 | Reconstruct Embankment | Compl. |
| 95-96 | DN | 199 | 8.6 | Stabilize Roadway | Compl. |
| 95-96 | Hum | 101 | 129.5-129.8 | Erosion Control | Compl. |
| 95-96 | Hum | 255 | 5.9-6.2 | Lt Turn Channel | Compl. |
| 95-96 | Hum | 101 | 0.9-2.7 | 0.15' Blanket of OGAC | Compl. |
| 95-96 | Men | 20 | 8.8-19.6 | Constr Turnouts | Compl. |
| 95-96 | DN | 101 |  | Seismic Retrofit | Compl. |
| 95-96 | DN | 199 | 23.8 | Remove Slide | Compl. |
| 95-96 | DN | 199 | 30.0-30.1 | Rock Buttress | Compl. |
| 95-96 | Hum | 101 | 28.2-33.3 | Place Test Striping | Compl. |
| 95-96 | Hum | 101 |  | Seismic Retrofit | Compl. |
| 95-96 | Hum | 254 | 17.3 | Place RSP | Compl. |
| 95-96 | Men | 1 | 34.2, 38.3 | Reconstruct Embankment | Compl. |
| 95-96 | Men | 1 | 44.0-47.4 | Drainage Repairs | Compl. |
| 95-96 | Men | 1 | 83.3 | Realign Roadway |  |
| 95-96 | Men | 101 | 76.1-76.3 | Restore Embankment | Compl. |
| 95-96 | Men | 253 | 0.8-1.0 | Restore Embankment |  |
| 96-97 | Hum | 101 | 78.4-78.6 | Upgrade Drainage & Signals | Yes |
| 96-97 | Lak | 29 | 34.6-34.8 | Place AC | Compl. |
| 96-97 | DN | 199 | 1.1-3.3 | Place OGAC Surfacing | Compl. |
| 96-97 | Hum | 254 | 0.9-1.1 | Curve Correction | Compl. |
| 96-97 | Lak | 20 |  | Widen & Channel | Compl. |
| 96-97 | Men | 1 | 54.5-R54.7 | Widen & Channelize | Compl. |
| 96-97 | Hum, Sis | 96 | 23.4, 13.9 | Restore Roadway | Compl. |
| 96-97 | Hum | 36 | 13.8 | Restore Embankment | Compl. |
| 96-97 | Hum | 101 | 29.3-29.5 | Restore Roadway | Compl. |
| 96-97 | Hum | 101 | 32.7 | Rock Buttress | Compl. |
| 96-97 | Hum | 101 | R133.62 | Restore Roadway |  |
| 96-97 | Hum | 169 | 15.2-22.2 | Remove Slides | Yes |
| 96-97 | Hum | 200 | 1.9 | Rock Buttress | Compl. |
| 96-97 | Hum | 254 | 4.1-17.1 | Repair Slipouts & Culvert | Compl. |
| 96-97 | Hum | 254 | 12.7 | Restore Embankment |  |
| 96-97 | Hum | 299 | R26.38 | Restore Roadway | Compl. |
| 96-97 | Lak | 20 | 37.0-46.5 | Remove Debris | Compl. |
| 96-97 | Lak | 29 | 21.8 | Stabilize Slide | Compl. |
| 96-97 | Men | 1 | 51.9-82.9 | Seismic Retrofit | Compl. |
| 96-97 | Men | 1 | 60.2 | Seismic Retrofit |  |
| 96-97 | Men | 1 | 75.0 | Seismic Retrofit | Compl. |
| 96-97 | Men | 101 | 36.0 | Restore Embankment | Compl. |
| 96-97 | Men | 101 | 83.8 | Restore Roadway |  |
| 96-97 | Men | 101 | 102.3 | Restore Embankment | Compl. |
| 96-97 | Men | 128 | 4.3-9.7 | Remove Debris | Compl. |
| 96-97 | Men | 162 | 5.7-6.1 | Restore Embankment | Compl. |
| Fiscal Year | County | Route | Mile Post | Type of Work | Under Construction |
| Minor STIP |
| 96-97 | Men | 162 | 6.0-6.1 | Restore Embankment | Yes |
| HQ 97-98 | Hum | 101 | 10.0-14.3 | Subsurface Drains |  |
| HQ 97-98 | Lak | 29 | 36.0-36.4 | Remove Islands |  |
| HQ 97-98 | Men | 101 | R97.8-R98.8 | Subsurface Drains |  |
| HQ 97-98 | Men | 271 | 19.7 | Restore Roadway |  |
| HQ 97-98 | DN,Hum-Var |  |  | Upgrade Appr Rail |  |
| HQ 97-98 | Hum | 101 | 25.6-25.9 | Recrown Roadway |  |
| HQ 97-98 | Hum | 101 | 56.6-57.2 | Median Barrier |  |
| HQ 97-98 | Hum | 101 | 76.0-76.1 | Retaining Wall |  |
| HQ 97-98 | Hum | 101 | R89.7-R90.2 | Median Barrier |  |
| HQ 97-98 | Men | 1 | 60.5-60.8 | Install Signals |  |
| HQ 97-98 | Hum | 36 | 13.8 | Place RSP |  |
| HQ 97-98 | Hum | 96 | 25.3-R41.0 | Reconstruct Embank. |  |
| HQ 97-98 | Hum | 299 | R2.3-20.0 | Restore Roadway |  |
| HQ 97-98 | Lak | 20 |  | Restore Roadway |  |
| HQ 97-98 | Lak | 175 | 21.07 | Restore Roadway |  |
| HQ 97-98 | Lak | 20 |  | Restore Roadway |  |
| HQ 97-98 | Men | 101 | R21.9 | Weigh-In-Motion |  |
| HQ 97-98 | Son | 101 | R49.7-50.2 | Message Signs |  |
| 97-98 | Hum | 96 | 33.9 | Replace Culverts | Compl. |
| 97-98 | Hum | 101 | R11.3-14.3 | Subsurface Drains |  |
| 97-98 | Lak | 29 | 36.0-36.4 | Remove Islands | Yes |
| 97-98 | Men | 101 | 18.5 | Replace Drainage | Compl. |
| 97-98 | Men | 101 | R97.8-R98.8 | Subsurface Drains | Yes |
| 97-98 | Men | 271 | 19.7 | Restore Roadway | Yes |
| 97-98 | DN,Hum-Var |  |  | Upgrade Appr Rail |  |
| 97-98 | Hum | 101 | 56.6-57.2 | Median Barrier |  |
| 97-98 | Hum | 101 | R89.7-R90.2 | Median Barrier | Yes |
| 97-98 | Men | 1 | 60.5-60.8 | Install Signals |  |
| 97-98 | Men | 20 | 12.6-26.8 | Place OGAC | Yes |
| 97-98 | DN | 101 | 12.1-12.5 | Place RSP | Yes |
| 97-98 | DN | 101 | 15.2-22.8 | Maintain Roadway | Yes |
| 97-98 | DN | 101 | 18.8-21.9 | Restore Roadway |  |
| 97-98 | DN | 199 | 5.9-6.0 | Remove Slide | Yes |
| 97-98 | DN | 199 | 23.8 | Remove Slide | Compl. |
| 97-98 | DN | 199 | 23.8 | Remove Slide | Yes |
| 97-98 | Hum | 36 | 21.4-21.8 | Slide & Slipout | Yes |
| 97-98 | Hum | 96 | 3.0-3.1 | Remove Slide | Yes |
| 97-98 | Hum | 101 | R89.8 | Place RSP |  |
| 97-98 | Hum | 200 | 2.1-2.2 | Repair Drainage | Yes |
| 97-98 | Hum | 299 | R2.3-20.0 | Restore Roadway | Compl. |
| 97-98 | Lak | 20 | 26.9-27.0 | Restore Slope | Yes |
| 97-98 | Lak | 20 |  | Restore Roadway | Compl. |
| 97-98 | Lak | 175 | 21.07 | Restore Roadway |  |
| 97-98 | Men | 1 |  | Restore Roadway | Compl. |
| 97-98 | Men | 1 | 4.7-5.0 | Maintain Roadway | Yes |
| 97-98 | Men | 1 | 9.9, 78.7 | Restore Roadway | Yes |
| 97-98 | Men | 1 | 38.2 | Restore Roadway | Yes |
| 97-98 | Men | 1 | 40.8, 41.0 | Place Rock Buttresses | Yes |
| 97-98 | Men | 1 | 41.0-41.1 | Restore Roadway | Yes |
| 97-98 | Men | 20 | 8.8 | Install Bailey Bridge | Yes |
| 97-98 | Men | 101 | R86.0-R86.2 | Remove Slide | Yes |
| 97-98 | Men | 128 | 34.0-34.1 | Restore Roadway | Compl. |
| Fiscal Year | County | Route | Mile Post | Type of Work | Under Construction |
| Minor STIP |
| 97-98 | Son | 101 | R49.7-50.2 | Message Signs | Yes |
| 98-99 | Hum-L-5703 (Brdgvle) |  |  | Cnstr Sand House |  |
| 98-99 | Hum-L-5712 Garberville |  |  | Mech. Shop |  |
| 98-99 | Hum | 101 | R5.6-R5.9 | Remove A.C. Berm |  |
| 98-99 | Hum | 101 | 112.2-112.3 | Restore Roadway |  |
| 98-99 | Hum | 169 | 22.0 | Restore Roadway |  |
| 98-99 | Hum | 255 | 8.5-8.6 | Modifiy Signals |  |
| 98-99 | Hum | 299 | R5.9-R7.2 | Rehab Rdwy - CAPM |  |
| 98-99 | Lak | 175 | 27.2-27.5 | Install Drainage |  |
| 98-99 | Men | 1 | 40.9 | Repair Slipout |  |
| 98-99 | Men | 101 | 18.5 | Improve Drainage |  |
| 98-99 | Men | 101 | R89.2 | Rehab Culvert - Invert |  |
| 98-99 | Hum | 101 | 25.6-25.9 | Recrown Roadway |  |
| 98-99 | Hum | 200 | R0.1-R0.5 | Widen Shoulder |  |
| 98-99 | Hum | 299 | 30.2-30.6 | Super Improvement |  |
| 98-99 | Lak | 20 |  | Mod Rt Turn Channel. |  |
| 98-99 | Lak | 175 | 6.8-7.0 | Curve Correction |  |
| 98-99 | Hum | 36 | 21.4-21.8 | Realign Highway |  |
| 98-99 | Hum | 36 | 22.2-23.9 | Restore Roadway |  |
| 98-99 | Hum | 101 | 0.3-0.4 | Restore Roadway |  |
| 98-99 | Hum | 254 | 4.4-4.6 | Stabilize Roadway |  |
| 98-99 | Hum | 299 | R21.5-R21.7 | Restore Roadway |  |
| 98-99 | Hum | 299 | R25.0-R25.1 | Restore Roadway |  |
| 98-99 | Men-L-5710 |  |  | Install Wash Rack |  |
| 98-99 | Men | 1 | 75.0 | Realign Highway |  |
| 98-99 | Men | 1 | 85.3-85.9 | Restore Roadway |  |
| 98-99 | Men | 1 | 95.1-99.4 | Restore Roadway |  |
| 98-99 | Men | 1 | 97.9 | Restore Roadway |  |
| 98-99 | Men | 20 | 8.8 | Restore Roadway |  |
| 98-99 | Men | 20 | 25.9-26.0 | Restore Roadway |  |
| 98-99 | Men | 101 | R21.9 | Weigh-In-Motion |  |
| 98-99 | Men | 101 | 76.4-76.5 | Restore Roadway |  |
| 98-99 | Men | 253 | 2.0-2.2 | Restore Roadway |  |
| 99-00 | DN | 101 | 9.4-9.7 | Grade Raise |  |
| 99-00 | Hum-L-5727 Willow Cr. |  |  | Mechanic Fac. |  |
| 99-00 | Hum | 101 | 113.3-113.4 | Stabilize Slope |  |
| 99-00 | Hum | 211 | 73.9-74.0 | Replace Driveways |  |
| 99-00 | Hum | 299 | R29.1 | Constr Sand House |  |
| 99-00 | Men | 1 | 90.9-105.3 | Rehab Culverts |  |
| 99-00 | Men | 101 | 41.1 | Constr Truck Scales |  |
| 99-00 | Men | 101 | 100.1 | Remove Rock |  |
| 99-00 | DN | 101 | 22.3-23.6 | Widen Shoulders |  |
| 99-00 | DN | 199 | 12.8-12.9 | Widen Roadway |  |
| 99-00 | Men | 128 | 43.7-44.0 | Vert Curve Correction |  |
| 99-00 | DN | 199 | 26.7-26.9 | Realign Roadway |  |
| 99-00 | DN | 199 | 6.41-9.81 | Remove Rock OC's |  |
| 99-00 | DN | 199 | 22.38-23.90 | Remove Rock OC's |  |
| 99-00 | DN | 199 | 26.12-26.92 | Remove Rock OC's |  |
| 00-01 | DN-5707 Crescent City |  |  | Rehab Shed |  |
| 00-01 | DN | 101 | 23.9-24.6 | Grade Raise |  |
| 00-01 | DN | 197 | 5.8-6.0 | Repair Embankment |  |
| 00-01 | DN | 199 | 7.5-8.8 | Reconstruct Roadway |  |
| Fiscal Year | County | Route | Mile Post | Type of Work | Under Construction |
| Minor STIP |
| 00-01 | Hum-L-5708 |  |  | Warehouse Expand |  |
| 00-01 | Hum-L-5512 |  |  | Remodel Lab |  |
| 00-01 | Hum | 36 | 5.7-7.6 | Widen Shoulders |  |
| 00-01 | Hum | 200 | 1.9-2.4 | Curve Correction |  |
| 00-01 | Men | 128 | 14.3-15.3 | E.B. Passing Lane |  |
| 00-01 | Men | 128 | 28.3-29.3 | Left Turn Lane |  |
| 01-02 | DN-5707 Crescent City |  |  | Rehab Shed |  |
| 01-02 | Hum-L-5711 |  |  | Modify Facilities |  |
| 01-02 | Lak-L-5706 |  |  | Mechanic Fac. |  |
| 01-02 | Men-L-5718 |  |  | Rehab Barn/Fuel |  |

Appendix C – Oregon STIP/SHOPP

| ODOT Region | County | Work Type | OR Hwy # | Route | Beg. MP | End MP | Const. Year | Work Description |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 3 | Coos | BRIDGE | 9 | 101 | 244.8 | 0 | 2001 | Replace structure. |
| 3 | Coos | PRESRV | 9 | 101 | 273.8 | 273.9 | 1998 | Reconstruct the channel and replace access bridge. |
| 3 | Coos | SAFETY | 240 |  | 1.83 | 1.87 | 2001 | Signal replacement. |
| 3 | Coos | SAFETY | 35 | 42 | 24 | 24.01 | 2001 | Signal replacement. |
| 3 | Coos | PRESRV | 35 | 42 | 30.3 | 36.35 | 2001 | Overlay roadway. |
| 3 | Coos | PRESRV | 35 | 42 | 4 | 7.8 | 2001 | Overlay roadway. |
| 3 | Coos | BRIDGE | 9 | 101 | 234 | 234.9 | 1998 | Remove all paint in sub structure; spot paint super structure, repair electrical system. |
| 3 | Coos | BRIDGE |  |  | 0.27 | 0.41 | 1998 | Replace structure. |
| 3 | Coos | SAFETY | 9 | 101 | 240 | 244.3 | 1998 | Construct left turn lanes, deceleration & acceleration lanes. |
| 3 | Coos | BRIDGE | 9 | 101 | 232.8 | 233.5 | 1999 | Replace structure, construct climbing lane. |
| 3 | Coos | MISCEL | 9 | 101 | 220 | 220.1 | 1999 | Repair slide. |
| 3 | Coos | SAFETY | 35 | 42 | 38.25 | 46.25 | 1999 | Install guardrail on this section of highway. |
| 3 | Coos | BRIDGE |  |  | 3.3 | 3.31 | 2000 | Replace structure. |
| 3 | Coos | BRIDGE |  |  | 0.21 | 0.22 | 2000 | Replace structure. |
| 3 | Coos | BRIDGE | 241 |  | 0.5 | 0 | 2000 | Replace grid deck and wood approach spans; realign easterly approach span. |
| 4 | Crook | BRIDGE | 41 | 26/126 | 28.11 | 28.25 | 1999 | Replace structure. |
| 4 | Crook | BRIDGE |  |  | 0 | 0 | 1999 | Replace structure. |
| 4 | Crook | SAFETY | 41 | 26/126 | 19.7 | 19.8 | 2000 | Traffic signal. |
| 4 | Crook | ENHANC | 41 | 26/126 | 0 | 0 | 1998 | Acquire, relocate & restore Redmond Depot building to Prineville junction. |
| 3 | Curry | MISCEL | 9 | 101 | 312 | 312.3 | 1999 | Repair slide. |
| 3 | Curry | MISCEL | 9 | 101 | 349.1 | 349.6 | 2001 | Repair slide. |
| 3 | Curry | SAFETY | 9 | 101 | 322 | 322.2 | 2000 | Construct a left turn refuge. |
| 3 | Curry | PRESRV |  |  | 0 | 3.3 | 2000 | Upgrade roadway. |
| 3 | Curry | MISCEL | 9 | 101 | 329 | 0 | 1998 |  |
| 3 | Curry | MISCEL | 9 | 101 | 311.2 | 311.7 | 2001 | Repair slide. |
| 3 | Curry | PRESRV | 9 | 101 | 330 | 334.8 | 2001 | Overlay roadway. |
| 3 | Curry | PRESRV | 9 | 101 | 315.4 | 317 | 1999 | Overlay roadway. |
| 3 | Curry | PRESRV | 9 | 101 | 285.3 | 289.6 | 2000 | Overlay roadway. |
| 3 | Curry | BRIDGE | 9 | 101 | 315.5 | 0 | 2000 | Replace structure. |
| 3 | Curry | PRESRV | 9 | 101 | 337.6 | 339.9 | 1998 | Construct a two-inch overlay. |
| 3 | Curry | SAFETY | 9 | 101 | 310.2 | 310.3 | 2001 | Repair slide. |
| 3 | Curry | BRIDGE | 9 | 101 | 347.8 | 0 | 2001 | Paint steel on the structure. |
| 3 | Curry | PRESRV | 9 | 101 | 295.1 | 299.8 | 2001 | Overlay roadway. |
| 4 | Deschutes | PRESRV | 15 | 126 | 0 | 0 | 1998 | Millout/inlay, preservation overlay. Work on Santiam & McKenzie Hwys. |
| 4 | Deschutes | PRESRV | 7 | 20 | 12.3 | 20.97 | 2001 | Millout/inlay travel lanes preservation overlay. |
| 4 | Deschutes | MODERN | 4 | 97 | 129.9 | 130.5 | 1998 | Construct over-crossing & intersection connections. |
| 4 | Deschutes | SAFETY | 4 | 97 | 122 | 122 | 1998 | Install traffic signal & widen Sister's Ave for left turn lane & 2 bike lanes. |
| 4 | Deschutes | MISCEL |  |  | 0 | 0 | 1999 | Promote/manage carpool program & implement transportation demand management initiatives. |
| ODOT Region | County | Work Type | OR Hwy # | Route | Beg. MP | End MP | Const. Year | Work Description |
| 4 | Deschutes | MODERN | 4 | 97 | 134.8 | 141.8 | 1999 | Construct new roadway. |
| 4 | Deschutes | MODERN | 4 | 97 | 129.9 | 130.5 | 1999 | Connext US 97 x'ing to Deschutes Market Rd. |
| 4 | Deschutes | MISCEL | 4 | 97 | 143.5 | 144.9 | 2000 | Relocate weigh scale. |
| 4 | Deschutes | SAFETY | 15 | 126 | 109.6 | 109.7 | 2000 | Left turn refuge. |
| 4 | Deschutes | MISCEL |  |  | 0 | 0 | 2001 | Promote/manage carpool program & implement transportation demand management initiatives. |
| 4 | Deschutes | MODERN | 4 | 97 | 133.5 | 134.9 | 2001 | Raised median barrier & partial frontage road. |
| 4 | Deschutes | SAFETY | 17 | 20 | 93 | 93.12 | 2001 | Intersection revision. |
| 4 | Deschutes | SAFETY | 4 | 97 | 143.5 | 149.5 | 2001 | Median barrier. |
| 4 | Deschutes | PRESRV | 4 | 97 | 135.4 | 142.2 | 2001 | Millout/inlay/overlay preservation. |
| 4 | Deschutes | PRESRV | 4 | 97 | 120.4 | 122 | 2001 | Millout/inlay, upgrade/ADA intersections & sidewalks. |
| 4 | Deschutes | MISCEL |  |  | 0 | 0 | 2000 | Promote/manage carpool program & implement transportation demand management initiatives. |
| 4 | Deschutes | MISCEL |  |  | 0 | 0 | 1998 | Promote/manage carpool program & implement transportation demand management initiatives. |
| 3 | Douglas | SAFETY | 1 | I-5 | 88.12 | 129.2 | 1998 | Install protective screening. |
| 3 | Douglas | MODERN |  |  | 21.7 | 26.2 | 2000 | Reconstruction, realignment. |
| 3 | Douglas | MODERN |  |  | 11 | 13.9 | 1999 | Reconstruct 2.8 miles. |
| 3 | Douglas | SAFETY |  |  | 0 | 0 | 1999 | Replacement of guard rail end connections to bridges. |
| 3 | Douglas | PRESRV | 45 | 38 | 0.01 | 6.6 | 1999 | Inlay/overlay construction. Widen WB connection through railroad x'ing. Improve vertical alignment. |
| 3 | Douglas | PRESRV | 231 | 138 | 14 | 17 | 1999 | Overlay roadway. |
| 3 | Douglas | PRESRV | 73 | 138 | 16 | 18 | 1999 | Overlay roadway. |
| 3 | Douglas | PRESRV | 45 | 38 | 49.52 | 52.3 | 1999 | Construct a two-inch overlay. |
| 3 | Douglas | MODERN | 1 | I-5 | 124 | 125 | 2001 | Add a third lane Northbound. |
| 3 | Douglas | SAFETY | 35 | 42 | 76.14 | 76.19 | 1998 | Modify the existing signal and construct a new connection w/Hwy. 35 and Grant Smith Rd. |
| 3 | Douglas | PRESRV | 35 | 42 | 61.8 | 67.6 | 1998 | Construct a two inch wearing surface. |
| 3 | Douglas | PRESRV | 1 | I-5 | 108.4 | 112.5 | 2001 | Inlay/overlay. |
| 3 | Douglas | SAFETY |  |  | 0 | 0 | 1998 | Regionwide permanent striping. |
| 3 | Douglas | PRESRV | 1 | I-5 | 117.7 | 122.3 | 2000 | Inlay/overlay. |
| 3 | Douglas | PRESRV | 73 | 138 | 77.5 | 83.5 | 2000 | Overlay roadway. |
| 3 | Douglas | PRESRV | 45 | 38 | 10 | 16 | 2000 | Overlay roadway. |
| 3 | Douglas | PRESRV | 45 | 38 | 51 | 54 | 2000 | Overlay roadway. |
| 3 | Douglas | SAFETY | 1 | I-5 | 109.2 | 109.6 | 2000 | Repair rockfall. |
| 3 | Douglas | SAFETY | 234 | 99 | 17.41 | 17.64 | 2000 | Signal replacement. |
| 3 | Douglas | BRIDGE | 45 | 38 | 19.05 | 0 | 2001 | Widen or replace structure. |
| 3 | Douglas | PRESRV | 9 | 101 | 198.6 | 207.5 | 1998 | Construct a two-inch overlay. |
| 3 | Douglas | MODERN | 45 | 38 | 36.44 | 0 | 2001 | Improve intersection and widen Bridge #01614. |
| 3 | Douglas | BRIDGE |  |  | 1.7 | 1.71 | 2000 | Replace structure. |
| 3 | Douglas | PRESRV | 35 | 42 | 71.8 | 76 | 2001 | Overlay roadway. |
| 3 | Douglas | PRESRV | 231 | 138 | 1 | 4 | 2001 | Overlay roadway. |
| 3 | Douglas | SAFETY | 1 | I-5 | 131.6 | 131.7 | 2001 | Repair rockfall. |
| 3 | Douglas | SAFETY | 35 | 42 | 48.82 | 49 | 2001 | Repair rockfall. |
| 3 | Douglas | MODERN | 1 | I-5 | 136.2 | 0 | 2001 | Construct signals & ramps; construct new SB off-ramp. |
| 3 | Douglas | PRESRV | I-5 | I-5 | 98.92 | 108.4 | 1998 | Inlay/overlay; raise structures and widen Riddle (tri-cities) undercrossing. (cmb.w/09204). |
| ODOT Region | County | Work Type | OR Hwy # | Route | Beg. MP | End MP | Const. Year | Work Description |
| 3 | Douglas | BRIDGE | 9 | 101 | 210.2 | 211 | 1998 | Replace Smith River Bridge & Long Bell Bridge on new alignment. |
| 3 | Douglas | PRESRV | 1 | I-5 | 140.6 | 147.7 | 1998 | Construct a overlay with an inlay in the slow lane replace bridge rails; rubbilize PCC. |
| 3 | Douglas | BRIDGE | 45 | 38 | 22.6 | 28.31 | 1998 | Replace Weatherly Creek Bridge on new alignment; widen Paradise Creek Bridge. |
| 5 | Harney | MODERN |  |  | 20 | 24.3 | 2001 | 4.3 mile reconstruct. |
| 5 | Harney | PRESRV | 48 | 395 | 40.38 | 67.78 | 1999 | 2 inch grind out, 2 inch EAC inlay, chip seal, and guard-rail installation. |
| 5 | Harney | BRIDGE |  |  | 0.68 | 0.69 | 2001 | Replace structure and realign county road. |
| 5 | Harney | PRESRV | 7 | 20 | 171.1 | 183 | 2000 | Grind, emulsified ashaltic concrete (EAC) paving, chip seal and bridge work. |
| 5 | Harney | PRESRV | 440 | 205 | 49.6 | 71.3 | 2000 | Leveling, overlay, and guardrail. |
| 5 | Harney | BRIDGE |  |  | 0.49 | 0.54 | 1999 | Replace structure. |
| 5 | Harney | PRESRV | 7 | 20 | 133.7 | 134.4 | 1998 | Raise roadway, reconstruct intersection, replace structure. |
| 3 | Jackson | BRIDGE |  |  | 0.01 | 0.04 | 2000 | Replace existing bridge. |
| 3 | Jackson | PLANNG |  |  | 0 | 0 |  | TDM rideshare. |
| 3 | Jackson | OPERTN |  |  | 0 | 0 |  | Operations support. |
| 3 | Jackson | TRANST |  |  | 0 | 0 |  | Operations support. |
| 3 | Jackson | TRANST |  |  | 0 | 0 |  | Rideshare. |
| 3 | Jackson | OPERTN |  |  | 0 | 0 |  | Operation support. |
| 3 | Jackson | OPERTN |  |  | 0 | 0 |  |  |
| 3 | Jackson | MODERN | 22 | 62 | 7.4 | 10.2 | 1998 | Widen highway to 3 & 4 lanes and new connection to Alta Vista Road. |
| 3 | Jackson | MODERN | 272 | 238 | 37.6 | 38.8 | 2000 | Build new alignment for Hwy. 238 from junction of Hwy 62/OR 99 to intersection of Sage Rd./Rossanley. |
| 3 | Jackson | MISCEL |  |  | 0 | 0 |  | Planning assistance. |
| 3 | Jackson | SAFETY |  |  | 0 | 0 | 1999 | Install traffic signal. |
| 3 | Jackson | SAFETY | 63 | 99 | 19.03 | 19.4 | 2001 | Signal replacement. |
| 3 | Jackson | MODERN |  |  | 0 | 0 | 1999 | Construct a new three lane roadway. |
| 3 | Jackson | MISCEL |  |  | 0 | 0 | 1998 | CMAQ reserve fund; projects to be selected. |
| 3 | Jackson | TRANST |  |  | 0 | 0 | 1999 | Adv public transportation system. |
| 3 | Jackson | TRANST |  |  | 0 | 0 | 2001 | Vehicle maintenance support. |
| 3 | Jackson | MODERN |  |  | 0 | 0 | 2001 | Construct new three lane roadway. |
| 3 | Jackson | MODERN |  |  | 0 | 0 | 2001 | Realign and widen to five lanes. |
| 3 | Jackson | MODERN |  |  | 0 | 0 | 2001 | Construct new three or five lane roadway. |
| 3 | Jackson | MODERN |  |  | 0 | 0 | 2001 | Widen to three lanes. |
| 3 | Jackson | MODERN |  |  | 0 | 0 | 2001 | Construct new three lane roadway. |
| 3 | Jackson | TRANST |  |  | 0 | 0 | 2000 | Vehicle maintenance support. |
| 3 | Jackson | OPERTN |  |  | 0 | 0 |  | Operation support. |
| 3 | Jackson | TRANST |  |  | 0 | 0 | 1999 | Vehicle maintenance support. |
| 3 | Jackson | OPERTN |  |  | 0 | 0 |  | Operations support. |
| 3 | Jackson | TRANST |  |  | 0 | 0 | 1998 | Bus Purchases. |
| 3 | Jackson | PLANNG |  |  | 0 | 0 |  | TDM rideshare. |
| 3 | Jackson | MODERN |  |  | 0 | 0 | 1999 | Widen to three lanes with curb gutter, bike lanes, and sidewalk. |
| 3 | Jackson | OPERTN |  |  | 0 | 0 |  | Operations support. |
| 3 | Jackson | SAFETY |  |  | 0.01 | 1.51 | 2000 | Safety improvements. |
| ODOT Region | County | Work Type | OR Hwy # | Route | Beg. MP | End MP | Const. Year | Work Description |
| 3 | Jackson | SAFETY | 22 | 62 | 0.01 | 7.4 | 2000 | Safety work. |
| 3 | Jackson | PLANNG |  |  | 0 | 0 |  | TDM rideshare. |
| 3 | Jackson | OPERTN |  |  | 0 | 0 |  | Operations support. |
| 3 | Jackson | MODERN |  |  | 0 | 0 | 2000 | Widen to three lanes with curb gutter, bike lanes, and sidewalk. |
| 3 | Jackson | PRESRV | 22 | 62 | 62 | 65 | 2001 | Overlay roadway. |
| 3 | Jackson | PRESRV | 1 | I-5 | 43.13 | 49.05 | 2000 | 6" overlay. |
| 3 | Jackson | MODERN |  |  | 0 | 0 | 1998 | Widen From 2 To 5 Lanes, Safety Improvements. |
| 3 | Jackson | MODERN |  |  | 0 | 0 | 1998 | Widen to three lanes with bike lanes. |
| 3 | Jackson | BRIDGE | 293 |  | 12.97 | 0 | 1998 | Replace structure. |
| 3 | Jackson | SAFETY | 1 | I-5 | 0.01 | 12 | 1998 | Drainage & erosion correction and Durastripe. |
| 3 | Jackson | BIKPED |  |  | 0 | 0 | 1998 | Construct bike path. |
| 3 | Jackson | MODERN |  |  | 0 | 0 | 1998 | Widen with shoulder bike ways. |
| 3 | Jackson | PRESRV | 1 | I-5 | 14 | 27 | 2000 | Overlay ramps. |
| 3 | Jackson | PRESRV | 271 | 99 | 0 | 3 | 1999 | Overlay roadway. |
| 3 | Jackson | MODERN |  |  | 0 | 0 | 1998 | Construct 5 lane section with bike lanes. |
| 3 | Jackson | PRESRV | 272 | 238 | 29.5 | 32.41 | 1999 | Overlay roadway. |
| 3 | Jackson | MODERN |  |  | 0 | 0 | 1998 | Widen to rural two lane with shoulder bikeways. |
| 3 | Jackson | PRESRV | 63 | 99 | 17.02 | 19.55 | 1999 | Overlay roadway. |
| 3 | Jackson | MISCEL |  |  | 0 | 0 | 1998 | Portals, signs, rec. and scenic @ various locations on Rogue and Umpqua. |
| 3 | Jackson | PRESRV | 272 | 238 | 13 | 16 | 2001 | Overlay roadway. |
| 3 | Jackson | MODERN |  |  | 0 | 0 | 1998 | Widen to three lanes with bike lanes. |
| 3 | Jackson | MODERN |  |  | 0 | 0 | 1998 | Widen to rural two lane with shoulder bikeways. |
| 3 | Jackson | TRANST |  |  | 0 | 0 | 1998 | Vehicle maintenance support. |
| 3 | Jackson | PRESRV | 25 | 199 | 28 | 36 | 1998 | Overlay roadway. |
| 3 | Jackson | TRANST |  |  | 0 | 0 | 1998 | Seal fuel tanks. |
| 3 | Jackson | MODERN |  |  | 0 | 0 | 1998 | Construct new two lane roadway with bike lanes. |
| 3 | Jackson | BRIDGE | 271 | 99 | 10 | 10 | 1998 | Deck overlay. |
| 3 | Jackson | BIKPED |  |  | 0 | 0 | 1998 |  |
| 3 | Jackson | PRESRV | 21 | 66 | 9 | 22 | 2000 | Overlay roadway. |
| 3 | Jackson | BRIDGE | 1 | I-5 | 13.2 | 17.2 | 2001 | Structural overlay. |
| 3 | Jackson | BIKPED |  |  | 0 | 0 | 1998 | Obtain adequate row and construct sidewalks along Crater Lake Avenue to provide continuous walkway for peds. |
| 3 | Jackson | SAFETY | 1 | I-5 | 0 | 0 | 2000 | Install protective screening. |
| 3 | Jackson | PRESRV |  |  | 0 | 0 | 1998 | Pave .25 miles of dirt roads within city limits to reduce airborne particulate. Add sidewalks, bike lanes. |
| 3 | Jackson | MODERN |  |  | 0 | 0 | 1998 | Realign and construct three lanes with bike lanes. |
| 3 | Jackson | MODERN |  |  | 0 | 0 | 1998 | Widen to two to three lanes with bike lanes & sidewalks. |
| 3 | Jackson | MODERN |  |  | 0 | 0 | 1998 | Widen to two to three lanes with bike lanes. |
| 3 | Josephine | PRESRV | 25 | 199 | 0.35 | 6.92 | 1998 | Widen shoulders & overlay entire section and traffic signal at Dowell Road. |
| 3 | Josephine | SAFETY | 25 | 199 | 2.04 | 2.06 | 1998 | Install a 5 phase fully actuated traffic signal. |
| 3 | Josephine | SAFETY |  |  | 0 | 0 | 1999 | 0.6 mile intersection reconstruction. |
| 3 | Josephine | BRIDGE |  |  | 0.38 | 0.45 | 1999 | Rehabilitation of the structure. |
| 3 | Josephine | PRESRV | 1 | I-5 | 49.05 | 58.2 | 1999 | Structure work. |
| ODOT Region | County | Work Type | OR Hwy # | Route | Beg. MP | End MP | Const. Year | Work Description |
| 3 | Josephine | BRIDGE |  |  | 0.02 | 0.04 | 1998 | Replace structure. |
| 3 | Josephine | PRESRV | 60 | 99 | 0.01 | 8.9 | 1999 | Overlay roadway. |
| 3 | Josephine | BRIDGE |  |  | 0.07 | 0.08 | 1998 | Replace structure. |
| 3 | Josephine | BRIDGE | 260 |  | 12.7 | 13 | 2000 | Replace structure. |
| 3 | Josephine | BRIDGE |  |  | 2.4 | 2.42 | 1998 | Replace structure. |
| 3 | Josephine | PRESRV | 272 | 238 | 5.87 | 13.78 | 2000 | Overlay roadway. |
| 3 | Josephine | PRESRV | 25 | 199 | 0.01 | 1.5 | 2000 | Overlay roadway. |
| 3 | Josephine | BRIDGE | 272 | 238 | 6.06 | 6.22 | 2001 | Replace approach spans. |
| 3 | Josephine | PRESRV | 38 | 46 | 0 | 0 | 1998 | Variable rehabilitation. |
| 3 | Josephine | PRESRV | 25 | 199 | 16 | 24 | 2001 | Overlay roadway. |
| 3 | Josephine | SAFETY | 25 | 199 | 1 | 1.2 | 1999 | Construct new signal. |
| 3 | Josephine | MODERN | 25 | 199 | 0.01 | 2.7 | 1999 | Reconstruct 6th & 7th Streets, replace traffic signals, reconstruct curb radii. |
| 4 | Klamath | BRIDGE |  |  | 0.19 | 0.21 | 2000 | Replace structure. |
| 4 | Klamath | PRESRV | 4 | 97 | 185.6 | 195.6 | 2000 | Mill out/inlay travel lanes; overlay entire surface; widen shoulders. |
| 4 | Klamath | BRIDGE |  |  | 0 | 0 | 2001 | Replace structure. |
| 4 | Klamath | PRESRV | 4 | 97 | 227 | 237 | 2000 | Millout/inlay travel lanes preservation overlay. |
| 4 | Klamath | BRIDGE | 50 | 39 | 4.97 | 5.1 | 1998 | Replace bridge deck & geothermal de-icing system. |
| 4 | Klamath | MISCEL |  |  | 0 | 0 | 2000 | Slide correction, pavement reconstruction. |
| 4 | Klamath | MODERN | 422 |  | 0.16 | 5.34 | 2000 | 5.18 mile reconstruct. |
| 4 | Klamath | PRESRV | 4 | 97 | 280.3 | 291.7 | 1998 | Overlay existing roadway. |
| 4 | Klamath | MISCEL |  |  | 0 | 0 | 1998 | CMAQ projects for Klamath Falls. |
| 4 | Klamath | PRESRV | 20 | 140-B | 54.11 | 63.4 | 1998 | Overlay existing roadway; with some widening & realigning. |
| 4 | Klamath | PRESRV |  |  | 0 | 0 | 2000 | 6.1 miles resurfacing. |
| 4 | Klamath | PRESRV | 50 | 39 | 16.25 | 27.1 | 2001 | Preservation overlay. |
| 4 | Klamath | PRESRV | 21 | 66 | 43 | 50 | 2001 | Digout base failures; preservation overlay. |
| 4 | Klamath | PRESRV | 18 | 58 | 75 | 86.25 | 1998 | Overlay roadway; install guardrail; slope work. |
| 4 | Klamath | SAFETY | 424 | 140 | 1.36 | 1.76 | 1999 | Construct median divider. |
| 4 | Klamath | SAFETY | 4 | 97 | 271.2 | 271.9 | 2001 | Acceleration lane; guardrail. |
| 4 | Lake | BRIDGE | 19 | 31 | 109.3 | 109.4 | 2000 | Replace bridge. |
| 4 | Lake | PRESRV | 19 | 31 | 144 | 152.7 | 2000 | Preservation overlay. |
| 4 | Lake | BRIDGE | 20 | 140-B | 93.92 | 93.92 | 2000 | Replace bridges. |
| 4 | Lake | BRIDGE | 19 | 31 | 46.75 | 46.75 | 2001 | Replace bridge. |
| 4 | Lake | SAFETY | 19 | 31 | 27.1 | 28.3 | 1998 | Install guardrail some earth work will be required to provide wide area for flares. |
| 4 | Lake | MODERN | 431 | 140 | 0 | 8.6 | 1998 | Widen roadway and correct horizontal curves. |
| 4 | Lake | PRESRV | 20 | 140-B | 92.2 | 95 | 2001 | Millout/inlay travel lanes preservation overlay. |
| 4 | Lake | PRESRV | 19 | 31 | 142.6 | 144.1 | 2001 | Millout/inlay crown preservation overlay upgrade/ADA sidewalks. |
| 4 | Lake | PRESRV | 19 | 31 | 86 | 95 | 2001 | Preservation overlay, guardrail. |
| 4 | Lake | PRESRV | 19 | 31 | 95 | 100 | 2001 | Preservation overlay & shoulder widening. |
| 4 | Lake | MISCEL |  |  | 0 | 0 | 1998 | CMAQ projecs for City of Lakeview. |
| 2 | Lane | BRIDGE | 9 | 101 | 191 | 191 | 2001 | Rehab electrical. |
| 2 | Lane | TRANST |  |  | 0 | 0 | 1999 | State Participation = $8,000.0 |
| 2 | Lane | TRANST |  |  | 0 | 0 | 1998 | Rideshare |
| 2 | Lane | TRANST | 69 |  | 12.7 | 12.8 | 1998 |  |
| ODOT Region | County | Work Type | OR Hwy # | Route | Beg. MP | End MP | Const. Year | Work Description |
| 2 | Lane | TRANST |  |  | 0 | 0 | 1999 |  |
| 2 | Lane | TRANST |  |  | 0 | 0 | 2001 |  |
| 2 | Lane | BRIDGE | 18 | 58 | 56 | 56.03 | 2000 | Tunnel and rail improvements at MP 53.23, 56.29, & 56.32. |
| 2 | Lane | BRIDGE | 9 | 101 | 168.4 | 0 | 2000 | Rehab & install cathodic protection. |
| 2 | Lane | MISCEL |  |  | 0 | 0 | 2000 |  |
| 2 | Lane | MODERN | 69 |  | 3.1 | 6.3 | 2001 | Construct an over-crossing at Royal Avenue. |
| 2 | Lane | TRANST |  |  | 0 | 0 | 1998 |  |
| 2 | Lane | SAFETY | 200 |  | 18.07 | 18.7 | 2001 | Construct continuous center turn lane. |
| 2 | Lane | TRANST |  |  | 0 | 0 | 1999 |  |
| 2 | Lane | TRANST |  |  | 0 | 0 | 1999 |  |
| 2 | Lane | TRANST |  |  | 0 | 0 | 1999 |  |
| 2 | Lane | TRANST |  |  | 0 | 0 | 1999 |  |
| 2 | Lane | TRANST |  |  | 0 | 0 | 1998 |  |
| 2 | Lane | TRANST |  |  | 0 | 0 | 1998 |  |
| 2 | Lane | TRANST |  |  | 0 | 0 | 1998 | Cost = $1.25M S5309, $75K TGM, $170 STP and $781 SIB Funds. |
| 2 | Lane | SAFETY | 69 |  | 12.98 | 12.99 | 1998 | Safety improvements. |
| 2 | Lane | MODERN |  |  | 0 | 0 | 2001 | Interchange reconstruction. |
| 2 | Lane | MODERN | 62 | 126 | 55.6 | 57.25 | 1998 | 4-lane new construction. |
| 2 | Lane | PRESRV |  |  | 0 | 0 | 2000 |  |
| 2 | Lane | BRIDGE | 1 | I-5 | 192.8 | 192.8 | 2000 | Seismic retro bridge #08329. |
| 2 | Lane | BIKPED |  |  | 0 | 0 | 2000 | New bicycle/pedestrian path. |
| 2 | Lane | SAFETY |  |  | 0 | 0 | 1999 | Funds will go to McKenzie Hwy-Jasper Rd. (42nd) job if Jasper exten. is withdrawn. |
| 2 | Lane | PRESRV |  |  | 0 | 0 | 1999 | Various street improvements. |
| 2 | Lane | SAFETY | 62 | 126 | 0 | 0.3 | 2000 | Realign intersection & construct left-turn refuge. |
| 2 | Lane | PRESRV | 69 |  | 6.58 | 13 | 1999 | Pavement preservation. |
| 2 | Lane | PRESRV |  |  | 0 | 0 | 1998 | Overlay and minor reconstruction. |
| 2 | Lane | TRANST |  |  | 0 | 0 | 2001 |  |
| 2 | Lane | TRANST |  |  | 0 | 0 | 1998 |  |
| 2 | Lane | PRESRV | 1W |  | 107 | 108.7 | 1998 | Pulverize old PCC roadway and leave as base, then reconstruct section. |
| 2 | Lane | MISCEL | 15 | 126 | 0 | 0 | 1998 | Scenic enhancement. |
| 2 | Lane | PRESRV | 18 | 58 | 0.4 | 6.5 | 1999 | Preserve pavement, safety improvements, widen shoulders. |
| 2 | Lane | MODERN |  |  | 4.1 | 8.1 | 1998 | Slide and curve correction. |
| 2 | Lane | SAFETY | 18 | 58 | 44.13 | 44.35 | 1999 | Geological study to determine best solution. |
| 2 | Lane | TRANST |  |  | 0 | 0 | 2000 |  |
| 2 | Lane | SAFETY | 62 | 126 | 7 | 7.57 | 1998 |  |
| 2 | Lane | TRANST |  |  | 0 | 0 | 2000 |  |
| 2 | Lane | TRANST |  |  | 0 | 0 | 2001 |  |
| 2 | Lane | TRANST |  |  | 0 | 0 | 2000 |  |
| 2 | Lane | TRANST |  |  | 0 | 0 | 1998 |  |
| 2 | Lane | TRANST |  |  | 0 | 0 | 1998 |  |
| 2 | Lane | TRANST |  |  | 0 | 0 | 2000 |  |
| 5 | Malheur | PRESRV | 7 | 20 | 245.7 | 258.2 | 1999 | Hot mix pavement through Vale, EAC pavement, chip seal, rock-fall correction, and guardrail. |
| ODOT Region | County | Work Type | OR Hwy # | Route | Beg. MP | End MP | Const. Year | Work Description |
| 5 | Malheur | SAFETY | 6 |  | 377.6 | 377.6 | 1998 | Erect variable message sign. |
| 5 | Malheur | MODERN | 455 | 95 | 27.4 | 30.3 | 2001 | Address transportation problems associated with Snake River Correctional Facility expansion. |
| 5 | Malheur | BRIDGE | 456 | 95 | 10.98 | 11.08 | 2001 | Place scour protection. |
| 5 | Malheur | BRIDGE |  |  | 4.41 | 4.42 | 1998 | Replace structure. |
| 5 | Malheur | BRIDGE | 7 | 20 | 203.3 | 203.3 | 2000 | Place scour protection. |
| 5 | Malheur | PRESRV | 456 | 95 | 66.18 | 75.7 | 1998 | 2 inch EAC leveling, 6 inch EAC overlay, and dry key chip seal. |
| 5 | Malheur | SAFETY | 456 | 95 | 0 | 121 | 1999 | Construct rumble strips. |
| 5 | Malheur | BRIDGE |  |  | 12.2 | 12.3 | 1999 | Replace structure. |
| 5 | Malheur | BRIDGE |  |  | 10 | 10.01 | 1999 | Rehabilitate structure. |
| 5 | Malheur | PRESRV | 7 | 20 | 223.1 | 245.7 | 2000 | EAC overlay, chipseal, guardrail. |

Appendix d – Advanced Technology Projects/Programs

| CPA/Technology | Existing/Planned, Date | State | Region(R)/District(D) | Route | MP | Dir | Location |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Traveler Safety and Security |  |  |  |  |  |  |  |
| RWIS | E | CA | D1 | 101 | R128.95 |  |  |
| RWIS | E | CA | D2 | I-5 | R14.45 | N | Black Butte Summit |
| RWIS | E | CA | D2 | I-5 | R7.1 | S | Truck Scales |
| RWIS | E | CA | D2 | 5 | 23 | N | Edgewood |
| RWIS & AutomatedWind Advisory | E | CA | D2 | I-5 | R18.5 | N | Weed Airport |
| RWIS | P | CA | D2 | 299 | 51.27 |  | Cedar Pass Summit |
| RWIS | P | CA | D2 | 395 | 133.3 |  | Sage Hen Summit |
| RWIS | P | CA | D2 | 299 | 12.7 |  | Adin Summit |
| RWIS | P | CA | D2 | 36 | 11.76 |  | Fredonyer Summit |
| RWIS | P | CA | D2 | 44 | 50.5 |  | Eskimo Hill |
| RWIS | P | CA | D2 | 299 | 68.17 |  | Hatchet Mt. Summit |
| RWIS | P | CA | D2 | 89 | 3.23 |  | Deadhorse Summit |
| RWIS | P | CA | D2 | 299 | 72.2 |  | Buckhorn Summit |
| RWIS | P | CA | D2 | 299 | 48.5 |  | Mtn Oregon |
| RWIS | P | CA | D2 | 97 | 29.91 |  | Mt. Hebron |
| RWIS | P | CA | D2 | 89 | 29.2 |  | McCloud Summit |
| RWIS | P | CA | D2 | 36 | 87.8 |  | Morgan Summit |
| RWIS* | P | CA | D2 | 70 | 55.24 |  | Lee Summit |
| RWIS & AutomatedWind Advisory* | P | CA | D2 | 395 | 20.2 |  | Hallelujah Junct. |
| RWIS & AutomatedWind Advisory | P | CA | D2 | 395 | 56.5 |  | Janesville |
| RWIS & AutomatedWind Advisory | P | CA | D2 | I-5 | R44.3 | N | Walters Rd |
| RWIS | E | OR | R2 | 20, 126 | 80.77 | 2-3-7 | Santiam Pass |
| RWIS | E | OR | R2 | 58 | 62.07 | 2-5-1 | Willamette Pass Ski Area |
| RWIS | E | OR | R2 | 58 | 53.00 | 2-5-2 |  |
| RWIS | E | OR | R2 | 126 | 12.74 | 2-5-3 | Walterville Scalehouse |
| RWIS | E | OR | R2 | 99 | 16.81 | 2-5-4 |  |
| RWIS | E | OR | R2 | 126 | 26.48 | 2-5-5 | Siuslaw/Whiteacre Turnoff |
| RWIS* | E | OR | R2 | 20 | 20.00 | 4-10-5 | Horse Ridge |
| RWIS | E | OR | R2 | 20, 126 | 85.03 | 4-10-4 | Jack Lake Rd. Suttle Lake |
| RWIS | E | OR | R3 | 5 | 147.20 | 3-6-1 |  |
| RWIS | E | OR | R3 | 5 | 167.60 | 3-6-2 |  |
| RWIS | E | OR | R3 | 5 | 90.20 | 3-6-3 |  |
| RWIS | E | OR | R3 | 42 | 58.50 | 3-6-4 |  |
| RWIS | E | OR | R3 | 5 | 109.00 | 3-6-5 |  |
| RWIS | E | OR | R3 | 42 | 42.00 | 3-7-1 |  |
| RWIS | E | OR | R3 | 101 | 233.00 | 3-7-2 |  |
| RWIS | E | OR | R3 | 42 | 40.00 | 3-7-3 |  |
| RWIS | E | OR | R3 | 101 | 307.00 | 3-7-4 |  |
| RWIS | E | OR | R3 | 101 | 293.50 | 3-7-5 |  |
| RWIS | E | OR | R3 | 101 | 258.00 | 3-7-6 |  |
| RWIS | E | OR | R3 | 5 | 5.02 | 3-8-1 | Siskiyou Summit |
| RWIS | E | OR | R3 | 230 | 12.5 | 3-8-2 | West Diamond Lake Summit |
| CPA/Technology | Existing/Planned, Date | State | Region(R)/District(D) | Route | MP | Dir | Location |
| Traveler Safety and Security |  |  |  |  |  |  |  |
| RWIS | E | OR | R3 | 140 | 8.57 | 4-11-4 | Camas Prairie |
| RWIS | E | OR | R3 | 66 | 49.9 | 4-11-6 | Hayden Mountain Summit |
| RWIS | E | OR | R3 | 5 | 28.33 | 3-8-3 | Medford Viaduct |
| RWIS | E | OR | R4 | 97 | 142.27 | 4-10-1 | Lava Butte |
| RWIS | E | OR | R4 | 372 | 21.98 | 4-10-6 | Mt. Bachelor |
| RWIS | E | OR | R4 | 97 | 230.00 | 4-10-7 | Sand Creek/Silver Lake Cutoff |
| RWIS | E | OR | R4 | 58 | 72.63 | 4-10-8 | Stockpile Site |
| RWIS | E | OR | R4 | 31 | 29.00 | 4-10-9 | Horse Ranch Hill |
| RWIS | E | OR | R4 | 31 | 63.01 | 4-10-10 | Picture Rock Pass |
| RWIS | E | OR | R4 | 140 | 30.93 | 4-11-1 | Bly Mountain Summit |
| RWIS | E | OR | R4 | 140 | 66.75 | 4-11-2 | Quartz Mountain Summit |
| RWIS | E | OR | R4 | 395 | 90.02 | 4-11-3 | Valley Falls Junction |
| RWIS | E | OR | R4 | 97 | 136.00 |  | Bend |
| RWIS | E | OR | R4 | 20 | 104.62 |  | Riley Junction |
| RWIS | E | OR | R4 | 140 | 58.7 | 4-11-5 | Doak Mountain |
| RWIS | E | OR | R5 | 95 | 2.28 | 5-14-2 | Succor Creek |
| RWIS | E | OR | R5 | 205 | 62.5 | 5-14-3 | P'Hill |
| RWIS | E | OR | R5 | 95 | 121.11 | 5-14-5 | McDermitt |
| RWIS* | P 1998 | OR | R2 | I-5 | 236.06 |  | Wah-Chang Rd in Albany |
| RWIS | P 1999 | OR | R2 | 58 | 62.5 |  | Odell Lake |
| RWIS | P 1999 | OR | R3 | I-5 | 167.84 |  | N. Douglas County Line |
| RWIS | P 1999 | OR | R3 | 42 | 43.53 |  | Coos Bay - Roseburg Hwy |
| RWIS | P 1998 | OR | R3 | I-5 | 27 |  | Medford Viaduct |
| RWIS | P 1998 | OR | R4 | 26 | 36.29 |  | Brightwood Weigh Station |
| RWIS | P 1999 | OR | R4 | 140 | 31 |  | Klamath Falls - Lakeview Hwy |
| RWIS | P 1999 | OR | R4 | 395 | 39.78 |  | Battle Mountain |
| RWIS | P 1998 | OR | R4 | 97 | 150 |  |  |
| RWIS | P 1999 | OR |  | 6 | 32.76 |  | Wilson River Hwy |
| RWIS | P 1998 | OR |  | 233 | 19.53 |  | W. Diamond Lake Hwy |
| CMS | E | CA | D1 | 101 | 31.6 | S | N OF 101/20 SEP |
| CMS Portable* | E | CA | D1 |  |  | N | BRACUT |
| CMS Portable* | E | CA | D1 |  |  | N | BRACUT |
| CMS Portable* | E | CA | D1 |  |  | S | UKIAH |
| CMS Portable* | E | CA | D1 |  |  | S | UKIAH |
| CMS Portable* | E | CA | D1 |  |  | S | UKIAH |
| CMS Portable | E | CA | D1 |  |  | N | FORTUNA |
| CMS Portable | E | CA | D1 |  |  | N | CRESCENT CITY |
| CMS Portable | E | CA | D1 |  |  | S | CLEARLAKE OAKS |
| CMS Portable | E | CA | D1 |  |  | S | LAKEPORT |
| CMS | E | CA | D2 | I-5 | R44.3 | N/S | Walters Rd |
| CMS | E | CA | D2 | I-5 | 9.68 | N | Ream Rd |
| CMS | E | CA | D2 | I-5 | R13.19 | S | Abrams Lake Rd |
| CMS | E | CA | D2 | I-5 | 39.8 | N | Truck Scales |
| CMS | E | CA | D2 | I-5 | 41.53 | S | Truck Scales |
| CMS | E | CA | D2 | I-5 | 10.86 | N | Smith Rd |
| CPA/Technology | Existing/Planned, Date | State | Region(R)/District(D) | Route | MP | Dir | Location |
| Traveler Safety and Security |  |  |  |  |  |  |  |
| CMS | E | CA | D2 | I-5 | 20.98 | N | Pine Grove |
| CMS* | P 1999 | CA | D1 | 101 | 20.0 | N | S OF CUSHING CRK |
| CMS | P 2000 | CA | D1 | 101 | 37.4 | S | S OF SMITH RIVER |
| CMS | P 2000 | CA | D1 | 101 | R28.5 | N | S OF 101/199 SEP |
| CMS | P 2000 | CA | D1 | 199 | 36.2 | S | S OF STATE LINE |
| CMS | P 1998 | CA | D1 | 101 | 89.4 | S | N OF 101/299 SEP |
| CMS | P 1998 | CA | D1 | 101 | 87.7 | N | S OF 101/299 SEP |
| CMS | P 1998 | CA | D1 | 101 | 58.7 | S | N OF JCT 36 |
| CMS | P 2000 | CA | D1 | 101 | 56.5 | N | S OF JCT 36 |
| CMS | P 2000 | CA | D1 | 20 | 32.6 | W | E OF JCT 53 |
| CMS | P 2000 | CA | D1 | 20 | 30.6 | E | W OF JCT 53 |
| CMS | P 2000 | CA | D1 | 20 | 7.4 | E | W OF JCT 29 |
| CMS | P 2000 | CA | D1 | 53 | 5.1 | N | S OF JCT 20 |
| CMS | P 2000 | CA | D1 | 1 | 57.3 | S | S OF JCT 20 AT GIBNEY |
| CMS | P 2000 | CA | D1 | 101 | 49.2 | N | N OF WILLITS |
| CMS | P 1998 | CA | D1 | 101 | 29.8 | N | S OF 101/20 SEP |
| CMS | P 1998 | CA | D1 | 101 | 31.6 | S | N OF 101/20 SEP |
| CMS | P 2000 | CA | D1 | 20 | 1.0 | E | E OF JCT 1 |
| CMS | P 2000 | CA | D1 | 20 E | 33.9 | W | W OF WILLITS |
| CMS | P 2000 | CA | D1 | 20 W | 32.6 | W | E OF 20/101 SEP |
| CMS | P | CA | D2 | I-5 | R65.52 | N | Bailey Hill Rd |
| CMS | P | CA | D2 | 395 | R27.1 |  | Jct. 395/36 |
| CMS | P | CA | D2 | 36 | 21.1 |  | W of Susanville |
| CMS* | P | CA | D2 | 395 | R2.08 | N | CA/NV State Line |
| CMS | P | CA | D2 | I-5 | 0 |  | Dist 2/3 Border (Orland) |
| CMS | P | CA | D2 | I-5 | 8.8 | S | N of Corning |
| CMS | P | CA | D2 | 36 | 43 | E | Red Bluff |
| CMS | P | CA | D2 | I-5 | 39.5 | N | Truck Scales |
| CMS | P | CA | D2 | 299 | 22.1 | W | Redding |
| CMS | P | CA | D2 | I-5 | R43.5 | S | Lakehead Rest Area |
| CMS | P | CA | D2 | 44 | R2.08 |  | Shasta View |
| CMS | P | CA | D2 | 299 | R27.22 |  | Old Oregon Trail UC |
| CMS | E | OR | R3 | 5 (1) | 28.33 |  | Medford |
| CMS | P 1998 | OR | R3 | I-5 | 16.72 |  |  |
| CMS | P 1998 | OR | R3 | I-5 | 31.31 |  |  |
| HAR | E | CA | D1 | 101 | 46.4 |  | WILLITS AT JCT 20 |
| HAR | E | CA | D1 | 53 | 1.47 |  | CLEARLAKE AT DAM RD |
| HAR | E | CA | D1 | 101 | 77.3 |  | EUREKA-DIST OFFICE |
| HAR | E | CA | D1 | 101 | 77.3 | N | EUREKA SHOP YARD |
| HAR | E | CA | D2 | 395 | R27.1 |  | Jct. 395/36 |
| HAR | E | CA | D2 | I-5 | R44.31 | S | Walters Rd |
| HAR | E | CA | D2 | I-5 | R13.19 | S | Abrams Lake Rd |
| HAR | E | CA | D2 | I-5 | 26.6 |  | Red Bluff Central IC |
| HAR | E | CA | D2 | 299 | 79.68 |  | Jct. 89/299 |
| HAR* | E | CA | D2 | 395 | 1.5 | N | Inspection Station |
| CPA/Technology | Existing/Planned, Date | State | Region(R)/District(D) | Route | MP | Dir | Location |
| Traveler Safety and Security |  |  |  |  |  |  |  |
| HAR* | P | CA | D2 | 70 | 20.5 |  | E of Chico |
| HAR* | P | CA | D2 | 99 | 35 |  | Intersection of 32/99 |
| HAR | P | CA | D2 | 299 | 42 |  | Alturas |
| HAR | P | CA | D2 | I-5 | 0 |  | Dist 2/3 Border (Orland) |
| HAR | P | CA | D2 | 36 | R12.5 |  | Rest Area |
| HAR | P | CA | D2 | 299 | 0.9 |  | Adin Jct 299/139 |
| HAR | P | CA | D2 | 299 | 58.2 |  | Douglas City |
| HAR Super Station | P | CA | D2 | I-5 | R16.15 |  | Hilltop OC |
| Call Box | E | CA | D1 | 199 | 1 | Right | Del Norte County |
| Call Box | E | CA | D1 | 199 | 3 | Right | Del Norte County |
| Call Box | E | CA | D1 | 199 | 8 | Left | Del Norte County |
| Call Box | E | CA | D1 | 199 | 10.81 | Right | Del Norte County |
| Call Box | E | CA | D1 | 199 | 20.07 | Right | Del Norte County |
| Call Box | E | CA | D1 | 199 | 23.13 | Right | Del Norte County |
| Call Box | E | CA | D1 | 199 | 26.12 | Right | Del Norte County |
| Call Box | E | CA | D1 | 199 | 33.32 | Left | Del Norte County |
| Call Box | E | CA | D1 | 101 | 14.8 | Left | Del Norte County |
| Call Box | E | CA | D1 | 101 | 18.97 | Right | Del Norte County |
| Call Box | E | CA | D1 | 101 | 36.53 | Left | Del Norte County |
| Call Box | E | CA | D1 | 299 | 12.6 |  | Humboldt County |
| Call Box | E | CA | D1 | 299 | 21.1 |  | Humboldt County |
| Call Box | E | CA | D1 | 299 | 27.8 |  | Humboldt County |
| Call Box | E | CA | D1 | 299 | 37.7 |  | Humboldt County |
| Call Box | E | CA | D1 | 299 | 42.5 |  | Humboldt County |
| Call Box | E | CA | D1 | 101 | 97.6 |  | Humboldt County |
| Call Box | E | CA | D1 | 101 | 97.5 |  | Humboldt County |
| Call Box | E | CA | D1 | 101 | 107.2 |  | Humboldt County |
| Call Box | E | CA | D1 | 101 | 107.3 |  | Humboldt County |
| Call Box | E | CA | D1 | 101 | 56.1 |  | Humboldt County |
| Call Box | E | CA | D1 | 101 | 56 |  | Humboldt County |
| Call Box | E | CA | D1 | 101 | 47.1 |  | Humboldt County |
| Call Box | E | CA | D1 | 101 | 39.3 |  | Humboldt County |
| Call Box | E | CA | D1 | 101 | 39.2 |  | Humboldt County |
| Call Box | E | CA | D1 | 101 | 32.1 |  | Humboldt County |
| Call Box | E | CA | D1 | 101 | 32 |  | Humboldt County |
| Call Box | E | CA | D1 | 101 | 23.1 |  | Humboldt County |
| Call Box | E | CA | D1 | 101 | 23 |  | Humboldt County |
| Call Box | E | CA | D1 | 101 | 15.7 |  | Humboldt County |
| Call Box | E | CA | D1 | 101 | 15.6 |  | Humboldt County |
| Call Box | E | CA | D1 | 101 | 8.1 |  | Humboldt County |
| Call Box | E | CA | D1 | 101 | 8 |  | Humboldt County |
| Call Box | E | CA | D1 | 101 | 68.4 |  | Humboldt County |
| Call Box | E | CA | D1 | 101 | 68.5 |  | Humboldt County |
| Call Box | E | CA | D1 | 101 | 131.6 |  | Humboldt County |
| Call Box | E | CA | D1 | 101 | 131.7 |  | Humboldt County |
| CPA/Technology | Existing/Planned, Date | State | Region(R)/District(D) | Route | MP | Dir | Location |
| Traveler Safety and Security |  |  |  |  |  |  |  |
| Call Box | E | CA | D1 | 20 | 4.45 |  | Lake County |
| Call Box | E | CA | D1 | 20 | 5.94 |  | Lake County |
| Call Box | E | CA | D1 | 20 | 10.85 |  | Lake County |
| Call Box | E | CA | D1 | 20 | 12.68 |  | Lake County |
| Call Box | E | CA | D1 | 20 | 15.52 |  | Lake County |
| Call Box | E | CA | D1 | 20 | 21.16 |  | Lake County |
| Call Box | E | CA | D1 | 20 | 23.09 |  | Lake County |
| Call Box | E | CA | D1 | 20 | 32.82 |  | Lake County |
| Call Box | E | CA | D1 | 20 | 34.42 |  | Lake County |
| Call Box | E | CA | D1 | 20 | 36.4 |  | Lake County |
| Call Box | E | CA | D1 | 20 | 38.66 |  | Lake County |
| Call Box | E | CA | D1 | 20 | 40.85 |  | Lake County |
| Call Box | E | CA | D1 | 20 | 42.36 |  | Lake County |
| Call Box | E | CA | D1 | 20 | 44.7 |  | Lake County |
| Call Box | E | CA | D1 | 20 | 46.22 |  | Lake County |
| Call Box | E | CA | D1 | 29 | 3.33 |  | Lake County |
| Call Box | E | CA | D1 | 29 | 8.04 |  | Lake County |
| Call Box | E | CA | D1 | 29 | 12.06 |  | Lake County |
| Call Box | E | CA | D1 | 29 | 16.78 |  | Lake County |
| Call Box | E | CA | D1 | 29 | 18.02 |  | Lake County |
| Call Box | E | CA | D1 | 29 | 22.5 |  | Lake County |
| Call Box | E | CA | D1 | 29 | 24.47 |  | Lake County |
| Call Box | E | CA | D1 | 29 | 26.81 |  | Lake County |
| Call Box | E | CA | D1 | 29 | 29.65 |  | Lake County |
| Call Box | E | CA | D1 | 29 | 33.59 |  | Lake County |
| Call Box | E | CA | D1 | 29 | 35.71 |  | Lake County |
| Call Box | E | CA | D1 | 29 | 38.2 |  | Lake County |
| Call Box | E | CA | D1 | 29 | 48.63 |  | Lake County |
| Call Box | E | CA | D1 | 29 | 51.43 |  | Lake County |
| Call Box | E | CA | D1 | 53 | 4.13 |  | Lake County |
| Call Box | E | CA | D1 | 53 | 6.43 |  | Lake County |
| Call Box | E | CA | D1 | 20 | 31.05 |  | Lake County |
| Call Box | E | CA | D1 | 29 | 14.28 |  | Lake County |
| Call Box | E | CA | D1 | 29 | 31.2 |  | Lake County |
| Emergency Services |  |  |  |  |  |  |  |
| EMS | P 2000 | CA | D1 | 101 | 42.3 | N | S OF WILLITS |
| EMS | P 2000 | CA | D1 | 101 | 49.2 | S | N OF WILLITS |
| EMS | P 2000 | CA | D1 | 20 W | 32.6 | E | W OF WILLITS |
| Tourism and Travel Information Services |
| Information Kiosks | P '98 | CA | D2 | I-5 | R58.0 | S | Collier Rest Area |
| Information Kiosks | P '98 | CA | D2 | I-5 | 33.3 | N | Rest Area |
| Information Kiosks | P '98 | CA | D2 | I-5 | 34.3 | S | Rest Area |
| Information Kiosks | P '98 | CA | D2 | I-5 | 10.3 | N/S | Corning Rest Area |
| Information Kiosks | P '98 | CA | D2 | I-5 | R25.8 | N/S | Weed Rest Area |
| Information Kiosks | P '98 | CA | D2 | I-5 | R7.1 | S | Truck Scales |
| CPA/Technology | Existing/Planned, Date | State | Region(R)/District(D) | Route | MP | Dir | Location |
| Tourism and Travel Information Services |
| Information Kiosks | P '98 | CA | D2 | I-5 | R43.5 | S | Lakehead Rest Area |
| Information Kiosks | P '98 | CA | D2 | I-5 | 9.77 |  | Knighton Rd Truck Stop |
| Information Kiosks | P '98 | CA | D2 | I-5 | 31.1 | N | Obrian Rest Area |
| Information Kiosks | E | OR | R2 | 58 | 62.07 |  | Willamette Pass |
| Information Kiosks | E | OR | R3 | 101 | 234.03 |  | North Bend |
| Information Kiosks | E | OR | R3 | 101 | 260.64 |  | Bandon |
| Information Kiosks | E | OR | R3 | 101 | 327.85 |  | Gold Beach |
| Information Kiosks | E | OR | R3 | 101 | 354.73 |  | Rest Area N.E. of Brookings |
| Information Kiosks | E | OR | R3 | 101 | 355.38 |  | Brookings |
| Information Kiosks | E | OR |  | 101 | 358.76 |  | Harbor |
| Information Kiosks | E | OR | R3 | 199 | 27.71 |  | Cave Junction |
| Information Kiosks | E | OR | R3 | 46 | 19.51 |  | Oregon Caves National Monument |
| Information Kiosks | E | OR | R3 | 5 | 19.10 |  | Ashland |
| Information Kiosks | E | OR | R3 | 5 | 28.33 |  | Medford |
| Information Kiosks | E | OR | R3 | 5 | 28.33 |  | Medford |
| Information Kiosks | E | OR | R3 | 5 | 28.33 |  | Medford |
| Information Kiosks | E | OR | R3 | 5 | 28.33 |  | Medford |
| Information Kiosks | E | OR | R3 | 5 | 35.44 |  | Central Point |
| Information Kiosks | E | OR | R3 | 5 | 55.38 |  | Grants Pass |
| Information Kiosks | E | OR | R3 | 5 | 58.06 |  | Grants Pass |
| Information Kiosks | E | OR | R3 | 5 | 98.28 |  | Canyonville |
| Information Kiosks | E | OR | R3 | 5 | 124.14 |  | Roseburg |
| Information Kiosks | E | OR | R3 | 5 | 124.14 |  | Roseburg |
| Information Kiosks | E | OR | R3 | 42 | 72.74 |  | Winston |
| Information Kiosks | E | OR | R3 | 138 | 16.34 |  | Glide |
| Information Kiosks | E | OR | R3 | 138 | 50.00 |  |  |
| Information Kiosks | E | OR | R3 | 138 | 78.83 |  | Diamond Lake |
| Information Kiosks | E | OR | R4 | 97 | 272.61 |  | Klamath Falls |
| Information Kiosks | E | OR | R4 | 97 | 280.16 |  | Klamath Falls |
| Information Kiosks | E | OR | R4 | 97 | 289.44 |  | Worden |
| Infrastructure Operations and Maintenance |
| Flood and Scour Detection | E | CA | D2 | 96 | 75.01 |  | Horse Creek |
| Flood and Scour Detection | E | CA | D2 | 3 | 8.66 |  | Scott River |
| CCTV | P | CA | D2 | 89 | 29.2 |  | McCloud Summit |
| CCTV | P | CA | D2 | I-5 | R65.52 | N | Bailey Hill Rd |
| CCTV | P | CA | D2 | I-5 | R14.45 | N | Black Butte Summit |
| CCTV | P | CA | D2 | I-5 | 16.8 |  | Central IC |
| CCTV | P 1998 | OR | R3 | I-5 | 5 |  |  |
| CCTV | P 1998 | OR | R3 | I-5 | 73 |  |  |
| CCTV | P 1998 | OR | R3 | 199 | 16.1 |  |  |
| CCTV | P 1998 | OR | R4 | 97 | 135.97 |  | Various locations in & around Bend |
| ATR | E | CA | D2 | 3 | L 0.10 |  | JCT RTE 36 |
| ATR | E | CA | D2 | 3 | 6.56 |  | HAYFORK |
| ATR | E | CA | D2 | 3 | 30.31 |  | JCT RTE 299 |
| CPA/Technology | Existing/Planned, Date | State | Region(R)/District(D) | Route | MP | Dir | Location |
| Infrastructure Operations and Maintenance |
| ATR | E | CA | D2 | 3 | 30.88 |  | WEAVERVILLE JCT RTE 299 |
| ATR | E | CA | D2 | 3 | 32.31 |  | WEAVERVILLE CTY DMP RD |
| ATR | E | CA | D2 | 3 | 37.60 |  | RUSH CREEK ROAD |
| ATR | E | CA | D2 | 3 | 59.64 |  | TRINITY CNTR MAINT STA |
| ATR | E | CA | D2 | 3 | 32.23 |  | FT. JONES SCOTT RVR RD |
| ATR | E | CA | D2 | 3 | 45.18 |  | FOREST MNTN RANCH |
| ATR | E | CA | D2 | 3 | R46.87 |  | JERRYS RD (CONN TO I-5) |
| ATR | E | CA | D2 | 3 | L49.20 |  | WEST CENTER STREET |
| ATR | E | CA | D2 | 3 | R48.30 |  | N JCT RTE 5 |
| ATR | E | CA | D2 | I-5 | R9.97 |  | GALLAGHER AVE. O.C. |
| ATR | E | CA | D2 | I-5 | R10.06 |  | CORNING N RDSIDE REST |
| ATR | E | CA | D2 | I-5 | R24.47 | N | OFF TO SO. RDBL |
| ATR | E | CA | D2 | I-5 | R24.57 | S | ON FR SO. RDBL |
| ATR | E | CA | D2 | I-5 | R24.71 | N | ON FR SO. RDBL |
| ATR | E | CA | D2 | I-5 | R24.83 | S | OFF TO SO. RDBL |
| ATR | E | CA | D2 | I-5 | R25.12 |  | DIAMOND AVE 8-100 N ON |
| ATR | E | CA | D2 | I-5 | R25.15 |  | DIAMOND AVE 8-100 S OFF |
| ATR | E | CA | D2 | I-5 | R28.53 | S | OFF TO HOFT RD/OLD 99 |
| ATR | E | CA | D2 | I-5 | 30.15 |  | WILCOX RD INTERCHANGE |
| ATR | E | CA | D2 | I-5 | R3.39 |  | JCT RTE 273 |
| ATR | E | CA | D2 | I-5 | R6.53 | N | OFF TO RIVERSIDE AVE |
| ATR | E | CA | D2 | I-5 | R6.60 | S | ON FROM RIVERSIDE AVE |
| ATR | E | CA | D2 | I-5 | R6.70 | N | ON FROM RIVERSIDE AVE |
| ATR | E | CA | D2 | I-5 | R6.90 | S | OFF TO RIVERSIDE AVE |
| ATR | E | CA | D2 | I-5 | R7.90 |  | 0.8 MI. N. OF SACTO. RIVER |
| ATR | E | CA | D2 | I-5 | R13.95 |  | HARTNELL AVE. |
| ATR | E | CA | D2 | I-5 | R14.23 |  | CYPRESS ST NB OFF |
| ATR | E | CA | D2 | I-5 | R14.28 |  | CYPRESS ST SB ON |
| ATR | E | CA | D2 | I-5 | R14.65 |  | CYPRESS ST SB OFF |
| ATR | E | CA | D2 | I-5 | R14.76 |  | CYPRESS ST NB ON |
| ATR | E | CA | D2 | I-5 | R14.91 |  | REDDING, CYPRESS ST |
| ATR | E | CA | D2 | I-5 | R15.15 | N | OFF TO WB 299 |
| ATR | E | CA | D2 | I-5 | R15.27 | N | OFF TO HILLTOP |
| ATR | E | CA | D2 | I-5 | R15.39 | S | OFF TO EB 299 |
| ATR | E | CA | D2 | I-5 | R15.71 | S | OFF TO WB 299 |
| ATR | E | CA | D2 | I-5 | 16.15 | N | HILLTOP AT OFF FROM I-5 |
| ATR | E | CA | D2 | I-5 | R23.91 | N | OFF TO MTN GATE |
| ATR | E | CA | D2 | I-5 | R23.92 | S | ON FROM MTN GATE |
| ATR | E | CA | D2 | I-5 | R24.24 | S | OFF TO MTN GATE |
| ATR | E | CA | D2 | I-5 | R24.26 | N | ON FROM MTN GATE |
| ATR | E | CA | D2 | I-5 | R24.88 |  | 0.8 MI N/O MNTN GATE OC |
| ATR | E | CA | D2 | I-5 | R25.86 |  | FAWNDALE OVRCRSSING |
| ATR | E | CA | D2 | I-5 | R26.22 |  | FAWNDALE N/B ON |
| ATR | E | CA | D2 | I-5 | R26.23 |  | FAWNDALE S/B OFF |
| ATR | E | CA | D2 | I-5 | R27.46 |  | BRIDGE BAY N/B OFF |
| CPA/Technology | Existing/Planned, Date | State | Region(R)/District(D) | Route | MP | Dir | Location |
| Infrastructure Operations and Maintenance |
| ATR | E | CA | D2 | I-5 | R27.60 |  | BRIDGE BAY S/B ON |
| ATR | E | CA | D2 | I-5 | R27.62 |  | BRIDGE BAY N/B ON |
| ATR | E | CA | D2 | I-5 | R27.77 |  | BRIDGE BAY S/B OFF |
| ATR | E | CA | D2 | I-5 | R45.74 |  | VOLLMERS RD N/B OFF |
| ATR | E | CA | D2 | I-5 | R45.86 |  | VOLLMERS RD S/B ON |
| ATR | E | CA | D2 | I-5 | R45.91 |  | VOLLMERS RD N/B ON |
| ATR | E | CA | D2 | I-5 | R46.19 |  | VOLLMERS RD S/B OFF |
| ATR | E | CA | D2 | I-5 | R48.96 |  | LA MOINE S/B ON |
| ATR | E | CA | D2 | I-5 | R49.18 |  | LA MOINE RD N/B OFF |
| ATR | E | CA | D2 | I-5 | R49.32 |  | LA MOINE RD S/B OFF |
| ATR | E | CA | D2 | I-5 | R49.38 |  | LA MOINE N/B ON |
| ATR | E | CA | D2 | I-5 | R50.55 |  | POLLARD FLAT S/B ON |
| ATR | E | CA | D2 | I-5 | R50.58 |  | POLLARD FLAT N/B OFF |
| ATR | E | CA | D2 | I-5 | R50.91 |  | POLLARD FLAT N/B ON |
| ATR | E | CA | D2 | I-5 | R50.99 |  | POLLARD FLAT S/B OFF |
| ATR | E | CA | D2 | I-5 | R57.33 |  | SIMS RD IC |
| ATR | E | CA | D2 | I-5 | R11.37 |  | O.2 MI N/O LASSEN AVE OC |
| ATR | E | CA | D2 | I-5 | R12.91 |  | ABRAMS LK RD INTCHNGE |
| ATR | E | CA | D2 | I-5 | R23.17 |  | EDGEWOOD IC |
| ATR | E | CA | D2 | I-5 | R68.170 |  | HILT ROAD INTERCHANGE |
| ATR | E | CA | D2 | 32 | R24.63 |  | JCT RTE 36 |
| ATR | E | CA | D2 | 36 | R28.96 |  | JCT RTE 3 NORTH |
| ATR | E | CA | D2 | 36 | R22.05 |  | BOWMAN RD. |
| ATR | E | CA | D2 | 36 | R30.00 |  | CANNON ROAD |
| ATR | E | CA | D2 | 36 | 39.40 |  | BAKER ROAD |
| ATR | E | CA | D2 | 36 | R41.24 |  | MAIN STREET |
| ATR | E | CA | D2 | 36 | L39.75 |  | MAIN STREET |
| ATR | E | CA | D2 | 36 | L41.10 |  | RED BLUFF, WALNUT ST |
| ATR | E | CA | D2 | 36 | L41.20 |  | RED BLUFF, WALNUT ST |
| ATR | E | CA | D2 | 36 | 41.40 |  | RED BLUFF SACTO RVR BR |
| ATR | E | CA | D2 | 36 | 42.72 |  | RED BLUFF CHESTNUT AVE |
| ATR | E | CA | D2 | 36 | 42.87 |  | RED BLUFF CHESTNUT AVE |
| ATR | E | CA | D2 | 36 | 43.90 |  | JCT RTE 99 |
| ATR | E | CA | D2 | 36 | 44.37 |  | JCT RTE 99 RED BLUFF E |
| ATR | E | CA | D2 | 36 | 55.20 |  | CO RD A6 MANTON RD |
| ATR | E | CA | D2 | 36 | 57.21 |  | CO RD A6 MANTON RD |
| ATR | E | CA | D2 | 36 | 82.19 |  | MINERAL MAINT STA |
| ATR | E | CA | D2 | 36 | 6.05 |  | JCT RTE 89 SOUTH |
| ATR | E | CA | D2 | 36 | 6.54 |  | JCT RTE 89 SOUTH |
| ATR | E | CA | D2 | 36 | 8.89 |  | CHESTER, N. FORK FEATHER RIVER BR. |
| ATR | E | CA | D2 | 36 | 9.18 |  | CHESTER, MELLISA AVE |
| ATR | E | CA | D2 | 36 | 18.40 |  | JCT RTE 147 |
| ATR | E | CA | D2 | 36 | 18.95 |  | JCT RTE 44 |
| ATR | E | CA | D2 | 36 | R19.67 |  | JCT RTE 44 |
| CPA/Technology | Existing/Planned, Date | State | Region(R)/District(D) | Route | MP | Dir | Location |
| Infrastructure Operations and Maintenance |
| ATR | E | CA | D2 | 36 | 24.45 |  | COTTAGE STREET |
| ATR | E | CA | D2 | 36 | 24.99 |  | SUSANVILLE, PACIFIC ST. |
| ATR | E | CA | D2 | 36 | 26.01 |  | RIVERSIDE DRIVE |
| ATR | E | CA | D2 | 36 | R28.00 |  | JCT RTE 395 |
| ATR | E | CA | D2 | 44 | R0.07 | E | OFF TO NB RTE 5 |
| ATR | E | CA | D2 | 44 | R0.10 | W | OFF TO NB RTE 5 |
| ATR | E | CA | D2 | 44 | 0.13 |  | ON HILLTOP RD |
| ATR | E | CA | D2 | 44 | 0.13 |  | ON HILLTOP RD |
| ATR | E | CA | D2 | 44 | R0.16 | E | OFF TO HILLTOP |
| ATR | E | CA | D2 | 44 | R0.18 | E | ON FR NB 5/HILLTOP |
| ATR | E | CA | D2 | 44 | R0.62 | W | ON FR DANA/FRIENDLY |
| ATR | E | CA | D2 | 44 | R0.79 | E | OFF TO DANA/FRIENDLY |
| ATR | E | CA | D2 | 44 | R1.09 | W | OFF FR VICTOR AVE. |
| ATR | E | CA | D2 | 44 | R1.14 | E | OFF TO VICTOR AVE. |
| ATR | E | CA | D2 | 44 | 1.40 |  | ON VICTOR AVE. |
| ATR | E | CA | D2 | 44 | R1.37 | W | OFF TO VICTOR AVE. |
| ATR | E | CA | D2 | 44 | R1.43 | E | ON FR VICTOR AVE. |
| ATR | E | CA | D2 | 44 | R1.51 |  | REDDING, VICTOR AVENUE |
| ATR | E | CA | D2 | 44 | R1.87 | W | ON FROM SHASTA VW DR |
| ATR | E | CA | D2 | 44 | R1.88 | E | OFF TO SHASTA VIEW DR |
| ATR | E | CA | D2 | 44 | R2.11 | W | ON FRM N SHASTA VW DR |
| ATR | E | CA | D2 | 44 | R2.26 | W | OFF TO SHASTA VIEW DR |
| ATR | E | CA | D2 | 44 | R2.27 | E | ON FROM SHASTA VW DR |
| ATR | E | CA | D2 | 44 | R4.30 |  | AIRPORT ROAD |
| ATR | E | CA | D2 | 44 | R6.71 |  | DESCHUTES RD IC |
| ATR | E | CA | D2 | 44 | R6.77 | W | WB ON RAMP |
| ATR | E | CA | D2 | 44 | R6.81 | E | EB OFF RAMP |
| ATR | E | CA | D2 | 44 | R7.21 | W | WB OFF RAMP |
| ATR | E | CA | D2 | 44 | 7.23 | E | EB ON RAMP |
| ATR | E | CA | D2 | 44 | R7.38 |  | DESCHUTES ROAD |
| ATR | E | CA | D2 | 44 | R18.87 |  | DERSCH ROAD |
| ATR | E | CA | D2 | 44 | R19.03 |  | DERSCH ROAD |
| ATR | E | CA | D2 | 44 | 32.00 |  | SHINGLETOWN |
| ATR | E | CA | D2 | 44 | 42.48 |  | VIOLA |
| ATR | E | CA | D2 | 44 | 49.10 |  | LASSEN NATL PARK ENTR |
| ATR | E | CA | D2 | 44 | 62.60 |  | JCT RTE 89 |
| ATR | E | CA | D2 | 44 | 63.55 |  | JCT RTE 89 |
| ATR | E | CA | D2 | 44 | 37.17 |  | JCT RTE 36 |
| ATR | E | CA | D2 | 49 | 7.42 |  | JCT RTE 70 |
| ATR | E | CA | D2 | 89 | 8.65 |  | BLAIRSDEN, JCT RTE 70 |
| ATR | E | CA | D2 | 89 | 14.50 |  | JCT RTE 70 |
| ATR | E | CA | D2 | 89 | 20.47 |  | GREENVILLE BECKWOURTH RD |
| ATR | E | CA | D2 | 89 | R41.73 |  | JCT RTE 36 |
| ATR | E | CA | D2 | 89 | R0.24 |  | WEST JCT RTE 36 |
| CPA/Technology | Existing/Planned, Date | State | Region(R)/District(D) | Route | MP | Dir | Location |
| Infrastructure Operations and Maintenance |
| ATR | E | CA | D2 | 89 | 0.07 |  | JCT RTE 44 |
| ATR | E | CA | D2 | 89 | 21.69 |  | 4 CORNERS JCT RTE 299 |
| ATR | E | CA | D2 | 89 | 22.06 |  | 4 CORNERS JCT RTE 299 |
| ATR | E | CA | D2 | 89 | 28.60 |  | LAKE BRITTON |
| ATR | E | CA | D2 | 89 | 24.52 |  | MINNESOTA AVE |
| ATR | E | CA | D2 | 89 | 25.10 |  | BROADWAY & S AVE |
| ATR | E | CA | D2 | 89 | 33.94 |  | MOUNT SHASTA BLVD. |
| ATR | E | CA | D2 | 96 | 38.92 |  | HAPPY CAMP MAINT STA |
| ATR | E | CA | D2 | 96 | 41.32 |  | HAPPY CAMP, MAIN ST. |
| ATR | E | CA | D2 | 96 | 60.75 |  | SEIAD MAINT. STATION |
| ATR | E | CA | D2 | 96 | 103.31 |  | JCT RTE 263 |
| ATR | E | CA | D2 | 96 | 105.82 |  | JCT RTE 5 KLMTH RVR BR |
| ATR | E | CA | D2 | 97 | L0.09 |  | JCT RTE 5 |
| ATR | E | CA | D2 | 97 | 0.96 |  | JCT. RTE 265 |
| ATR | E | CA | D2 | 97 | 1.14 |  | LINCOLN STREET, WEED |
| ATR | E | CA | D2 | 97 | 20.20 |  | GRASS LAKE |
| ATR | E | CA | D2 | 97 | 34.53 |  | 1.7 MI. S/O BALL MTN ROAD |
| ATR | E | CA | D2 | 97 | 50.90 |  | DORRIS, FIRST STREET |
| ATR | E | CA | D2 | 97 | 53.69 |  | JCT. RTE 161 EAST |
| ATR | E | CA | D2 | 99 | 0.11 |  | BUTTE-TEHAMA CO LINE |
| ATR | E | CA | D2 | 99 | 5.08 |  | SOUTH AVENUE |
| ATR | E | CA | D2 | 99 | 11.18 |  | SHERMAN STREET |
| ATR | E | CA | D2 | 99 | 12.31 |  | ARAMAYO WAY |
| ATR | E | CA | D2 | 99 | 24.76 |  | JCT RTE 36 RED BLUFF E |
| ATR | E | CA | D2 | 139 | 0.09 |  | SUSANVILLE, JCT RTE 36 MAIN ST |
| ATR | E | CA | D2 | 139 | 3.40 |  | SUSANVILLE DUMP ROAD |
| ATR | E | CA | D2 | 139 | 0.03 |  | ADIN, JCT RTE 299 |
| ATR | E | CA | D2 | 139 | 17.12 |  | CANBY, JCT RTE 299 |
| ATR | E | CA | D2 | 139 | 17.86 |  | TULELAKE QRNTINE STA |
| ATR | E | CA | D2 | 139 | 50.68 |  | MODOC-SISKIYOU CO LINE |
| ATR | E | CA | D2 | 139 | 4.77 |  | JCT RTE 161 OR STATE LN |
| ATR | E | CA | D2 | 147 | 0.13 |  | JCT RTE 89 |
| ATR | E | CA | D2 | 147 | 1.79 |  | JCT RTE 36 |
| ATR | E | CA | D2 | 151 | 0.08 |  | SHASTA DAM |
| ATR | E | CA | D2 | 151 | 3.97 |  | LAKE BLVD |
| ATR | E | CA | D2 | 151 | 5.51 |  | SPRR UNDERPASS |
| ATR | E | CA | D2 | 151 | 6.76 |  | CASCADE BLVD; JCT RTE 5 |
| ATR | E | CA | D2 | 161 | 1.11 |  | JCT RTE 97 |
| ATR | E | CA | D2 | 161 | 19.18 |  | JCT RTE 139 |
| ATR | E | CA | D2 | 172 | 0.05 |  | JCT RTE 36 |
| ATR | E | CA | D2 | 172 | 8.84 |  | JCT RTE 36 |
| ATR | E | CA | D2 | 263 | 49.39 |  | JCT RTE 3 TEBEE STREET |
| ATR | E | CA | D2 | 263 | 56.34 |  | JCT RT 96 SHASTA RVR BR |
| ATR | E | CA | D2 | 265 | 20.21 |  | WEED, JCT RTE 5 |
| CPA/Technology | Existing/Planned, Date | State | Region(R)/District(D) | Route | MP | Dir | Location |
| Infrastructure Operations and Maintenance |
| ATR | E | CA | D2 | 273 | 3.41 |  | S. JCT ROUTE 5 |
| ATR | E | CA | D2 | 273 | 3.56 |  | S.JCT ROUTE 5 |
| ATR | E | CA | D2 | 273 | 11.08 |  | CANYON ROAD |
| ATR | E | CA | D2 | 273 | 11.16 | N | CANYON ROAD |
| ATR | E | CA | D2 | 273 | 11.20 | S | CANYON ROAD |
| ATR | E | CA | D2 | 273 | 12.57 |  | BONNEYVIEW/CEDARS RD. |
| ATR | E | CA | D2 | 273 | 14.08 |  | BRESLAUER |
| ATR | E | CA | D2 | 273 | 14.32 |  | BRESLAUER |
| ATR | E | CA | D2 | 273 | 15.76 |  | MARKET / CYPRESS & PINE |
| ATR | E | CA | D2 | 273 | 15.97 |  | MARKET / PINE |
| ATR | E | CA | D2 | 273 | 17.35 |  | QUARTZ HILL RD-LT R10-RT |
| ATR | E | CA | D2 | 273 | 18.50 |  | LAKE BLVD |
| ATR | E | CA | D2 | 273 | 18.65 |  | LAKE BLVD |
| ATR | E | CA | D2 | 273 | 19.90 |  | N. JCT ROUTE 5 |
| ATR | E | CA | D2 | 273 | 20.03 |  | N. JCT ROUTE 5 |
| ATR | E | CA | D2 | 284 | 0.04 |  | JCT RTE 70 |
| ATR | E | CA | D2 | 299 | 50.24 |  | WEAVERVILLE W CITY LMT |
| ATR | E | CA | D2 | 299 | 52.15 |  | WEAVERVILLE WASH ST. |
| ATR | E | CA | D2 | 299 | 52.92 |  | WEAVERVILLE MARTIN RD |
| ATR | E | CA | D2 | 299 | 56.87 |  | JCT RTE 3 SOUTH |
| ATR | E | CA | D2 | 299 | 69.08 |  | TRI/SHA COUNTY LINE |
| ATR | E | CA | D2 | 299 | 8.72 |  | FRENCH GULCH RD. |
| ATR | E | CA | D2 | 299 | 21.86 |  | REDDING WEST CITY LIMIT |
| ATR | E | CA | D2 | 299 | 23.81 |  | COURT STREET |
| ATR | E | CA | D2 | 299 | 24.06 |  | REDDING JCT RTE 273 |
| ATR | E | CA | D2 | 299 | R24.47 |  | REDDING BUTTE ST OVERCROSSING |
| ATR | E | CA | D2 | 299 | R25.56 |  | REDDING JCT. RTE. 5 |
| ATR | E | CA | D2 | 299 | R25.65 |  | E/B OFF RAMP TO S/B I-5 |
| ATR | E | CA | D2 | 299 | R25.82 |  | W/B OFF RAMP TO S/B I-5 |
| ATR | E | CA | D2 | 299 | 25.13 |  | N JCT RTE 5 LAKE BLVD IC |
| ATR | E | CA | D2 | 299 | 28.43 |  | OLD OR TRAIL INTRSCTN |
| ATR | E | CA | D2 | 299 | 31.71 |  | BELLA VISTA DSCHTS RD |
| ATR | E | CA | D2 | 299 | 58.62 |  | BIG BEND ROAD |
| ATR | E | CA | D2 | 299 | 71.69 |  | TAMARACK ROAD |
| ATR | E | CA | D2 | 299 | 75.63 |  | BURNEY MAINT STA |
| ATR | E | CA | D2 | 299 | 79.68 |  | 4 CORNERS JCT RTE 89 |
| ATR | E | CA | D2 | 299 | 80.24 |  | 4 CORNERS JCT RTE 89 |
| ATR | E | CA | D2 | 299 | 91.42 |  | FALL RIVER MILLS |
| ATR | E | CA | D2 | 299 | 91.42 |  | FALL RIVER MILLS |
| ATR | E | CA | D2 | 299 | 3.77 |  | CEMETERY ROAD |
| ATR | E | CA | D2 | 299 | 14.42 |  | LOOKOUT-SUSANVILLE RD |
| ATR | E | CA | D2 | 299 | 15.31 |  | LOOKOUT-SUSANVILLE RD |
| ATR | E | CA | D2 | 299 | 0.10 |  | ADIN, JCT. RTE. 139 |
| ATR | E | CA | D2 | 299 | 17.94 |  | JCT. RTE. 139, NORTH |
| CPA/Technology | Existing/Planned, Date | State | Region(R)/District(D) | Route | MP | Dir | Location |
| Infrastructure Operations and Maintenance |
| ATR | E | CA | D2 | 299 | 39.33 |  | JUNIPER STREET |
| ATR | E | CA | D2 | 299 | 40.38 |  | ALTURAS JCT. RTE. 395 S. |
| ATR | E | CA | D2 | 299 | 41.17 |  | ALTURAS JCT. RTE. 395 N. |
| ATR | E | CA | D2 | 395 | R1.5 |  | JCT. RTE. 70 |
| ATR | E | CA | D2 | 395 | 7.75 |  | JCT. RTE. 70 |
| ATR | E | CA | D2 | 395 | 31.35 |  | GARNIER ROAD |
| ATR | E | CA | D2 | 395 | 51.83 |  | BUNTINGVILLE-STANDISH RD CO RD A 3 |
| ATR | E | CA | D2 | 395 | R60.93 |  | JCT. RTE. 36 |
| ATR | E | CA | D2 | 395 | R61.29 |  | JCT. RTE. 36 |
| ATR | E | CA | D2 | 395 | 69.98 |  | BUNTINGVILLE CO RD A 3 |
| ATR | E | CA | D2 | 395 | 70.20 |  | STANDISH COUNTY RD. A3 |
| ATR | E | CA | D2 | 395 | 2.68 |  | LIKELY JESS VALLEY RD. |
| ATR | E | CA | D2 | 395 | 22.07 |  | ALTURAS FIRST STREET |
| ATR | E | CA | D2 | 395 | 22.76 |  | JCT RTE 299 |
| ATR | E | CA | D2 | 395 | 23.04 |  | ALTURAS MAINT STA |
| ATR | E | CA | D2 | 395 | 28.37 |  | JCT. RTE. 299 EAST |
| ATR | E | OR | R2 | 36 | 41.04 |  | 6.6 miles west of |
| ATR | E | OR | R2 | 58 | 35.53 |  | 1.4 miles east of Oakridge |
| ATR | E | OR | R2 | 126 | 43.86 |  | 2.7 miles west of Elmira |
| ATR | E | OR | R2 | 126 | 23.7 |  | 2.7 miles east of Vida |
| ATR | E | OR | R3 | 62 | 15.47 |  | 2.9 miles south of Shady Cove |
| ATR | E | OR | R3 | 62 | 0.66 |  | 0.1 mile NE of Biddle Rd Overpass |
| ATR | E | OR | R3 | 38 | 23.68 |  | 6.8 miles east of Scottsburg |
| ATR | E | OR | R3 | 42 | 70.51 |  | 1.2 miles west of Brockway |
| ATR | E | OR | R3 | 66 | 23.3 |  | 4.2 miles east of Ashland |
| ATR | E | OR | R3 | 99 | 15.82 |  | 1.4 miles south of Talent |
| ATR | E | OR | R3 | 101 | 221.67 |  | 1.09 mile S of Coos-Douglas Co line |
| ATR | E | OR | R3 | 101 | 261.94 |  | 1.3 miles south of Bandon |
| ATR | E | OR | R3 | 101 | 362.01 |  | 1.1 miles N of OR-CA Border |
| ATR | E | OR | R3 | 138 | 28.3 |  | 1 mile E of Susan Creek State Park |
| ATR | E | OR | R3 | 140 | 16.03 |  | 1.27 mile E of Lake Creek Rd (E Jct) |
| ATR | E | OR | R3 | 199 | 41.29 |  | 0.4 mile N of OR-CA Border |
| ATR | E | OR | R3 | 238 | 24.94 |  | 0.5 mile west of Ruch |
| ATR | E | OR | R3 | I-5 | 143.26 |  | 4.9 miles north of Oakland Junction |
| ATR | E | OR | R3 | I-5 | 42.84 |  | 2 miles west of Gold Hill |
| ATR | E | OR | R3 | I-5 | 16 |  | 3.1 miles south of Ashland |
| ATR | E | OR | R3 | I-5 | 22.3 |  | 3.2 miles north of Ashland |
| ATR | E | OR | R3 | I-5 | 28.33 |  | south approach of Medford Viaduct |
| ATR | E | OR | R3 | I-5 | 61.48 |  | 5.7 miles north of Grants Pass |
| CPA/Technology | Existing/Planned, Date | State | Region(R)/District(D) | Route | MP | Dir | Location |
| Infrastructure Operations and Maintenance |
| ATR | E | OR | R4 | 39 | 11.89 |  | 1.7 miles east of Merrill |
| ATR | E | OR | R4 | 20 | 13.51 |  | 5 miles east of Bend |
| ATR | E | OR | R4 | 31 | 49.65 |  | 2.3 miles east of SilverLake |
| ATR | E | OR | R4 | 62 | 92.58 |  | 0.3 mile south of Fort Klamath |
| ATR | E | OR | R4 | 97 | 138.57 |  | 2.6 miles south of Bend |
| ATR | E | OR | R4 | 97 | 204.7 |  | 1.5 miles south of Chemult |
| ATR | E | OR | R4 | 97 | 289.43 |  | 2.3 miles N of OR-CA Border |
| ATR | E | OR | R4 | 140 | 36.58 |  | 4.2 miles east of Beatty |
| ATR | E | OR | R4 | 372 | 19.25 |  | 0.4 mile west of road to Sunriver |
| ATR | E | OR | R4 | 395 | 49.6 |  | 0.3 mile N. of Central Oregon Hwy. |
| ATR | E | OR | R4 | 395 | 120.83 |  | 0.3 mile of Jct w/Lakeview-Burns Hwy |
| ATR | E | OR | R4 | 395 | 157.43 |  | 0.3 mile N of OR-CA Border |
| ATR | E | OR | R5 | 20 | 126.63 |  | 2.1 miles south of Hines |
| ATR | E | OR | R5 | 20 | 258.44 |  | 0.3 mile west of Cairo Junction |
| ATR | E | OR | R5 | 20 | 189.35 |  | at Juntura |
| ATR | E | OR | R5 | 95 | 101.17 |  | 3.0 miles S of Blue Mtn Pass Summit |
| Traffic Management Center* | E | CA | D3 | 20 | 1.47 |  | Marysville |
| Traffic Management Center* | E | CA | D3 | 5 | 29.91 |  | Sacramento |
| Traffic Management Center* | E | OR | R1 | 99 | 4.59 |  | Portland |
| Traffic Management Center* | E | OR | R2 | 22 | 2.82 |  | Salem |
| Traffic Management Center | E | OR | R3 | 5 | 28.33 |  | Medford |
| Traffic Management Center | E | OR | R4 | 20 | 18.51 |  | Bend |
| Satellite Operations Center | E | CA | D1 | 101 | 75.91 |  | Eureka |
| Satellite Operations Center | E | CA | D2 | 5 | 14.46 |  | Redding |
| Surveillance Cameras | E | OR | R3 | 5 (1) | 28.33 |  | Medford |
| Fleet Operations and Maintenance |
| Automated Snow Plow | P | CA | D2 | 44 | 15.5 |  | E of Bogard |
| Commercial Vehicle Operations |
| WIM | E | CA | D1 | 101 | 65.6 |  |  |
| WIM | E | CA | D2 | 97 | 45 |  | Between Mt. Hebron Summit & Macdoel |
| WIM | E | CA | D2 | I-5 | 39.7 |  | Cottonwood Scales |
| WIM | E | CA | D2 | I-5 | 22.14 |  | N of N. Jct 151/I-5 |
| WIM | E | CA | D2 | I-5 | 7.1 |  | Dunsmuir Scales |
| WIM | P '99 | CA | D1 | 101 | R21.9 |  |  |
| WIM | E | OR | R2 | 58 | 17.17 | E/W | Lowell |
| WIM | E | OR | R3 | 5 | 130.03 | S | Wilbur |
| WIM | E | OR | R4 | 97 | 271.41 | N/S | Klamath Falls |
| WIM | E | OR | R4 | 97 | 271.73 | N | Klamath Falls |
| AVI – Preclearance | E | CA | D2 | I-5 | 39.7 |  | Cottonwood Scales |
| AVI – Preclearance | E | CA | D2 | I-5 | 7.1 |  | Dunsmuir Scales |
| AVI – Preclearance | P | OR | R2 | 58 | 17.17 | E/W | Lowell |
| AVI – Preclearance | E | OR | R3 | 5 | 19.1 | N/S | Ashland |
| CPA/Technology | Existing/Planned, Date | State | Region(R)/District(D) | Route | MP | Dir | Location |
| Commercial Vehicle Operations |
| AVI – Preclearance | P | OR | R3 | 5 | 130.03 | S | Wilbur |
| AVI – Preclearance | P | OR | R4 | 97 | 271.41 | S | Klamath Falls |
| AVI – Preclearance | P | OR | R4 | 97 | 271.73 | N | Klamath Falls |
| RCMS | P '98 | CA | D2 | I-5 | 58.1 | N | N of Sima Rd |
| RCMS | P '98 | CA | D2 | I-5 | 29.9 | S | N of Side Hill Viaduct |
| RCMS | P '98 | CA | D2 | I-5 | 31.9 | S | N of Obrian UC |
| RCMS | P '98 | CA | D2 | I-5 | 36.7 | S | N of Upper Salt Creek |
| RCMS | P '98 | CA | D2 | I-5 | 49.1 | S | N of Lamoine OC |
| * Not included in the figures due to locations outside the study area. |  |  |

Appendix e – Traditional Projects/Programs

| Program/Infrastructure | Existing/Planned, Date | State | Region(R)/District(D) | Route | MP | Dir | Location |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Infrastructure |  |  |  |  |  |  |
| CA Western Railroad | E | CA | D1 |  |  |  | Fort Bragg to Willits |
| Rail Facility | E | OR | R2 | 5 | 191 |  | Eugene |
| Rail Facility | E | OR | R4 | 97 | 203.2 |  | Chemult |
| Rail Facility | E | OR | R4 | 97 | 272.31 |  | Klamath Falls |
| Ward Airport | E | CA | D1 | 199 | 14.64 |  | Gasquet |
| Andy McBeth Airport | E | CA | D1 | 101 | 4.64 |  | Klamath |
| Hoopa Airport | E | CA | D1 | 96 | 11.6 |  | On Trinity River |
| FSS Arcata Airport | E | CA | D1 | 101 | 85.83 |  | North of Arcata |
| Eureka Airport | E | CA | D1 | 101 | 75.91 |  | Eureka |
| Kneeland Airport | E | CA | D1 | 101 | 75.91 |  | South of Eureka |
| Dinsmore Airport | E | CA | D1 | 3 | 7.2 |  | West of Hayfork |
| Shelter Cove Airport | E | CA | D1 | 101 | 11.13 |  | West of Garberville |
| Ukiah Municipal Airport | E | CA | D1 | 101 | 24.59 |  | Ukiah, Intermodal |
| Willits Municipal Airport | E | CA | D1 | 101 | 45.17 |  | Willits, Intermodal |
| Garberville Airport | E | CA | D1 | 101 | 11.13 |  | Garberville |
| Rohnerville Airport | E | CA | D1 | 101 | 61.53 |  | South of Fortuna |
| Murray Field | E | CA | D1 | 101 | 75.91 |  | Eureka, Intermodal |
| Arcata/Eureka Airport | E | CA | D1 | 101 | 91.47 |  | McKinleyville, Intermodal |
| McNamara Field | E | CA | D1 | 101 | 25.84 |  | Crescent City, Intermodal |
| Rohrer Airport | E | CA | D2 | 5 | 47.56 |  | Between Montague & Yreka |
| Siskiyou County Airport | E | CA | D2 | 3 | 53.22 |  | North of Montague |
| Tulelake Airport | E | CA | D2 | 139 | 44.5 |  | South of Newell |
| Butte Valley Airport | E | CA | D2 | 97 | 40.41 |  | North of Macdoel |
| Weed Airport | E | CA | D2 | 5 | 19.07 |  | North of Weed |
| Scott Valley Airport | E | CA | D2 | 44 | 30 |  | North of Greenview |
| Happy Camp Airport | E | CA | D2 | 96 | 41.1 |  | Happy Camp |
| Cedarville Airport | E | CA | D2 | 299 | 57.35 |  | Cedarville |
| Eagleville Airport | E | CA | D2 | 299 | 65 |  | Eagleville |
| Alturas Airport | E | CA | D2 | 395 | 22.07 |  | Alturas |
| California Pines Airport | E | CA | D2 | 395 | 22.07 |  | South of Alturas |
| Ravendale Airport | E | CA | D2 | 395 | 108.46 |  | Ravendale |
| Adin Airport | E | CA | D2 | 299 | 0.33 |  | Adin |
| Southard Airport | E | CA | D2 | 299 | 15.1 |  | North of Bieber |
| Spaulding Airport | E | CA | D2 | 139 | 30.8 |  | Eagle Lake |
| Susanville Airport | E | CA | D2 | 36 | 24.46 |  | Susanville |
| Fall River Mills Airport | E | CA | D2 | 299 | 74.98 |  | Between Burney & Bieber |
| Chester-Rogers Airport | E | CA | D2 | 89 | 36.66 |  | Lake Almanor |
| Dunsmuir-Mott Airport | E | CA | D2 | 89 | 24.75 |  | McCloud |
| Shingletown Airport | E | CA | D2 | 44 | 42.82 |  | West of Viola |
| Trinity Center Airport | E | CA | D2 | 3 | 60 |  | Clair Engle Lake |
| Program/Infrastructure | Existing/Planned, Date | State | Region(R)/District(D) | Route | MP | Dir | Location |
| Infrastructure |
| Lonnie Pool Airport | E | CA | D2 | 299 | 51.03 |  | Weaverville |
| Benton Airport | E | CA | D2 | 5 | 14.46 |  | Redding |
| Red Bluff Airport | E | CA | D2 | 5 | 24.87 |  | Red Bluff |
| Corning Airport | E | CA | D2 | 5 | 8.98 |  | Corning |
| Haigh Airport | E | CA | D2 | 5 | 0 |  | Orlano & Hamilton City |
| Hyampom Airport | E | CA | D2 | 3 | 6.7 |  | Hyampom |
| Hayfork Airport | E | CA | D2 | 3 | 7.2 |  | Hayfork |
| Ruth Airport | E | CA | D2 | 36 | 15 |  | South of Ruth |
| Round Valley Airport | E | CA | D2 | 162 | 29 |  | Covelo |
| Glenn County Airport | E | CA | D2 | 5 | 9.87 |  | Willows |
| Colusa County Airport | E | CA | D2 | 5 | 18.72 |  | Colusa |
| Redding Airport | E | CA | D2 | 5 | 14.46 |  | Redding |
| Crescent Lake State Airport | E | OR | R2 | 429 | 2.25 |  | Crescent Lake Jct |
| Cottage Grove State Airport | E | OR | R2 | 5 | 174.74 |  | Cottage Grove |
| McKenzie Brdg State Airport | E | OR | R2 | 126 | 49.78 |  | McKenzie Bridge |
| Oakridge State Airport | E | OR | R2 | 58 | 34.13 |  | Oakridge |
| Santiam Jct State Airport | E | OR | R2 | 20 | 71.45 |  | Santiam Jct |
| Eugene Airport | E | OR | R2 | 5 | 191 |  | Eugene |
| Bandon State Airport | E | OR | R3 | 101 | 260.64 |  | Bandon |
| Lakeside State Airport | E | OR | R3 | 101 | 222.01 |  | Lakeside |
| Brookings State Airport | E | OR | R3 | 101 | 355.38 |  | Brookings |
| Cape Blanco State Airport | E | OR | R3 | 101 | 290 |  | Denmark |
| Toketee State Airport | E | OR | R3 | 138 | 54.6 |  | Clearwater |
| Pinehurst State Airport | E | OR | R3 | 66 | 23.4 |  | Pinehurst |
| Prospect State Airport | E | OR | R3 | 62 | 42.21 |  | Prospect |
| North Bend Airport | E | OR | R3 | 101 | 234.03 |  | North Bend |
| Roseburg Airport | E | OR | R3 | 5 | 124.14 |  | Roseburg |
| Medford Airport | E | OR | R3 | 5 | 28.33 |  | Medford |
| Beaver Marsh State Airport | E | OR | R4 | 138 | 13.7 |  | Beaver Marsh |
| Chiloquin State Airport | E | OR | R4 | 97 | 247.44 |  | Chiloquin |
| Alkali Lake State Airport | E | OR | R4 | 395 | 41.3 |  | Alkali Lake |
| Paisley State Airport | E | OR | R4 | 31 | 98.22 |  | Paisley |
| Klamath Falls Airport | E | OR | R4 | 97 | 272.31 |  | Klamath Falls |
| McDermitt State Airport | E | OR | R5 | 95 | 121.11 |  | McDermitt |
| Owyhee Rsrvr State Airport | E | OR | R5 | 201 | 8.01 |  | Owyhee Dam |
| Rome State Airport | E | OR | R5 | 95 | 53.18 |  | Rome |
| Trinidad Bay | E | CA | D1 | 101 | 100.71 |  | Trinidad |
| Crescent City Harbor | E | CA | D1 | 101 | 25.84 |  | Crescent City |
| Marine Transportation | E | CA | D1 | 101 | 75 |  | Humbolt Bay |
| Marine Facility | E | OR | R3 | 101 | 236.77 |  | Coos Bay (8) |
| Marine Facility | E | OR | R3 | 101 | 234.03 |  | North Bend (6) |
| Reload Facility | E | OR | R3 | 140 | 0 |  | White City (1) |
| Reload Facility | E | OR | R3 | 101 | 236.77 |  | Coos Bay (1) |
| Reload Facility | E | OR | R3 | 5 | 55.78 |  | Grants Pass (1) |
| Reload Facility | E | OR | R4 | 97 | 289.44 |  | Worden (1) |
| Program/Infrastructure | Existing/Planned, Date | State | Region(R)/District(D) | Route | MP | Dir | Location |
| Infrastructure |
| Reload Facility | E | OR | R2 | 5 | 191 |  | Eugene (6) |
| Safety Rest Area | E | CA | D1 | 101 | R105.2 | N | Hum Cnty |
| Safety Rest Area | E | CA | D1 | 101 | R105.9 | S | Hum Cnty |
| Safety Rest Area | E | CA | D1 | 199 | 33.4 | N/S | DN Cnty |
| Safety Rest Area | E | CA | D1 | 101 | 82.5 | N | Men Cnty |
| Safety Rest Area | E | CA | D1 | 101 | 61.8 | N/S | Men Cnty |
| Safety Rest Area | E | CA | D1 | 101 | 58.9 | S | Men Cnty |
| Safety Rest Area | E | CA | D2 | I-5 | R25.6 | N/S | Sis Cnty, Weed |
| Safety Rest Area | E | CA | D2 | I-5 | R58.6 | N/S | Sis Cnty, Collier |
| Safety Rest Area | E | CA | D2 | 97 | 21.8 | N/S | Sis Cnty |
| Safety Rest Area | E | CA | D2 | 44 | 14.5 | E/W | Las Cnty, Bogard |
| Safety Rest Area | E | CA | D2 | 395 | 96.5 | N/S | Las Cnty, Secret Valley |
| Safety Rest Area | E | CA | D2 | I-5 | R10.3 | N/S | Teh Cnty, Corning |
| Safety Rest Area | E | CA | D2 | I-5 | 35 | N | Teh Cnty |
| Safety Rest Area | E | CA | D2 | I-5 | 34.7 | S | Teh Cnty |
| Safety Rest Area | E | CA | D2 | 299 | 60.6 | E/W | Sha Cnty, Hatchett Mountain |
| Safety Rest Area | E | CA | D2 | 44 | 34.7 | E/W | Sha Cnty, Shingletown |
| Safety Rest Area | E | CA | D2 | I-5 | R31.1 | N | Sha Cnty, O'Brien |
| Safety Rest Area | E | CA | D2 | I-5 | R43.1 | S | Sha Cnty, Lakehead |
| Safety Rest Area | E | CA | D2 | 299 | R3.6 | E/W | Tri Cnty |
| Safety Rest Area | E | CA | D2 | 299 | 56.9 | E | Tri Cnty, Douglas City |
| Safety Rest Area | E | CA | D2 | 36 | 12.8 |  | Chester, Plumas County |
| Safety Rest Area | E | CA | D2 | 96 | 105.82 |  | Collier, Jct 96/I-5 |
| Safety Rest Area | E | CA | D2 | 96 | 28.5 |  | Independence Creek |
| Safety Rest Area | E | CA | D2 | 97 | 0.2 | Left |  |
| Safety Rest Area | E | CA | D2 | I-5 | 33.3 |  | Red Bluff |
| Safety Rest Area | E | CA | D2 | I-5 | 34.3 |  | Red Bluff |
| Safety Rest Area | E | CA | D2 | 395 | 49.6 | Right | Honey Lake |
| Safety Rest Area | E | CA | D2 | 89 | 36.63 | Left | Plumas County |
| Safety Rest Area | E | CA | D3 | I-5 | R14.6 | N/S | Gle Cnty |
| Safety Rest Area | E | CA | D3 | I-5 | R24.3 | N/S | Col Cnty |
| Safety Rest Area | E | OR | R2 | I-5 | 177 | N/S | 14 mi S of Eugene |
| Safety Rest Area | E | OR | R2 | I-5 | 242.23 | N/S | 8 mi N of Albany |
| Safety Rest Area | E | OR | R3 | I-5 | 144.14 | N/S | 20 mi N of Roseburg |
| Safety Rest Area | E | OR | R3 | I-5 | 80.78 | N/S | 25 mi N of Grants Pass |
| Safety Rest Area | E | OR | R3 | I-5 | 60.78 | N/S | 5 mi N of Grants Pass |
| Safety Rest Area | E | OR | R3 | I-5 | 10 | N | 10 mi N of CA Line |
| Safety Rest Area | E | OR | R3 | I-5 | 114.14 | N/S | 12 mi S of Roseburg |
| Safety Rest Area | E | OR | R3 | I-5 | 21.33 | S | 7 mi S of Medford |
| Safety Rest Area | E | OR | R3 | 101 | 317.85 | N/S | 10 mi N of Gold Beach |
| Safety Rest Area | E | OR | R4 | 395 | 79.64 | N/S | 63 mi N of Lakeview |
| Safety Rest Area | E | OR | R4 | 20 | 41 | E/W | 41 mi E of Bend |
| Safety Rest Area | E | OR | R4 | 97 | 208.2 | N/S | 5 mi S of Chemult |
| Safety Rest Area | E | OR | R4 | 97 | 280.31 | N/S | 8 mi S of Klamath Falls |
| Safety Rest Area | E | OR | R5 | 20 | 154.1 | E/W | 24 mi E of Burns |
| Program/Infrastructure | Existing/Planned, Date | State | Region(R)/District(D) | Route | MP | Dir | Location |
| Infrastructure |
| Safety Rest Area | E | OR | R5 | 20 | 112.1 | E/W | 18 mi W of Burns |
| Emergency Services |  |  |  |  |  |  |  |
| Del Norte Air Ambulance | E | CA |  | 101 | 25.84 |  | Cresent City |
| Lakeshore Fire Department | E | CA |  | 53 | 2.96 |  | Clear Lake |
| Coffee Creek Volunteer FD | E | CA |  | 3 | 59.64 |  | Trinity Center |
| Palo Cedro Fire Company | E | CA |  | 44 | 7 |  | Palo Cedro |
| Shasta Fire Department | E | CA |  | 299 | 18.5 |  | Shasta |
| Shasta Lake City Fire Prot Dis | E | CA |  | 5 | 22.14 |  | Shasta Lake |
| Weed Fire Department | E | CA |  | 5 | 19.07 |  | Weed |
| City of Dunsmuir Fire Dept. | E | CA |  | 5 | 2.51 |  | Dunsmuir |
| Hamilton Branch FPD | E | CA |  | 89 | 36.66 |  | Lake Almanor |
| Keswick Volunteer Fire Co. | E | CA |  | 299 | 18.5 |  | Shasta |
| Montgomery Creek Fire Dept. | E | CA |  | 299 | 56.9 |  | Montgomery |
| Hat Creek Volunteer Fire Co. | E | CA |  | 89 | 10.5 |  | Hat Creek |
| Ca Dept. of Forestry/Fire Prev | E | CA |  | 5 | 14.46 |  | Redding |
| Loleta Fire Dept. | E | CA |  | 101 | 65.95 |  | Loleta |
| Orleans Fire Dept. | E | CA |  | 96 | 37.83 |  | Orleans |
| Shelter Cove Fire Dept. | E | CA |  | 101 | 10.8 |  | Whitethorn |
| City of Red Bluff Fire Dept. | E | CA |  | 5 | 24.87 |  | Red Bluff |
| Hayfork Volunteer Fire Dept. | E | CA |  | 3 | 7.2 |  | Hayfork |
| Platina-Wildwood Fire Dept | E | CA |  | 36 | 35.3 |  | Wildwood |
| Shasta Lake Volunteer Fire Dep | E | CA |  | 5 | 42.31 |  | Lakehead |
| Tehama County Fire Dept. | E | CA |  | 5 | 24.87 |  | Red Bluff |
| Grenada Fire Department | E | CA |  | 5 | 38.21 |  | Grenada |
| Montague Fire District | E | CA |  | 3 | 53.22 |  | Montague |
| Fort Jones Fire Department | E | CA |  | 3 | 32.2 |  | Fort Jones |
| Bella Vista Volunteer Fire Co. | E | CA |  | 299 | 31.47 |  | Bella Vista |
| Anderson Fire Department | E | CA |  | 5 | 4.29 |  | Anderson |
| West Almanor Comm. Serv. Dist. | E | CA |  | 36 | 8.84 |  | Chester |
| Big Bend Vol. Fire Co. | E | CA |  | 299 | 60.05 |  | Big Bend |
| Old Station Volunteer Fire Dep | E | CA |  | 44 | 62.69 |  | Old Station |
| Oak Run Vol. Fire Company | E | CA |  | 299 | 46.74 |  | Oak Run |
| Mountain Gate Fire Dept. | E | CA |  | 5 | 14.46 |  | Redding |
| Jones Valley Fire Department | E | CA |  | 5 | 14.46 |  | Redding |
| Igo-Ono Volunteer Fire Co. | E | CA |  | 299 | 18.5 |  | Igo |
| Happy Valley Fire Dept. | E | CA |  | 5 | 4.29 |  | Anderson |
| French Gulch Fire District | E | CA |  | 299 | 8.65 |  | French Gulch |
| Cottonwood Fire Protection Dis | E | CA |  | 5 | 1.91 |  | Cottonwood |
| Centerville Fire Dept. | E | CA |  | 5 | 14.46 |  | Redding |
| Cassell Volunteer Fire Co. | E | CA |  | 89 | 18.53 |  | Cassell |
| City Ambulance of Eureka Inc. | E | CA |  | 101 | 75.91 |  | Eureka |
| Fortuna Rescue | E | CA |  | 101 | 75.91 |  | Eureka |
| Garberville Rescue | E | CA |  | 101 | 75.91 |  | Eureka |
| Hoopa Health Assn EMS | E | CA |  | 96 | 10.95 |  | Hoopa |
| Lakeport Fire Department | E | CA |  | 29 | 39.8 |  | Lakeport |
| Program/Infrastructure | Existing/Planned, Date | State | Region(R)/District(D) | Route | MP | Dir | Location |
| Emergency Services |
| Lucerne Fire Department | E | CA |  | 20 | 18.53 |  | Lucerne |
| Redwood Empire Life Support | E | CA |  | 29 | 39.8 |  | Lakeport |
| Arcata Mad River Ambulance Inc | E | CA |  | 101 | 85.83 |  | Arcata |
| St. Elizabeth Hospital | E | CA |  | 5 | 24.87 |  | Red Bluff |
| Northern Siskiyou Ambulance | E | CA |  | 3 | 47.38 |  | Yreka |
| Mount Shasta Ambulance | E | CA |  | 5 | 10.49 |  | Mt. Shasta |
| Happy Camp Ambulance | E | CA |  | 96 | 41.1 |  | Happy Camp |
| Seneca District Hospital | E | CA |  | 36 | 8.84 |  | Chester |
| Peninsula Fire District | E | CA |  | 89 | 36.66 |  | Lake Almanor Penin. |
| Indian Valley Hospital Amb. | E | CA |  | 89 | 20.22 |  | Greenville |
| Modoc Medical Center | E | CA |  | 395 | 22.07 |  | Alturas |
| Westwood Fire Department | E | CA |  | 36 | 3.71 |  | Westwood |
| Westside Ambulance Association | E | CA |  | 5 | 25.53 |  | Orland |
| Glenn Ambulance | E | CA |  | 5 | 9.87 |  | Willows |
| Colusa Ambulance | E | CA |  | 5 | 18.72 |  | Colusa |
| North Valley Ambulance | E | CA |  | 5 | 14.46 |  | Redding |
| Mayers Memorial Hospital | E | CA |  | 299 | 91.56 |  | Fall River Mills |
| Burney Fire District | E | CA |  | 299 | 74.98 |  | Burney |
| Southern Trinity Area Rescue | E | CA |  | 36 | 3.33 |  | Mad River |
| Clearlake Oaks Fire Dept. | E | CA |  | 53 | 2.96 |  | Clearlake |
| Nice Fire and Rescue Dept. | E | CA |  | 20 | 10.5 |  | Nice |
| Lewiston Volunteer Fire Dept. | E | CA |  | 299 | 67.43 |  | Lewiston |
| McCloud Comm Serv Dist. | E | CA |  | 89 | 24.75 |  | McCloud |
| Shingletown Volunteer Fire Dep | E | CA |  | 44 | 27.83 |  | Shingletown |
| Butte Valley Ambulance Service | E | CA |  | 97 | 50.89 |  | Dorris |
| City of Etna Ambulance | E | CA |  | 3 | 21 |  | Etna |
| Surprise Valley Hospital Amb. | E | CA |  | 299 | 57.35 |  | Cedarville |
| Trinity Center Volulnteer FD | E | CA |  | 3 | 59.64 |  | Trinity Center |
| Del Norte Ambulance Inc. | E | CA |  | 101 | 25.84 |  | Crescent City |
| Mountain EMS Inc. | E | CA |  | 36 | 24.46 |  | Susanville |
| Mercy Medical Center | E | CA |  | 5 | 14.46 |  | Redding |
| Upper Lake Fire Protection Dis | E | CA |  | 20 | 8.79 |  | Upper Lake |
| Ukiah Ambulance | E | CA |  | 101 | 24.59 |  | Ukiah |
| Ukiah Fire Department | E | CA |  | 101 | 24.59 |  | Ukiah |
| Laytonville Fire Dept | E | CA |  | 101 | 68.78 |  | Laytonville |
| Northern Pacific Emer Serv | E | CA |  | 101 | 45.17 |  | Willits |
| Mendocino Coast Hosp Amb | E | CA |  | 1 | 60.68 |  | Fort Bragg |
| Covelo Fire Dept Amb | E | CA |  | 162 | 29 |  | Covelo |
| Brooktrails Fire Dept Amb | E | CA |  | 101 | 45.17 |  | Willits |
| CA-OR Life Flight | E | CA | D1 | 101 | 36.31 |  | Smith River |
| Air Life of Oregon | E | OR |  | 97 | 135.97 |  | Bend |
| Ashland Fire & Rescue | E | OR |  | 5 | 19.1 |  | Ashland |
| Basin Volunteer Ambulance Service | E | OR |  | 39 | 23.82 |  | Malin |
| Bay Cities Ambulance | E | OR |  | 101 | 236.77 |  | Coos Bay |
| Bend Fire Department | E | OR |  | 97 | 135.97 |  | Bend |
| Bly Rescue Unit | E | OR |  | 140 | 53.87 |  | Bly |
| Program/Infrastructure | Existing/Planned, Date | State | Region(R)/District(D) | Route | MP | Dir | Location |
| Emergency Services |
| Bonanza Area Ambulance | E | OR |  | 140 | 5.94 |  | Bonanza |
| Burns Ambulance Service | E | OR |  | 20 | 130.1 |  | Burns |
| Chemult Rural Fire Protection District | E | OR |  | 97 | 203.2 |  | Chemult |
| Chiloquin Volunteer Ambulance Service | E | OR |  | 97 | 247.44 |  | Chiloquin |
| Coquille Valley Ambulance | E | OR |  | 42 | 10.85 |  | Coquille |
| Cottage Grove/South Lane Rural Fire Department Ambulance | E | OR |  | 5 | 174.74 |  | Cottage Grove |
| Crescent Rural Fire Protection District | E | OR |  | 97 | 185.57 |  | Crescent |
| Douglas County Fire District #2 | E | OR |  | 5 | 124.14 |  | Roseburg |
| Drain Rural Fire District | E | OR |  | 38 | 50.2 |  | Drain |
| Eugene Department of Public Safety-Fire/EMS Division | E | OR |  | 5 | 191 |  | Eugene |
| Glendale Ambulance | E | OR |  | 5 | 80.3 |  | Glendale |
| Glide Rural Fire Protection District | E | OR |  | 138 | 16.34 |  | Glide |
| Harriman Ambulance Service | E | OR |  | 97 | 272.31 |  | Klamath Falls |
| Jackson County Fire District #3 | E | OR |  | 140 | 0 |  | White City |
| Jackson County Fire District #4 | E | OR |  | 62 | 18.37 |  | Shady Cove |
| Jackson County Fire District #5 | E | OR |  | 99 | 17.22 |  | Talent |
| Jordon Valley Ambulance Service | E | OR |  | 95 | 19.44 |  | Jordan Valley |
| Keno Fire Department Ambulance | E | OR |  | 66 | 49.91 |  | Keno |
| Klamath County Fire District #4 | E | OR |  | 97 | 272.31 |  | Klamath Falls |
| La Pine Rural Fire Protection District | E | OR |  | 97 | 168.04 |  | La Pine |
| Lakeview Disaster Unit | E | OR |  | 395 | 142.64 |  | Lakeview |
| Lower Umpqua EMS | E | OR |  | 101 | 211.11 |  | Reedsport |
| Medic 4 Ambulance | E | OR |  | 5 | 124.14 |  | Roseburg |
| Mercy Flights, Inc | E | OR |  | 5 | 28.33 |  | Medford |
| Merle West Medical Center | E | OR |  | 97 | 272.31 |  | Klamath Falls |
| Mid-County Ambulance Service, Inc | E | OR |  | 140 | 35.92 |  | Sprague River |
| Myrtle Point Ambulance | E | OR |  | 42 | 20.01 |  | Myrtle Point |
| North Lake County Emergency Medical Services | E | OR |  | 31 | 55.3 |  | Christmas Valley |
| Nyssa Ambulance Service | E | OR |  | 201 | 0.4 |  | Nyssa |
| Oakridge Fire Department Ambulance | E | OR |  | 58 | 24.13 |  | Oakridge |
| Pacific Flights, Inc | E | OR |  | 5 | 28.33 |  | Medford |
| Paisley Disaster Unit | E | OR |  | 31 | 98.22 |  | Paisley |
| Port Orford Community Ambulance, Inc | E | OR |  | 101 | 299.83 |  | Port Orford |
| Powers Volunteer Fire Department | E | OR |  | 42 | 17.52 |  | Powers |
| Rogue River Rural Fire Protection District | E | OR |  | 5 | 45.61 |  | Rogue River |
| Silver Lake Rural Fire Protection District | E | OR |  | 31 | 47.35 |  | Silver Lake |
| Sisters-Camp Sherman Rural Fire Protection District | E | OR |  | 126 | 100.03 |  | Sisters |
| Springfield Fire & Life Safety | E | OR |  | 126 | 1.34 |  | Springfield |
| Sunriver Fire Department-Ambulance | E | OR |  | 372 | 19.25 |  | Sunriver |
| Superior Air Charter, Inc | E | OR |  | 5 | 28.33 |  | Medford |
| Sutherlin Fire Department | E | OR |  | 5 | 136.52 |  | Sutherlin |
| Timberland Logging | E | OR |  | 5 | 19.1 |  | Ashland |
| Vale Ambulance Service | E | OR |  | 20 | 245.49 |  | Vale |
| West Medic 1 of Oregon, Inc | E | OR |  | 97 | 272.31 |  | Klamath Falls |
| Western Lane Ambulance District | E | OR |  | 101 | 190.23 |  | Florence |
| Winston-Dillard Fire District #5 | E | OR |  | 42 | 72.74 |  | Winston |
| Coos Bay Police Department | E | OR |  | 101 | 236.77 |  | Coos Bay |
| Coos County Sheriff's Office | E | OR |  | 42 | 10.85 |  | Coquille |
| Myrtle Point Police Department | E | OR |  | 42 | 20.01 |  | Myrtle Point |
| Program/Infrastructure | Existing/Planned, Date | State | Region(R)/District(D) | Route | MP | Dir | Location |
| Emergency Services |
| North Bend Police Department | E | OR |  | 101 | 234.03 |  | North Bend |
| OSP Regional Dispatch - Medford | E | OR |  | 5 | 28.33 |  | Medford |
| Brookings Police Department | E | OR |  | 101 | 355.38 |  | Brookings |
| Curry County Sheriff's Office | E | OR |  | 101 | 327.85 |  | Gold Beach |
| Deschutes County Communications | E | OR |  | 97 | 135.97 |  | Bend |
| OSP Regional Dispatch | E | OR |  | 97 | 135.97 |  | Bend |
| Douglas County Communications | E | OR |  | 5 | 124.14 |  | Roseburg |
| Myrtle Creek Police Department | E | OR |  | 5 | 108.31 |  | Myrtle Creek |
| Coos Forest Protective Association | E | OR |  | 101 | 211.11 |  | Reedsport |
| Douglas Fire Protection Association | E | OR |  | 5 | 124.14 |  | Roseburg |
| WES Ambulance | E | OR |  | 5 | 124.14 |  | Roseburg |
| Reedsport Police Department | E | OR |  | 101 | 211.11 |  | Reedsport |
| Burns Police Department | E | OR |  | 20 | 130.1 |  | Burns |
| Ashland Police Department | E | OR |  | 5 | 19.1 |  | Ashland |
| Medford Emergency Center | E | OR |  | 5 | 28.33 |  | Medford |
| Southern Oregon Regional Communications | E | OR |  | 5 | 28.33 |  | Medford |
| Josephine County 911 Agency | E | OR |  | 5 | 55.78 |  | Grants Pass |
| Klamath County 911 Communications | E | OR |  | 97 | 272.31 |  | Klamath Falls |
| Lakeview Fire Department | E | OR |  | 395 | 142.64 |  | Lakeview |
| Central Lane Communications Center | E | OR |  | 5 | 191 |  | Eugene |
| Florence Police Department | E | OR |  | 101 | 190.23 |  | Florence |
| Cottage Grove Police Department | E | OR |  | 5 | 174.74 |  | Cottage Grove |
| Oakridge Police Department | E | OR |  | 58 | 34.13 |  | Oakridge |
| Lane County Sheriff's Office | E | OR |  | 5 | 191 |  | Eugene |
| Springfield Police Department | E | OR |  | 126 | 1.34 |  | Springfield |
| Ontario Police Department | E | OR |  | 201 | 25.51 |  | Ontario |
| Malheur County Sheriff's Office | E | OR |  | 20 | 245.49 |  | Vale |
| COQUILLE FD | E | OR |  | 42 | 10.85 |  | COQUILLE |
| NORTH BAY RFPD | E | OR |  | 101 | 234.03 |  | NORTH BEND |
| COOS BAY F&R | E | OR |  | 101 | 236.77 |  | COOS BAY |
| MILLINGTON FD | E | OR |  | 101 | 236.77 |  | COOS BAY |
| MYRTLE POINT FD | E | OR |  | 42 | 20.01 |  | MYRTLE POINT |
| DORA-SITKUM RFPD | E | OR |  | 42 | 20.01 |  | MYRTLE POINT |
| NORTH BEND FD | E | OR |  | 101 | 234.03 |  | NORTH BEND |
| SHUTTER CREEK CORR INST | E | OR |  | 101 | 234.03 |  | NORTH BEND |
| CHARLESTON RFPD | E | OR |  | 101 | 236.77 |  | COOS BAY |
| POWERS FD | E | OR |  | 42 | 17.52 |  | POWERS |
| GREENACRES RFPD | E | OR |  | 101 | 236.77 |  | COOS BAY |
| BANDON RFD | E | OR |  | 101 | 260.64 |  | BANDON |
| LAKESIDE RFPD | E | OR |  | 101 | 222.01 |  | LAKESIDE |
| FAIRVIEW RFPD | E | OR |  | 42 | 10.85 |  | COQUILLE |
| SUMNER RFPD | E | OR |  | 101 | 236.77 |  | COOS BAY |
| BRIDGE VOL RFPD | E | OR |  | 42 | 20.01 |  | MYRTLE POINT |
| HAUSER RFPD | E | OR |  | 101 | 234.03 |  | NORTH BEND |
| PISTOL RIVER VOL FD | E | OR |  | 101 | 339.1 |  | PISTOL RIVER |
| LANGLOIS RFPD | E | OR |  | 101 | 281.53 |  | LANGLOIS |
| BROOKINGS FD | E | OR |  | 101 | 355.38 |  | BROOKINGS |
| OPHIR RFPD | E | OR |  | 101 | 316.95 |  | OPHIR |
| SQUAW VALLEY N BANK RFPD | E | OR |  | 101 | 327.85 |  | GOLD BEACH |
| GOLD BEACH FD | E | OR |  | 101 | 327.85 |  | GOLD BEACH |
| UPPER CHETCO RFPD | E | OR |  | 101 | 358.76 |  | HARBOR |
| Program/Infrastructure | Existing/Planned, Date | State | Region(R)/District(D) | Route | MP | Dir | Location |
| Emergency Services |
| WINCHUCK RFPD | E | OR |  | 101 | 358.76 |  | HARBOR |
| SIXES RFPD | E | OR |  | 101 | 295.75 |  | SIXES |
| HARBOR RFPD | E | OR |  | 101 | 358.76 |  | HARBOR |
| CAPE FERRELO RFPD | E | OR |  | 101 | 355.38 |  | BROOKINGS |
| PORT ORFORD FD | E | OR |  | 101 | 399.83 |  | PORT ORFORD |
| CLOVERDALE RFPD | E | OR |  | 126 | 100.03 |  | SISTERS |
| SUNRIVER FD | E | OR |  | 372 | 19.25 |  | SUNRIVER |
| LAPINE RFPD | E | OR |  | 97 | 168.04 |  | LAPINE |
| BEND FD | E | OR |  | 97 | 135.97 |  | BEND |
| SISTERS-CAMP SHERMAN RFPD | E | OR |  | 126 | 100.03 |  | SISTERS |
| AZALEA VOLS | E | OR |  | 5 | 88.12 |  | AZALEA |
| REEDSPORT VOL FD | E | OR |  | 101 | 211.11 |  | REEDSPORT |
| DAYS CREEK RFD | E | OR |  | 227 | 11.67 |  | DAYS CREEK |
| YONCALLA RFPD | E | OR |  | 5 | 149.94 |  | YONCALLA |
| GLIDE RFPD | E | OR |  | 138 | 16.34 |  | GLIDE |
| WINCHESTER BAY RFPD | E | OR |  | 101 | 215.74 |  | WINCHESTER BAY |
| OAKLAND RFPD | E | OR |  | 5 | 138.36 |  | OAKLAND |
| WINSTON-DILLARD RFPD #5 | E | OR |  | 42 | 72.74 |  | WINSTON |
| KELLOGG RFD | E | OR |  | 5 | 138.36 |  | OAKLAND |
| TILLER RFPD | E | OR |  | 227 | 26.3 |  | TILLER |
| FAIR OAKS RFPD | E | OR |  | 5 | 136.52 |  | SUTHERLIN |
| CANYONVILLE FD | E | OR |  | 5 | 98.28 |  | CANYONVILLE |
| SUTHERLIN FD | E | OR |  | 5 | 136.52 |  | SUTHERLIN |
| CAMAS VALLEY VOL RFD | E | OR |  | 42 | 56.02 |  | CAMAS VALLEY |
| GARDINER RFPD | E | OR |  | 101 | 208.3 |  | GARDINER |
| MILO RFPD | E | OR |  | 227 | 11.67 |  | DAYS CREEK |
| TENMILE RFPD | E | OR |  | 42 | 66.35 |  | TENMILE |
| ELKTON RFPD | E | OR |  | 38 | 35.87 |  | ELKTON |
| LOOKINGGLASS RFD | E | OR |  | 5 | 124.14 |  | ROSEBURG |
| MYRTLE CREEK FD | E | OR |  | 5 | 108.31 |  | MYRTLE CREEK |
| GLENDALE FD | E | OR |  | 5 | 80.3 |  | GLENDALE |
| RICE HILL RFD | E | OR |  | 5 | 138.36 |  | OAKLAND |
| TRI CITY FD 4 DOUG | E | OR |  | 5 | 108.31 |  | MYRTLE CREEK |
| SCOTTSBURG RFD | E | OR |  | 38 | 16.88 |  | SCOTTSBURG |
| GLENDALE RFPD | E | OR |  | 5 | 80.3 |  | GLENDALE |
| DRAIN RFPD | E | OR |  | 38 | 50.2 |  | DRAIN |
| DOUGLAS CO RFPD #2 | E | OR |  | 5 | 124.14 |  | ROSEBURG |
| DIAMOND LAKE VOL | E | OR |  | 138 | 78.83 |  | DIAMOND LAKE |
| UMPQUA VOL FD | E | OR |  | 5 | 163.13 |  | UMPQUA |
| ROSEBURG FD | E | OR |  | 5 | 124.14 |  | ROSEBURG |
| RIDDLE VOL FD | E | OR |  | 5 | 103.65 |  | RIDDLE |
| BURNS FD | E | OR |  | 20 | 130.1 |  | BURNS |
| HINES FD | E | OR |  | 20 | 128.73 |  | HINES |
| JACKSON CO RFPD #4 | E | OR |  | 62 | 18.37 |  | SHADY COVE |
| MEDFORD FD | E | OR |  | 5 | 28.33 |  | MEDFORD |
| APPLEGATE RFPD #9 | E | OR |  | 238 | 32.4 |  | JACKSONVILLE |
| JACKSON CO RFPD #3 | E | OR |  | 140 | 0 |  | WHITE CITY |
| ASHLAND F&R | E | OR |  | 5 | 19.1 |  | ASHLAND |
| TALENT FD | E | OR |  | 99 | 17.22 |  | TALENT |
| JACKSON CO RFPD #5 | E | OR |  | 99 | 17.22 |  | TALENT |
| JACKSON CO RFPD #6 | E | OR |  | 5 | 45.61 |  | ROGUE RIVER |
| Program/Infrastructure | Existing/Planned, Date | State | Region(R)/District(D) | Route | MP | Dir | Location |
| Emergency Services |
| JACKSONVILLE FD | E | OR |  | 238 | 32.4 |  | JACKSONVILLE |
| V A DOMICILIARY | E | OR |  | 140 | 0 |  | WHITE CITY |
| LAKE CREEK RFPD #8 | E | OR |  | 140 | 7.97 |  | EAGLE POINT |
| EAGLE POINT FD | E | OR |  | 140 | 7.97 |  | EAGLE POINT |
| BUTTE FALLS VOL FD | E | OR |  | 140 | 28.6 |  | BUTTE FALLS |
| PHOENIX VOL FD | E | OR |  | 99 | 11.03 |  | PHOENIX |
| ROGUE RIVER RFPD | E | OR |  | 5 | 45.61 |  | ROGUE RIVER |
| ROGUE VALLEY INTL AIRPORT FD | E | OR |  | 5 | 28.33 |  | MEDFORD |
| PROSPECT RFPD | E | OR |  | 62 | 42.21 |  | PROSPECT |
| COLESTIN RFPD | E | OR |  | 5 | 19.1 |  | ASHLAND |
| WOLF CREEK RFPD | E | OR |  | 5 | 76.5 |  | WOLF CREEK |
| GRANTS PASS DEPT PUB SFTY | E | OR |  | 5 | 55.78 |  | GRANTS PASS |
| WILLIAMS RFPD | E | OR |  | 238 | 13.77 |  | WILLIAMS |
| RURAL METRO FD | E | OR |  | 5 | 55.78 |  | GRANTS PASS |
| GRANTS PASS RURAL | E | OR |  | 5 | 55.78 |  | GRANTS PASS |
| ILLINOIS VALLEY RFPD | E | OR |  | 199 | 27.71 |  | CAVE JUNCTION |
| CRESCENT RFPD | E | OR |  | 97 | 185.57 |  | CRESCENT |
| CHEMULT RFPD | E | OR |  | 97 | 203.2 |  | CHEMULT |
| BLY RFPD | E | OR |  | 140 | 53.87 |  | BLY |
| BONANZA RFPD | E | OR |  | 140 | 5.94 |  | BONANZA |
| CRATER LAKE NAT'L PARK FD | E | OR |  | 62 | 83.63 |  | CRATER LAKE |
| KLAMATH CO FD #5 | E | OR |  | 140 | 5.94 |  | BONANZA |
| KLAMATH CO FD #4 | E | OR |  | 97 | 272.31 |  | KLAMATH FALLS |
| CHILOQUIN-AGENCY LK RFPD | E | OR |  | 97 | 247.44 |  | CHILOQUIN |
| KLAMATH CO FD #1 | E | OR |  | 97 | 272.31 |  | KLAMATH FALLS |
| MERRILL FD | E | OR |  | 39 | 13.59 |  | MERRILL |
| KINGSLEY FIELD FD | E | OR |  | 97 | 272.31 |  | KLAMATH FALLS |
| KENO RFPD | E | OR |  | 66 | 49.91 |  | KENO |
| HARRIMAN RFPD | E | OR |  | 97 | 272.31 |  | KLAMATH FALLS |
| MALIN RFPD | E | OR |  | 39 | 23.82 |  | MALIN |
| SPRAGUE RIVER VOL | E | OR |  | 140 | 35.92 |  | SPRAGUE RIVER |
| CRESCENT-ODELL LAKES RFPD | E | OR |  | 58 | 2.25 |  | CRESCENT LAKE |
| MERRILL RFPD | E | OR |  | 39 | 13.59 |  | MERRILL |
| KLAMATH CO FD #3 | E | OR |  | 140 | 35.92 |  | SPRAGUE RIVER |
| LAKEVIEW FD | E | OR |  | 395 | 142.64 |  | LAKEVIEW |
| NEW PINE CREEK RFPD | E | OR |  | 395 | 157.43 |  | NEW PINE CREEK |
| SILVER LAKE RFPD | E | OR |  | 31 | 47.35 |  | SILVER LAKE |
| PAISLEY VOL FD | E | OR |  | 31 | 98.22 |  | PAISLEY |
| THOMAS CREEK W SIDE RFPD | E | OR |  | 395 | 142.64 |  | LAKEVIEW |
| CHRISTMAS VALLEY RFPD | E | OR |  | 31 | 55.3 |  | CHRISTMAS VALLEY |
| SUMMER LAKE FD | E | OR |  | 31 | 69.09 |  | SUMMER LAKE |
| SPRINGFIELD FIRE LIFE SFTY | E | OR |  | 126 | 1.34 |  | SPRINGFIELD |
| LANE CO FD #1 | E | OR |  | 126 | 46.2 |  | VENETA |
| FLORENCE FD | E | OR |  | 101 | 190.23 |  | FLORENCE |
| CRESWELL RFPD | E | OR |  | 5 | 182.83 |  | CRESWELL |
| PLEASANT HILL RFPD | E | OR |  | 58 | 5.73 |  | PLEASANT HILL |
| SIUSLAW RFPD #1 | E | OR |  | 101 | 190.23 |  | FLORENCE |
| OAKRIDGE FD | E | OR |  | 58 | 34.13 |  | OAKRIDGE |
| SANTA CLARA RFPD | E | OR |  | 5 | 191 |  | EUGENE |
| COTTAGE GROVE/S LANE RURAL FD | E | OR |  | 5 | 174.74 |  | COTTAGE GROVE |
| EUGENE FIRE & EMS | E | OR |  | 5 | 191 |  | EUGENE |
| Program/Infrastructure | Existing/Planned, Date | State | Region(R)/District(D) | Route | MP | Dir | Location |
| Emergency Services |
| GOSHEN RFPD | E | OR |  | 5 | 191 |  | EUGENE |
| MAPLETON FD | E | OR |  | 126 | 14.09 |  | MAPLETON |
| WESTFIR FD | E | OR |  | 58 | 31.29 |  | WESTFIR |
| SWISSHOME-DEADWOOD RFPD | E | OR |  | 36 | 7.94 |  | SWISSHOME |
| UPPER MCKENZIE RFPD | E | OR |  | 126 | 49.78 |  | MCKENZIE BRIDGE |
| LORANE RFPD | E | OR |  |  | 37.7 |  | LORANE |
| LANE RURAL F&R | E | OR |  | 5 | 191 |  | EUGENE |
| BLUE RIVER FD | E | OR |  | 126 | 40.7 |  | BLUE RIVER |
| DEXTER RFPD | E | OR |  | 58 | 9.56 |  | DEXTER |
| LOWELL FPD | E | OR |  | 58 | 13.2 |  | LOWELL |
| MCKENZIE RFPD | E | OR |  | 126 | 1.34 |  | SPRINGFIELD |
| JORDAN VALLEY FD | E | OR |  | 95 | 19.44 |  | JORDAN VALLEY |
| ADRIAN RFPD | E | OR |  | 201 | 11.72 |  | ADRIAN |
| VALE FD | E | OR |  | 20 | 245.49 |  | VALE |
| CHP Humboldt Dispatch Center | E | CA |  |  |  |  | Arcata |
| CHP Redding Dispatch Center | E | CA |  |  |  |  | Redding |
| CHP Susanville Dispatch Center | E | CA |  |  |  |  | Susanville |
| CHP Yreka Dispatch Center | E | CA |  |  |  |  | Yreka |
| CHP Ukiah Dispatch Center | E | CA |  |  |  |  | Ukiah |
| Crescent City CHP | E | CA |  |  |  |  | Crescent City |
| Humboldt CHP | E | CA |  |  |  |  | Arcata |
| Garberville CHP | E | CA |  |  |  |  | Redway |
| Red Bluff CHP | E | CA |  |  |  |  | Red Bluff |
| Redding CHP | E | CA |  |  |  |  | Redding |
| Susanville CHP | E | CA |  |  |  |  | Susanville |
| Yreka CHP | E | CA |  |  |  |  | Yreka |
| MT. Shasta CHP | E | CA |  |  |  |  | Mt. Shasta |
| Ukiah CHP | E | CA |  |  |  |  | Ukiah |
| Williams CHP | E | CA |  |  |  |  | Williams |
| Willows CHP | E | CA |  |  |  |  | Willows |
| Quincy CHP | E | CA |  |  |  |  | Quincy |
| Alturas CHP | E | CA |  |  |  |  | Alturas |
| Trinity River CHP | E | CA |  |  |  |  | Weaverville |
| Gold Run CHP | E | CA |  |  |  |  | Gold Run |
| Grass Valley CHP | E | CA |  |  |  |  | Grass Valley |
| Oroville CHP | E | CA |  |  |  |  | Oroville |
| Humboldt County Sheriff | E | CA |  |  |  |  | Eureka |
| Lake County Sheriff | E | CA |  |  |  |  | Lakeport |
| Mendocino County Sheriff | E | CA |  |  |  |  |  |
| Shasta County Sheriff | E | CA |  |  |  |  | Redding |
| Siskiyou County Sheriff | E | CA |  |  |  |  |  |
| Chico Police | E | CA |  |  |  |  | Chico |
| Cloverdale Police | E | CA |  |  |  |  | Cloverdale |
| Eureka Police | E | CA |  |  |  |  | Eureka |
| Fort Bragg Police | E | CA |  |  |  |  | Fort Bragg |
| Fortuna Police | E | CA |  |  |  |  | Fortuna |
| Grass Valley Police | E | CA |  |  |  |  | Grass Valley |
| Mt. Shasta Police | E | CA |  |  |  |  | Mt. Shasta |
| Red Bluff Police | E | CA |  |  |  |  | Red Bluff |
| Redding Police | E | CA |  |  |  |  | Redding |
| Ukiah Police | E | CA |  |  |  |  | Ukiah |
| Program/Infrastructure | Existing/Planned, Date | State | Region(R)/District(D) | Route | MP | Dir | Location |
| Yuba City Police | E | CA |  |  |  |  | Yuba City |
| Intermodal Programs and Projects |  |  |  |  |  |  |
| Park and Ride Lot | E | CA | D1 | 101 | 59.9 | N/S | Fortuna |
| Park and Ride Lot | E | CA | D1 | 101 | 79.3 |  | Eureka |
| Park and Ride Lot | E | CA | D1 | 29 | 39.8 |  | Lakeport |
| Park and Ride Lot | E | CA | D1 | 101 | 100.7 | E/W | Trinidad |
| Park and Ride Lot | E | CA | D1 | 101 | 74.8 |  | Elk River |
| Park and Ride Lot | E | CA | D2 | 44 | 7 |  | Deschutes Rd |
| Park and Ride Lot | E | CA | D2 | 44 | 24.8 |  | Black Butte Store |
| Park and Ride Lot | E | CA | D2 | 44 | 31.7 |  | Shingletown, Shasta County |
| Park and Ride Lot | E | CA | D2 | 96 | 52.5 |  | Pacific Crest Trailhead |
| Park and Ride Lot | E | CA | D2 | I-5 | 41.5 |  | Bowman Rd Interchange |
| Park and Ride Lot | E | CA | D2 | 395 | 52.6 |  | Janesville |
| Park and Ride Lot | E | CA | D2 | 89 | 8.7 |  | Blairsden |
| Park and Ride Lot | E | CA | D2 | 89 | 21.6 |  | Burney |
| Park and Ride Lot | E | CA | D2 | 89 | R34.3 |  | Mt. Shasta |
| Park and Ride Lot | E | CA | D2 | 299 | 79.68 |  | Jct. 89/299 |
| Park and Ride Lot | E | CA | D2 | 273 | 11.8 |  | Clear Creek Rd |
| Park and Ride Lot | E | CA | D2 | I-5 | 41.5 |  | Cottonwood |
| Park and Ride | P 1998 | OR | R2 | 69 | 12.7 |  | Lane County |
| Intercity Transit Services | E | CA | D2 |  |  |  | Redding Amtrak |
| Intercity Transit Services | E | CA | D2 |  |  |  | Dunsmuir Amtrak |
| Intercity Transit Services | E | CA | D2 |  |  |  | Mount Lassen Motor Transit |
| Fixed Route | E | CA | D2 |  |  |  | Weaverville, Lewiston, Hayfork |
| Demand Responsive | E | CA | D2 |  |  |  | Alturas to Susanville/ Klamath Falls |
| Transit Service | E | CA | D1 |  |  |  | Eureka to Redding |
| Transit Service | E | CA | D1 |  |  |  | Arcata |
| Fixed Route | E | CA | D1 |  |  |  | Eureka |
| Bus Service | E | CA | D2 | 35 |  |  | Red Bluff to Susanville |
| Greyhound | E | CA | D2 | 97 |  |  |  |
| Greyhound | E | CA | D2 | I-5 |  |  | Tehama County |
| Greyhound | E | CA | D2 | I-5 |  |  | Shasta County |
| Program/Infrastructure | Existing/Planned, Date | State | Region(R)/District(D) | Route | MP | Dir | Location |
| Intermodal Programs and Projects |
| Greyhound | E | CA | D2 | I-5 |  |  | Siskiyou County |
| Trailways Lines, Inc | E | CA | D2 | I-5 |  |  | Tehama County |
| Trailways Lines, Inc | E | CA | D2 | I-5 |  |  | Shasta County |
| Trailways Lines, Inc | E | CA | D2 | I-5 |  |  | Siskiyou County |
| Greyhound | E | CA | D2 | 395 |  |  |  |
| Greyhound | E | CA | D2 | 139 |  | N/S |  |
| Del Norte Public Bus | E | CA | D1 | 101 | R4.6-26.2 | N/S | Klamath to Crescent City |
| Arcata Transit Service | E | CA | D1 |  |  |  | Humboldt County |
| Mad River Transit Service | E | CA | D1 |  |  |  | Humboldt County |
| Humboldt Transit Authority | E | CA | D1 |  |  |  | Humboldt County |
| Lake Transit Authority | E | CA | D1 |  |  |  | Lake County |
| Lassen Transit Authority | E | CA | D2 |  |  |  | Lassen County |
| Mendocino Stage | E | CA | D1 |  |  |  | Mendocino County |
| Mendocino Transit Authority | E | CA | D1 |  |  |  | Mendocino County |
| Redwood Coast Transit | E | CA | D1 |  |  |  | Redwood Coast |
| Sage Stage | E | CA | D2 |  |  |  | Modoc County |
| Lassen Rural Bus | E | CA | D2 |  |  |  | Susanville, W & S Lassen Co. |
| Mt Lassen Cab, Shuttle | E | CA | D2 |  |  |  | Susanville |
| Plumas County Transit | E | CA | D2 |  |  |  | Quincy, Portola, Chester, Meadow Valley, Bucks Lake Rd, Pineleaf |
| Redding Area Bus Authority | E | CA | D2 |  |  |  | Redding, Anderson, Shasta Lake |
| Consolidated Transportation Service Agency | E | CA | D2 |  |  |  | Outside RABA Service Area |
| STAGE (Siskiyou Transit & General Express) | E | CA | D2 |  |  |  | I-5 Corridor, Happy Camp, Yreka, Weed, Mt. Shasta, McCloud, Etna |
| Tehama Rural Area Express | E | CA | D2 |  |  |  | Corning, Red Bluff |
| VanTrans | E | CA | D2 |  |  |  | Red Bluff |
| Trinity County Service | E | CA | D2 |  |  |  | Hayfork to Weaverville |
| Eureka Transit Service | E | CA | D1 | 101 |  |  | Eureka |
| Redwood Empire Lines | E | CA | D1 | 299 |  | E/W | District 1 on 299 |
| Bus Station | E | CA | D1 |  |  |  | Ukiah Bus Stations |
| Bus Station | E | CA | D1 |  |  |  | Willits Bus Stations |
| Bus Station | E | CA | D1 |  |  |  | Laytonville Bus Stations |
| Bus Station | E | CA | D1 | 101 |  |  | Greyhound |
| Greyhound | E | CA | D2 |  |  |  | Redding |
| Bus Station | E | CA | D2 | 299E |  |  | Greyhound |
| Dial-a-Ride, Fixed Route | E | CA | D1 |  |  |  | Mendicino County |
| Redwood Dial-a-Ride | E | CA | D1 | 101 |  |  | Crescent City |
| Intercity Transit Services | E | OR | R4 |  |  |  | Klamath Falls Amtrak |
| Intercity Transit Services | E | OR | R4 |  |  |  | Chemult Amtrak |
| Intercity Transit Services | E | OR | R2 |  |  |  | Eugene Amtrak |
| Intercity | E | OR | R3 |  |  |  | North Bend-Bend & In Between |
| Program/Infrastructure | Existing/Planned, Date | State | Region(R)/District(D) | Route | MP | Dir | Location |
| Intermodal Programs and Projects |
| Intercity | E | OR | R3 |  |  |  | Jackson County |
| Fixed Route | E | OR | R5 |  |  |  | Ontario |
| Fixed Route | E | OR | R4 |  |  |  | Crook County to Redmond |
| Bus Station | E | OR | R4 | 97 | 135.97 |  | Bend |
| Bus Station | E | OR | R3 | 5 | 124.14 |  | Roseburg |
| Bus Station | E | OR | R3 | 5 | 28.33 |  | Medford |
| Bus Station | E | OR | R3 | 5 | 55.78 |  | Grants Pass |
| Bus Station | E | OR | R4 | 97 | 272.31 |  | Klamath Falls |
| Bus Station | E | OR | R4 | 395 | 142.64 |  | Lakeview |
| Bus Station | E | OR | R2 | 5 | 191 |  | Eugene |
| Dial-a-Ride | E | OR | R3 |  |  |  | Bandon |
| Dial-a-Ride | E | OR | R3 |  |  |  | Coos County |
| Dial-a-Ride | E | OR | R3 |  |  |  | Brookings |
| Dial-a-Ride | E | OR | R3 |  |  |  | Sutherlin |
| Dial-a-Ride | E | OR | R3 |  |  |  | Ashland |
| Dial-a-Ride | E | OR | R3 |  |  |  | Sutherlin, Oakland, 3-Mile Rd |
| Dial-a-Ride | E | OR | R3 |  |  |  | Winston |
| Dial-a-Ride | E | OR | R3 |  |  |  | Curry County |
| Dial-a-Ride, Taxi Ticket Stub | E | OR | R3 |  |  |  | Douglas County |
| Dial-a-Ride | E | OR | R3 |  |  |  | Roseburg & Winston |
| Dial-a-Ride | E | OR | R3 |  |  |  | Gold Beach |
| Dial-a-Ride | E | OR | R3 |  |  |  | Josephine County |
| Dial-a-Ride, Fixed Route | E | OR | R3 |  |  |  | Josephine County |
| Dial-a-Ride | E | OR | R3 |  |  |  | Myrtle Point |
| Dial-a-Ride | E | OR | R3 |  |  |  | Jackson County |
| Dial-a-Ride, Fixed Route | E | OR | R3 |  |  |  | Medford, Ashland, Etc. |
| Dial-a-Ride | E | OR | R3 |  |  |  | Grants Pass |
| Dial-a-Ride, Fixed Route | E | OR | R3 |  |  |  | Myrtle Creek, Green Dist., Etc. |
| Dial-a-Ride | E | OR | R3 |  |  |  | Roseburg |
| Dial-a-Ride | E | OR | R3 |  |  |  | NE Jackson County |
| Dial-a-Ride | E | OR | R3 |  |  |  | Coos Bay, North Bend |
| Dial-a-Ride | E | OR | R4 |  |  |  | Central Oregon |
| Dial-a-Ride, Fixed Route | E | OR | R4 |  |  |  | Klamath Falls |
| Dial-a-Ride | E | OR | R4 |  |  |  | Deschutes & Jefferson County |
| Dial-a-Ride | E | OR | R4 |  |  |  | Bend |
| Dial-a-Ride | E | OR | R4 |  |  |  | Deschutes County |
| Dial-a-Ride | E | OR | R4 |  |  |  | Deschutes, N. Klamath County |
| Dial-a-Ride | E | OR | R4 |  |  |  | Burns, Hines |
| Dial-a-Ride | E | OR | R4 |  |  |  | Klamath County |
| Dial-a-Ride | E | OR | R4 |  |  |  | Out of District |
| Dial-a-Ride, Taxi Ticket Stub | E | OR | R4 |  |  |  | Klamath County |
| Dial-a-Ride | E | OR | R4 |  |  |  | Lake County |
| Dial-a-Ride, Fixed Route | E | OR | R4 |  |  |  | Crook, Jefferson, Deschutes Co |
| Program/Infrastructure | Existing/Planned, Date | State | Region(R)/District(D) | Route | MP | Dir | Location |
| Intermodal Programs and Projects |
| Dial-a-Ride | E | OR | R4 |  |  |  | Klamath Falls |
| Dial-a-Ride | E | OR | R4 |  |  |  | Prineville |
| Dial-a-Ride | E | OR | R5 |  |  |  | Grant County |
| Dial-a-Ride | E | OR | R5 |  |  |  | Ontario |
| Dial-a-Ride | E | OR | R5 |  |  |  | Malheur County |
| Dial-a-Ride, Fixed Route | E | OR | R5 |  |  |  |  |
| Dial-a-Ride, Fixed Route | E | OR | R5 |  |  |  | Nyssa |
| Dial-a-Ride | E | OR | R5 |  |  |  | Vale |
| Commercial Vehicle Operations |  |  |  |  |  |  |
| Weigh Station** | E | CA | D2 | I-5 | 7 | S | N of Mott Rd |
| Weigh Station** | E | CA | D2 | I-5 | 41 | N | S of Bowman Rd |
| Weigh Station** | E | CA | D2 | I-5 | 41 | S | S of Bowman Rd |
| Weigh Station | E | CA | D1 | 101 | 49 | S | N of Willits |
| Weigh Station | E | CA | D1 | 20 | 34 | W | E of US 101 |
| Weigh Station | E | CA | D1 | 101 | 97 | S | N of McKinnlyville |
| Weigh Station | E | CA | D1 | 299 | 7 | W | E of Blue Lake |
| Weigh Station | E | CA | D2 | 299 | 13 | E | Whiskeytown Reservoir |
| Portable Scale Pit | E | CA | D2 | 97 | 3 | Left/Right |  |
| Truck Scales | E | CA | D2 | 299 | 12.7 | Right | Shasta County |
| Truck Scales | E | CA | D2 | 299 | 54.3 | Left | Shasta County |
| Truck Scales | E | CA | D2 | 299 | 76.2 | Left | Shasta County |
| Truck Escape Ramp | E | CA | D1 | 101 | R127.55 |  |  |
| Truck Escape Ramp | E | CA | D1 | 101 | R129.53 |  |  |
| Truck Escape Ramp | E | CA | D2 | I-5 | 58.2 |  | Siskiyou County |
| Truck Escape Ramp | E | CA | D2 | 299 | 58.4 |  | Shasta County |
| Truck Escape Ramp | E | CA | D2 | 299 | 47.1 |  | Trinity County |
| Inspection Stop | E | CA | D1 | 20 | 0.79 | E |  |
| Inspection Stop | E | CA | D1 | 20 | 34.90 | W | JEO Jct 53 |
| Inspection Stop | E | CA | D1 | 20 | 28.30 | E | 5 Mi W Willits |
| Inspection Stop | E | CA | D1 | 101 | 24.80 | S | JSO Crescent City |
| Inspection Stop | E | CA | D1 | 101 | 23.30 | S | JNO Garberville |
| Inspection Stop | E | CA | D1 | 101 | 55.90 | N | JSO Fortuna |
| Inspection Stop | E | CA | D1 | 101 | 97.26 | S | Crannell |
| Inspection Stop | E | CA | D1 | 101 | 121.60 | S | JNO Orick |
| Inspection Stop | E | CA | D1 | 101 | 19.00 | N | JNO Garberville |
| Inspection Stop | E | CA | D1 | 101 | 41.17 | S | 4 Mi S Willits |
| Inspection Stop | E | CA | D1 | 101 | 48.65 | S | Willits |
| Inspection Stop | E | CA | D1 | 101 | 65.00 | N | JSO Laytonville |
| Inspection Stop | E | CA | D1 | 101 | 86.60 | S | JSO Leggett |
| Inspection Stop | E | CA | D1 | 199 | 7.90 | S |  |
| Inspection Stop | E | CA | D1 | 199 | 33.20 | S |  |
| Inspection Stop | E | CA | D1 | 299 | 7.38 | W | JEO Blue Lake |
| Brake Check Area | E | CA | D1 | 36 | 28.17 | W |  |
| Brake Check Area | E | CA | D1 | 36 | 32.08 | W |  |
| Brake Check Area | E | CA | D1 | 101 | 130.29 | N |  |
| Brake Check Area | E | CA | D1 | 101 | 130.58 | S |  |
| Brake Check Area | E | CA | D1 | 101 | 16.46 | S |  |
| Program/Infrastructure | Existing/Planned, Date | State | Region(R)/District(D) | Route | MP | Dir | Location |
| Commercial Vehicle Operations |
| Brake Check Area | E | CA | D1 | 101 | 20.74 | N |  |
| Brake Check Area | E | CA | D1 | 199 | 33.45 | S |  |
| Weigh Station | E | OR | R3 | 101 | 276.11 | N | 2 mi S of Bandon |
| Weigh Station | E | OR | R3 | 42 | 21.87 | W | E City Lmts of Myrtle Point |
| Weigh Station | E | OR | R3 | 42 | 5.50 | N | 5 mi N of Coquille |
| Weigh Station | E | OR | R3 | 101 | 227.89 | S | 6 mi N of Coos Bay Brdg |
| Weigh Station | E | OR | R3 | 101 | 357.73 | N | S City Lmts of Brookings |
| Weigh Station | E | OR | R3 | 101 | 353.18 | S | 3 mi N of Brookings |
| Weigh Station | E | OR | R3 | 101 | 309.42 | N | 8 mi S of Port Orford |
| Weigh Station | E | OR | R2 | 20 | 0.15 | E | Jct US20/OR126 |
| Weigh Station | E | OR | R4 | 20 | 11.60 | W | 11 mi E of Bend |
| Weigh Station | E | OR | R3 | I-5 | 130.03 | S | 5 mi N of Roseburg |
| Weigh Station | E | OR | R3 | I-5 | 111.07 | N | 3 mi N of Myrtle Creek |
| Weigh Station | E | OR | R3 | 42 | 71.20 | E | 2 mi W of Winston |
| Weigh Station | E | OR | R3 | 138 | 15.14 | E/W | 1 mi W of Glide |
| Weigh Station | E | OR | R3 | 38 | 1.94 | W | ECL of Reedsport |
| Weigh Station | E | OR | R3 | 138 | 22.62 | E | 2 mi W of Sutherlin |
| Weigh Station | E | OR | R5 | 20 | 134.17 | E/W | 1 mi E of Burns |
| Weigh Station | E | OR | R3 | 62 | 7.66 | S | 4 mi N of Medford |
| Weigh Station | E | OR | R3 | I-5 | 18.24 | S | 3.5 mi N of OR 66 Exit |
| Weigh Station | E | OR | R3 | I-5 | 18.08 | N | 3.5 mi N of OR 66 Exit |
| Weigh Station | E | OR | R3 | 140 | 13.85 | W | 20 mi E of Medford |
| Weigh Station | E | OR | R3 | 140 | 2.70 | E | 2 mi E of White City |
| Weigh Station | E | OR | R3 | 199 | 0.49 | N | WCL of Grants Pass |
| Weigh Station | E | OR | R3 | 199 | 41.05 | N | 1/2 mi N of OR/CA Line |
| Weigh Station | E | OR | R3 | 199 | 8.70 | N | 8 mi S of Grants Pass |
| Weigh Station | E | OR | R3 | 199 | 20.60 | S | 7 mi N of Cave Jct |
| Weigh Station | E | OR | R4 | 97 | 271.41 | S | 1 mi N of Klamath Falls |
| Weigh Station | E | OR | R4 | 97 | 271.73 | N | 1 mi N of Klamath Falls |
| Weigh Station | E | OR | R4 | 66 | 44.81 | E | 5 mi W of Keno |
| Weigh Station | E | OR | R4 | 140 | 57.18 | E | 9 mi W of Klamath Falls |
| Weigh Station | E | OR | R4 | 140 | 14.59 | W | 13 mi E of Klamath Falls |
| Weigh Station | E | OR | R4 | 140 | 95.36 | E/W | W City Lmts of Lakeview |
| Weigh Station | E | OR | R4 | 31 | 47.30 | N | Silver Lake |
| Weigh Station | E | OR | R2 | 126 | 12.95 | W | 10 mi E of Springfield |
| Weigh Station | E | OR | R2 | 58 | 17.17 | W | 4 mi E of Lowell Jct |
| Weigh Station | E | OR | R2 | 126 | 43.00 | E | 1.2 mi E of Noti |
| Weigh Station | E | OR | R2 | 126 | 1.50 | E | 1.5 mi E of Florence |
| Weigh Station | E | OR | R2 |  | 6.31 | N | 1 mi S of Jasper |
| Weigh Station | E | OR | R2 | 126 | 45.20 | W | 3.2 mi E of Noti |
| Weigh Station | E | OR | R5 | 95 | 66.00 | N/S | Jct OR78/US95 |